## Slide 1
IEEE 802.21
DCN: 21-15-0102-00-SAUC
Title: Presentation of Open SLMCP use case
Date Submitted: Sep 16, 2015
IEEE 802.21 session #70 in Bangkok, Thailand
Authors or Source(s):
Sangkwon Peter Jeong, Chanyoung Kwon, Sunju Kwon (BlueCloud Co., Ltd.)
Changhwa Lyou (SeerooInformation)
Abstract: Open Social Learning Mobile Content Platform use cases for media independent handover

## Slide 2
  IEEE 802.21 presentation release statements
This document has been prepared to assist the IEEE 802.21 Working Group. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.21.
The contributor is familiar with IEEE patent policy, as stated in Section 6 of the IEEE-SA Standards Board bylaws <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and in Understanding Patent Issues During IEEE Standards Development http://standards.ieee.org/board/pat/faq.pdf>

## Slide 3: Open SLMCP Service Model
2015 BlueCloud Co., Ltd
Social Learning
Platform
Service
Supply
Consume
Quest
Professor
Friends
(students)
Social Networking Service Provider
Share
Share
&
Spread
Professor
Friends
(students)
Friends
(students)
Professor
Mobility Area

## Slide 4: Open SLMCP Architecture
2015 BlueCloud Co., Ltd

## Slide 5
2015 BlueCloud Co., Ltd
MIH Services in mobile nodes facilitate seamless handovers between heterogeneous networks. MIH Services are used by MIH users such as a mobility management protocol (e.g., Mobile IP). Other mobility management protocols (in addition to Mobile IP) and even other MIH users are not precluded from making use of MIH Services.
Open SLMCP don’t use new MIH parameters and functions. It is just use to exist MIS components.
I will presentation that Open SLMCP change the using network between 802.11 and 802.16.

## Slide 6: Example handover flow chart between IEEE 802.11 and IEEE 802.16
2015 BlueCloud Co., Ltd
Figure C.3 shows a handover flow chart between the IEEE 802.11 and the IEEE 802.16 network. This is an example of dual radio handover procedure wherein both the radios involved in handover can transmit and receive at the same time. The handover procedure operates as follows:
1) The Mobile Node is connected to the IEEE 802.11 network and receives the IEEE 802.11 link measurement report through the MIH_Link_Parameters_Report.indication and acquires the neighboring network information by the MIH_Get_Information.confirm.
2) When the Link_Going_Down event happens on the current IEEE 802.11 network, the Mobile Node performs the MIH_Link_Actions.request to scan the link status of the candidate networks.
The mobile node discovers the IEEE 802.16 network and can acquire the candidate IEEE 802.16 network's DL_MAP, UL_MAP, DCD and UCD parameters.
3) The Mobile Node identifies the resource availability status of the candidate network by sending the MIH_MN_HO_Candidate_Query message to the Serving PoS. When the Serving PoS receives the MIH_MN_HO_Candidate_Query request message from the Mobile Node, it retrieves resource information from target network by sending MIH_N2N_HO_Query_Resources message to the PoSs on the candidate networks.
4) Based on resource availability and other selection criteria the IEEE 802.16 network is selected as the target of the handover and the Mobile Node sends MIH_MN_HO_Commit request message to the Serving PoS to notify the decided target network information. The Serving PoS reserves the resource at the target network through MIH_N2N_HO_Commit messages.
5) The Mobile Node commits a link switch to the IEEE 802.16 interface and the new layer 2 connection for the target IEEE 802.16 network is established. The Mobile IP procedures are carried out between the Mobile Node and the IEEE 802.16 network. As a result of that, the active sessions are now shifted over to the IEEE 802.16 network.
6) The Mobile Node sends the MIH_MN_HO_Complete request message to the Serving PoS on the IEEE 802.16 network and that Serving PoS exchanges the MIH_N2N_HO_Complete messages with the previous PoS on the IEEE 802.11 network to release the resource that was reserved for the Mobile Node on that network.

## Slide 7: Call Flow for Handover
2015 BlueCloud Co., Ltd
Figure C.3—Example handover flow chart between IEEE 802.11 and IEEE 802.16

## Slide 8: High Level Process in case of Open SLMCP
2015 BlueCloud Co., Ltd
Open Social Learning
Mobile Content Platform
⑤ Request for sign in by token
Open SLMCP Client
SNS(Social Networking Service)
⑥ Request for confirmation by user token
③ Request
authentication token
① Request for joining membership
⑧ Respond confirmation message
② Check for user authentication of the SNS
④ Respond
authentication token
PoS
⑦ Respond confirmation message
Out of Scope

## Slide 9: Low Level Process in case of Registration
2015 BlueCloud Co., Ltd
Open SLMCP
Mobile Node (MIHF)
PoS (MIHF)
802.16
802.11
Occur to Handover
※ Network by Mobile IP
① Request for joining membership
② Check for user authentication of the SNS
③ Request for sign in by token
④ Respond confirmation message
①’ Request for joining membership
③’ Request for sign in by token
②’ Check for user authentication of the SNS
④’ Respond confirmation message
Open SLMCP is Server. It check the connected within the MN and Open SLMCP Server. For the stable Service and prevent bad users as hackers. Therefore, Open SLMCP should using by Mobile IP. And, MN is using for the QoS. It doesn’t make to disconnected status that is using the MIS.

## Slide 10: Low Level Process in case of Content Download
2015 BlueCloud Co., Ltd
Open SLMCP
Mobile Node (MIHF)
PoS (MIHF)
802.16
802.11
Occur to Handover
※ Network by Mobile IP
① Request for Content list
② Respond Content list
③ Request for Content download
④ Content download
①’ Request for Content list
③’ Request for Content download
②’ Respond Content list
④’ Content download
Mobile node must connect for stable QoS. If disconnect between MN and Open SLMCP then user cannot download the content to his wish timing.

## Slide 11: Low Level Process in case of Content Upload
2015 BlueCloud Co., Ltd
Open SLMCP
Mobile Node (MIHF)
PoS
802.16
802.11
Occur to Handover
※ Network by Mobile IP
① Call for Content Upload
② Respond Ready status
③ Content Upload
④ Respond Confirm message to upload complete
①’ Call for Content Upload
③’ Content Upload
②’ Respond Ready status
④’ Respond Confirm message to upload complete
Mobile node must connect for stable QoS. If disconnect between MN and Open SLMCP then user cannot upload the content to his wish timing.