## Slide 1
IEEE 802.21
DCN: 21-16-00xx-00-0000
Title: Some key points for Remedy 1 proposed in 21-15-00-0036-00-SAUC for Comments #106, #107, #108 and #109
Date Submitted: Feb.19, 2016
Presented at teleconference Feb. 22, 2016
Authors or Source(s):
Lily Chen (NIST)
Abstract: This presentation explains some key points in adoption remedy 1 proposed in 21-15-00-0036-00-SAUC for Comments #106, #107, #108 and #109

## Slide 2: Some key points for Remedy 1 proposed in 21-15-00-0036-00-SAUC for Comments #106, #107, #108 and #109
Lily Chen (NIST)
Feb. 19, 2016

## Slide 3: Optimize MIH SA establishment for Single Radio Handover
Whenever, it is possible, MN shall establish SA with TPoS with the methods provided in 21m (developed as in task group 21a)
  The reason for the fact that the mechanisms provided in 21m cannot be used is not well understood
    The issue is that MN cannot directly talk to TPoS, however
    In 21m, EAP is executed between an MN and PoS
    EAP is executed on the top of MIH (see Figure 40 of 21m)
The optimized MIH SA establishment for Single Radio Handover is provided as an option
  SPoS generates a key K and distributes it to TPoS and MN
  MN and TPoS shall use the key K as it is generated through EAP as in 21m to derive other keys (see Figure 46 of 21m)
  The cipher suites are defined in 21m for TPoS and MN to negotiate (tables 24 and 25 in 21m)
The optimized method must be restricted to reduce the security damage through domino effect
  If home domains of SPoS and TPoS have a kind of agreement, then there shall be a way to provide key K from a higher level entity
  In fact, it may be more reasonable to allow SPoS to derive a key K from whatever established before with MN, in stead of generating K from no where.
In any case, it is a default to fall back to EAP between MN and TPoS

## Slide 4: The interfaces
SPOS
MN
TPOS
K
K
K
MAIK
MIEK
MIIK
This interface shall be protected at the MIH level by the method specified in 21m
This interface can be protected by the mechanisms out of the scope of 21
This key K shall be used in the same way as the key obtained from EAP, like MSK (Fig.46)

## Slide 5: What are not needed in the current 21.1
The interface between MN and SPoS is protected through a cipher-suite defined in 21m
  PRFsPoS is not needed
  KsPoS is not needed
The interface between SPoS and TPoS is protected through an out-of-the-scope mechanism (see the first paragraph of 5.14)
  PRFstpos is not needed
  Kstpos is not needed
The PoS is a convenient and natural place to locate security services, and roaming partners have in place agreements that can be used to beneficially establish the needed security agreements between different PoS modules in partner networks. It is expected that the PoS functions in partner networks must often communicate by data paths that traverse the external Internet; in such cases, a secure communication channel must exist or must be established between the partners. It is out of scope for this document to specify exactly how the secure communication channel should be established, but this can be done by configuration when the partners enter into their roaming agreement. It can also be done on demand by using IKEv2 (RFC 7296) [B36]. The following overview describes in more detail the circumstances enabling dynamic establishment of security association between the SPoS and the TPoS.

## Slide 6: What are still needed in the current 21.1
Nonce-T and Nonce-N are still needed for key derivation from K to the keys needed to establish protections between MN and TPoS
The ciphersuite coded as c is still needed
  (see 9.2.2. in 21m)
SPOS
MN
TPOS
K
K
K
MAIK
MIEK
MIIK
Nonce -N
Nonce -T