## Slide 1: IEEE 802.21 Framework and Its Applicability to IMT-2020
Date: 05-20-2016
Authors:

## Slide 2: Outline
Applicable IMT-2020 Usage Scenarios and Requirements
IEEE 802.21 Technologies
  IEEE 802.21 key services and capabilities
  IEEE 802.21.1 use cases
IEEE 802.21 relevance to IMT-2020
References

## Slide 3: IMT-2020 Usage Scenarios and Requirements
Enhanced Mobile Broadband:
  New application areas and requirements for improved performance and an increasingly seamless user experience.
  Wide-area coverage: seamless coverage/connectivity, medium to high mobility, improved data rate (lower than Hotspot)
Ultra-reliable and low latency communications:
  Stringent requirements for throughput, latency and availability
    Seamless user experience and connectivity for example, in mission critical application and self driving car in heterogeneous environment
Massive machine type communications:
  Very large number of devices, low volume of non-delay-sensitive data, low cost devices with a very long battery life
    Seamless user experience and connectivity between home, office, and vehicle

## Slide 4: Key Capabilities of IMT-2020
Peak data rate
User experienced data rate
Low Latency
Mobility: Maximum speed at which a defined QoS and seamless transfer between radio nodes which may belong to different layers and/or radio access technologies (multi-layer/multi-RAT) can be achieved (in km/h).
Connection density
Energy efficiency
Spectrum efficiency
Area traffic capacity

## Slide 5: Future Network Technologies: Multi-RAT
The trend to integrate multiple radio access technologies seamlessly will accelerate.
it is beneficial to consider a general access system with new architecture and solution to optimize the multi-RAT coordination and interworking from RAN perspective to meet the following requirements:
– flexible RRM of multi-RAT for the improvement of resource utilization, load balancing and seamless mobility management.
– service aware traffic steering to different RATs for consistent user experience and user satisfactory, e.g. by simultaneously connecting to multi-RAT
– improve signalling robustness and efficiency with sending the signalling via the most appropriate way.
– scalability of adding new RAT from core network perspective
– reduce the maintenance and optimization complexity

## Slide 6: Future Terminal Technologies
Future mobile terminals will be equipped with multiple network interfaces, each for different RAT.
– deliver different multimedia traffic over the different RAT at the same time, after selecting the best RAT that is optimized to network conditions and accessibility, QoS/QoE requirements, mobile terminal conditions such as battery life-time, user preferences, and service cost over the RAT.
– combine simultaneously several different traffic flows transmitted over channels of the same or different RAT, achieving higher throughput and optimally using the heterogeneous radio resource.
– have key functional modules such as RAT connection control, quality policy-based routing, security and policy management, intra/inter-RAT handover control for seamless service continuity, and QoS/QoE control management.

## Slide 7
IEEE 802.21: Key Services and Capabilities
Link Layer
Triggers
State Change
Predictive
Network Initiated
Network
Information
Available Networks
Neighbor Maps
Network Services
Service
specific
Commands
Client Initiated
Network Initiated
IEEE 802.21 uses these services to support
several use cases in IEEE 802.21.1
Signaling
Protocol and
Security
Unicast and
multicast

## Slide 8: IEEE 802.21.1: Defined Use cases
Media Independent Services for Handover between 802 and non-802 networks
Media Independent Services for Software Defined Radio Access Networks
Media independent service for home energy management system (HEMS)
Media independent service for radio resource management (RRM)
Media independent service for D2D communication

## Slide 9: IEEE 802.21 for better Network Selection and Seamless User Experience (IMT Vision)
An extensible media access independent services (MIS) framework (function and protocol) that can help better discover and select the best network based on application requirements
  Information about all networks can be obtained even when a single radio is active
  Common information representation across different Networks
Media Independent signaling protocol to report observed network events and obtain network assistance
  Can be transported over L2 and L3 and secured
  L3 transport is standardized in IETF with IANA ports assigned
Media independent QoS parameter mapping to provide better user experience
  Techniques to derive generic QoS parameters from access link parameters

## Slide 10: Relevance of 802.21 to selected Technology Trends and Enablers (ITU-R M.2320)
Technology trend | IEEE 802.21 Relevance
Physical layer enhancements and interference handling for small cell | Facilitating fast service discovery and the handoff to small cells
Flexible spectrum usage | Support of D2D use case allows better integration of different technologies to provide heterogeneous carrier aggregation
Dual Connectivity and Multi-Stream Aggregation | Provides mobility robustness – vital control-plane information such as handover commands can be transmitted from an overlay macro node even if the user data is provided by a low-power node. Can be extended to provide cross-technology downlink-uplink separation
Technologies to support M2M | D2D use case enables direct M2M communication
RLAN Interworking | IEEE 802.21 facilitates traffic offloading to other non-802 networks (e.g., Cellular) embracing capacity expansion into licensed spectrum bands

## Slide 11: References
Recommendation ITU-R M.2083-0 (2015), “IMT Vision – Framework and overall objectives of the future development of IMT for 2020 and beyond”
Report ITU-R M.2320-0 (2014), “Future technology trends of terrestrial IMT systems”
IEEE P802.21/D02 (2016), “Draft Standard for Local and metropolitan area networks - Part 21: Media Independent Services Framework”
IEEE P802.21.1/D02 (2016), “Draft Standard for Local and metropolitan area networks - Part 21.1: Media Independent Services”

## Slide 12: Appendix (additional material)

## Slide 13: IMT-2020 Usage Scenarios Triangle [1]

## Slide 14: Enhancement of key capabilities from IMT-Advanced to IMT-2020 [1]

## Slide 15: IMT-2020 importance of key capabilities in different usage scenarios [1]