## Slide 1
IEEE 802.21 MEDIA INDEPENDENT SERVICES
DCN: 21-19-0002-01-0000
Title: Introduction to VR SG
Date Submitted: January 7, 2019
Presented at IEEE 802.21 session #89 in St. Louis, USA
Authors or Source(s): Jeong, Sangkwon Peter (JoyFun)
Seo, Dong-Il Dillon (VoleR Creative)
Presenter: Seo, Dong-Il Dillon (VoleR Creative)
Abstract: This document describes the current VR system layout and the industrial problems around so that the participants for the SG is aware of the problems they need to solve.

## Slide 2
  IEEE 802.21 presentation release statements
This document has been prepared to assist the IEEE 802.21 Working Group. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.21.
The contributor is familiar with IEEE patent policy, as outlined in Section 6.3 of the IEEE-SA Standards Board Operations Manual <http://standards.ieee.org/guides/opman/sect6.html#6.3> and in Understanding Patent Issues During IEEE Standards Development http://standards.ieee.org/board/pat/guide.html>
  IEEE 802.21 presentation release statements
This document has been prepared to assist the IEEE 802.21 Working Group. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.21.
The contributor is familiar with IEEE patent policy, as stated in Section 6 of the IEEE-SA Standards Board bylaws <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and in Understanding Patent Issues During IEEE Standards Development http://standards.ieee.org/board/pat/faq.pdf>

## Slide 3: Use Cases

## Slide 4: Case 1
HMD
LAN
Case 1
Local Content Server
HMD is connected to a local content server such a PC or a gaming console by a wired or wireless network.
VR content is being rendered or decoded in the local content server and HMD is receiving the VR content through either a wired or a wireless network.
* LAN: wired or wireless
※ Slide Source: Seo, Dong-Il Dillon, VoleR Creative(21-18-0039-02-0000, IEEE 802.21 86th meeting)

## Slide 5: Case 2
* WAN: wired + wireless
※ Slide Source: Seo, Dong-Il Dillon, VoleR Creative(21-18-0039-02-0000, IEEE 802.21 86th meeting)
HMD
WAN
Remote Content Server
Case 2
HMD is connected to a remote content server such as cloud rendering by wired and wireless network.
VR content is being rendered or decoded in the remote content server and streamed to the HMD.
The remote content server is connected via WAN as the remote content server is located outside of the local area.

## Slide 6: Case 3
HMD
LAN
Local Content Server
Remote Content Server
WAN
HMD
LAN
Local Content Server
Case 3
This is an extended version of case 1 – more than one VR system are connected to the remote content server.
HMD is connected to a local server like case 1 and the local content server is rendering or decoding VR content and send it back to the HMD.
The remote content server in this case is computing the content sent by the local content servers and redistributing the calculated data back to the local content servers rather than rendering the content in local content server.
* LAN: wired or wireless
* WAN: wired + wireless
※ Slide Source: Seo, Dong-Il Dillon, VoleR Creative(21-18-0039-02-0000, IEEE 802.21 86th meeting)

## Slide 7: Case 4
HMD
Remote Content Server
WAN
HMD
Case 4
This is an extended version of case 2 - more than one HMD are connected to the remote server.
HMD is connected to a remote server like case 2 and the remote server is rendering or decoding VR content and send it back to the HMD.
* WAN: wired + wireless
※ Slide Source: Seo, Dong-Il Dillon, VoleR Creative(21-18-0039-02-0000, IEEE 802.21 86th meeting)

## Slide 8: Diagrams
HMD
LAN
HMD
WAN
Case 1
Case 2
HMD
LAN
Local Content Server
Remote Content Server
WAN
HMD
LAN
Local Content Server
Case 3
HMD
Remote Content Server
WAN
HMD
Case 4
Local Content Server
Remote Content Server
* LAN: wired or wireless
* WAN: wired + wireless
※ Slide Source: Seo, Dong-Il Dillon, VoleR Creative(21-18-0039-02-0000, IEEE 802.21 86th meeting)

## Slide 9: Industry Problems
VR sickness is a subset of Motion Sickness
The IG focuses on the VR HMD based VR Sickness only
Caused by the mismatch between the visually received information and the vestibular system
Various Standard Organizations such as IEEE 3079, IEEE 2048, Khronos Group, ISO/IEC JTC1/SC24, SC29 WG11(MPEG), W3C, ITU-T SG12 are developing technical standards for VR
Car Sickness
Air Sickness
Sea Sickness
Space Sickness
Motion Sickness
Cybersickness
Simulator Sickness
VR Sickness
※ VR: Virtual Reality
※ HMD: Head Mounted Display
Notes: HMD VR sickness에 초점을 맞추어야 한다.
이 슬라이드에서 VR Sickness가 one of Cybersickness라는 것은 크게 중요한 내용이 아니다.

## Slide 10: Technical Requirements for VR QoE
Requirement | details
pixels/degree | - 40 pix/deg - no HMD is capable of displaying 40pix/deg today
video resolution | - 3 times 4K(3840x1920) vertical resolution = 11520x6480
framerate | - 90 fps - a 90fps framerate offers a latency low enough to prevent nausea
3D Audio | - support of scene-based and/or environmental audio - 360 surround sound, object-based audio, Ambisonics
motion-to-photon latency & motion-to-audio latency | - how much time there is between the user interacts and an image / audio - maximum 20ms
foreground & parallax | - objects in the foreground shall be far enough to prevent nausea - if objects are too close it is likely they can become an important cause of nausea - interactive parallax with background shall be present for such objects - pic1 shows how it is possible to look behind the figure in the foreground
Technicolor, Oct. 2016 (m39532, MPEG 116th Meeting)
※ Sourced by Prof. Lyou, Eunseok (Gacheon Univ.)

## Slide 11: Technical Challenges
Tracker
CPU
GPU
Display
Photons
Optics
Head motion
User’s retina
Under 20 milliseconds of latency for comfortability
Network requirements are directly related to MTP latency
For VR HMD based VR Content Service, the network should provide the following features:
  Link Layer Issues: Jitter, Latency
  High Layer Issue: QoS, QoE & Mobility
※ MTP: Motion to Photon

## Slide 12: Industry Relevance
Securing QoE is important for the following industry participants (Content Delivers)
  Mobile Network Infrastructure Providers
    Immediate killer app for 5G is immersive media (VR & AR) for Telecom Companies
    Need to have good VR QoE to grab more users to their 5G network
  HMD Manufacturers
    Stand-alone also known as all-in-one devices are designed to create a better QoE as it eliminates the cord that was attached to the device
    Added processor and batteries in a limited physical case space increase the weight and the heat; hence network solution is required to for cloud VR service
  Content Creators
    Creating more compelling visual experience comparable to the modern PCs and gaming consoles for VR using the stand-alone device is very challenging
    Current wired system limits the QoE of VR content; hence, needs a cloud VR
  Platform Holders
    Want to aggregate compelling VR content to grow their VR content ecosystem

## Slide 13: IEEE 802.21 Interest Group Activities
For the last few months, IG produced the followings:
  Produced a White Paper on problem statement, use case and analysis of existing technologies
  Conducted a test to verify the application data throughput requirements (MPEG test procedure) in a constraint environment
    Test Server : Linux Ubuntu
    Test Sequences : Gaslamp, KiteFlite
    Quantization Parameters : 22, 27, 32, 37
    FPS : 30, 60, 90
    Resolution : HD, UHD 4K, 8K
    Encoder/Decoder: HEVC/H.265 Reference SW

## Slide 14: Test Condition
Test Server : Linux Ubuntu
Test Sequences : Gaslamp, KiteFlite
Quantization Parameters : 22, 27, 32, 37
FPS : 30, 60, 90
Resolution : HD, UHD 4K, 8K
Encoder/Decoder: HEVC/H.265 Reference SW

## Slide 15: 360 Video Bitrates/Quality Test Process
Down sampling
Encoding,
Decoding
Up sampling
Encoding,
Decoding
Encoding,
Decoding
Up sampling
WS-PSNR Calculation
※ Slide Source: Ryu, eun-seok, Professor of Gachon University

## Slide 16: Test Sequences (Defined by ISO/IEC MPEG Standard-I)
- Gaslamp
- KiteFlite
※ Slide Source: Ryu, eun-seok, Professor of Gachon University

## Slide 17: Test Results – Plots (1/2)
Chart: Gaslamp FPS60
| 26.804524799999999 | 14.345062400000002 | 7.7823744000000001 | 4.1792448000000002
8K | 46.7672 | 44.8655 | 42.4664 | 39.8424
4K | 31.6334 | 31.4593 | 31.1189 | 30.5803
HD | 30.3217 | 30.1526 | 29.8232 | 29.2542
Chart: Gaslamp FPS90
| 40.206787200000001 | 21.517593600000001 | 11.673561600000001 | 6.2688671999999999
8k | 46.7672 | 44.8655 | 42.4664 | 39.8424
4K | 31.6334 | 31.4593 | 31.1189 | 30.5803
HD | 30.3217 | 30.1526 | 29.8232 | 29.2542
Chart: Gaslamp FPS 30
| 13.4022624 | 7.1725312000000008 | 3.8911872000000001 | 2.0896224000000001
8K | 46.7672 | 44.8655 | 42.4664 | 39.8424
4K | 31.6334 | 31.4593 | 31.1189 | 30.5803
HD | 30.3217 | 30.1526 | 29.8232 | 29.2542
※ Slide Source: Ryu, eun-seok, Professor of Gachon University

## Slide 18: Test Results – Plots (2/2)
Chart: KiteFlite FPS30
| 51.716576000000003 | 25.398278399999999 | 13.5746944 | 7.2491520000000005
8K | 44.1636 | 41.502 | 38.7266 | 35.8644
4K | 24.5208 | 24.51 | 24.4673 | 24.3705
HD | 24.2303 | 24.2066 | 24.1315 | 23.9529
Chart: KiteFlite FPS60
| 103.43315200000001 | 50.796556799999998 | 27.149388800000001 | 14.498304000000001
8K | 44.1636 | 41.502 | 38.7266 | 35.8644
4K | 24.5208 | 24.51 | 24.4673 | 24.3705
HD | 24.2303 | 24.2066 | 24.1315 | 23.9529
Chart: KiteFlite FPS90
| 155.14972800000001 | 76.1948352 | 40.724083200000003 | 21.747456
8K | 44.1636 | 41.502 | 38.7266 | 35.8644
4K | 24.5208 | 24.51 | 24.4673 | 24.3705
HD | 24.2303 | 24.2066 | 24.1315 | 23.9529
※ Slide Source: Ryu, eun-seok, Professor of Gachon University

## Slide 19: Test Results - Tables
KiteFlite | Bitrate | 51716.5760 | 25398.2784 | 13574.6944 | 7249.1520 | 27318.0352 | 13142.3904 | 6670.8544 | 3308.9440 | 8684.0704 | 4290.9440 | 2208.0320 | 1092.8608
 | Y-WSPSNR | 44.1636 | 41.5020 | 38.7266 | 35.8644 | 24.5208 | 24.5100 | 24.4673 | 24.3705 | 24.2303 | 24.2066 | 24.1315 | 23.9529
 | QP | 22 | 27 | 32 | 37 | 22 | 27 | 32 | 37 | 22 | 27 | 32 | 37
 | FPS 30 | 8K |  |  |  | 4K |  |  |  | FHD |  |  | 
KiteFlite | Bitrate | 103433.15 | 50796.557 | 27149.389 | 14498.304 | 54636.07 | 26284.781 | 13341.709 | 6617.888 | 17368.141 | 8581.888 | 4416.064 | 2185.7216
 | Y-WSPSNR | 44.1636 | 41.502 | 38.7266 | 35.8644 | 24.5208 | 24.51 | 24.4673 | 24.3705 | 24.2303 | 24.2066 | 24.1315 | 23.9529
 | QP | 22 | 27 | 32 | 37 | 22 | 27 | 32 | 37 | 22 | 27 | 32 | 37
 | FPS 60 | 8K |  |  |  | 4K |  |  |  | FHD |  |  | 
KiteFlite | Bitrate | 155149.73 | 76194.835 | 40724.083 | 21747.456 | 81954.106 | 39427.171 | 20012.563 | 9926.832 | 26052.211 | 12872.832 | 6624.096 | 3278.5824
 | Y-WSPSNR | 44.1636 | 41.502 | 38.7266 | 35.8644 | 24.5208 | 24.51 | 24.4673 | 24.3705 | 24.2303 | 24.2066 | 24.1315 | 23.9529
 | QP | 22 | 27 | 32 | 37 | 22 | 27 | 32 | 37 | 22 | 27 | 32 | 37
 | FPS 90 | 8K |  |  |  | 4K |  |  |  | FHD |  |  | 
Gaslamp | Bitrate | 13402.262 | 7172.5312 | 3891.1872 | 2089.6224 | 7011.4784 | 3712.96 | 1945.3984 | 1007.4144 | 2463.2704 | 1338.2368 | 721.0432 | 379.36
 | Y-WSPSNR | 46.7672 | 44.8655 | 42.4664 | 39.8424 | 31.6334 | 31.4593 | 31.1189 | 30.5803 | 30.3217 | 30.1526 | 29.8232 | 29.2542
 | QP | 22 | 27 | 32 | 37 | 22 | 27 | 32 | 37 | 22 | 27 | 32 | 37
 | FPS 30 | 8K |  |  |  | 4K |  |  |  | FHD |  |  | 
Gaslamp | Bitrate | 26804.525 | 14345.062 | 7782.3744 | 4179.2448 | 14022.957 | 7425.92 | 3890.7968 | 2014.8288 | 4926.5408 | 2676.4736 | 1442.0864 | 758.72
 | Y-WSPSNR | 46.7672 | 44.8655 | 42.4664 | 39.8424 | 31.6334 | 31.4593 | 31.1189 | 30.5803 | 30.3217 | 30.1526 | 29.8232 | 29.2542
 | QP | 22 | 27 | 32 | 37 | 22 | 27 | 32 | 37 | 22 | 27 | 32 | 37
 | FPS 60 | 8K |  |  |  | 4K |  |  |  | FHD |  |  | 
Gaslamp | Bitrate | 40206.787 | 21517.594 | 11673.562 | 6268.8672 | 21034.435 | 11138.88 | 5836.1952 | 3022.2432 | 7389.8112 | 4014.7104 | 2163.1296 | 1138.08
 | Y-WSPSNR | 46.7672 | 44.8655 | 42.4664 | 39.8424 | 31.6334 | 31.4593 | 31.1189 | 30.5803 | 30.3217 | 30.1526 | 29.8232 | 29.2542
 | QP | 22 | 27 | 32 | 37 | 22 | 27 | 32 | 37 | 22 | 27 | 32 | 37
 | FPS 90 | 8K |  |  |  | 4K |  |  |  | FHD |  |  | 
Bitrate (Kbps)
Y-WSPSNR (dB)
※ Slide Source: Ryu, eun-seok, Professor of Gachon University

## Slide 20: Conclusion of Test
Bitrates vary from 40Mbps to 160Mbps according to video content features.
  8K resolution and 90 fps contents: 40Mbps ~ 160Mbps
The WS-PSNR quality of HD and 4K UHD were much lesser than 8K UHD.
Target video resolution for VR service
  Fraunhofer HHI and TNO: 12K resolution
  KETI: 16K resolution
Considering VR sickness, 160Mbps (hopefully 200Mbps) application layer bandwidth is required for 8K 90fps.
  Physical layer bandwidth requirement: around 350Mbps
  If 16K/90fps is considered, 700Mbps (Phy. Layer) bandwidth will be required (estimation).

## Slide 21: SG Scopes
For Wired WGs related use cases
  Use case 1, 3
For Wireless WGs related use cases
  Use case 2, 3, 4
For Handover WG related use cases
  Use case 2, 3 and so on.

## Slide 22: Next Steps for SG
PAR’s scope fix to until March meeting