## Slide 1: Investigation on meeting the TVWS Spectrum Mask
IEEE P802.22 Wireless RANs Date: 2011-11-9
Authors:
Notice: This document has been prepared to assist IEEE 802.22. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.22.
Patent Policy and Procedures: The contributor is familiar with the IEEE 802 Patent Policy and Procedures
<http://standards.ieee.org/guides/bylaws/sb-bylaws.pdf>, including the statement "IEEE standards may include the known use of patent(s), including patent applications, provided the IEEE receives assurance from the patent holder or applicant with respect to patents essential for compliance with both mandatory and optional portions of the standard." Early disclosure to the Working Group of patent information that might be relevant to the standard is essential to reduce the possibility for delays in the development process and increase the likelihood that the draft publication will be approved for publication. Please notify the Chair Apurva Mody <apurva.mody@baesystems.com> as early as possible, in written or electronic form, if patented technology (or technology under patent application) might be incorporated into a draft standard being developed within the IEEE 802.22 Working Group. If you have questions, contact the IEEE Patent Committee Administrator at patcom@ieee.org.

## Slide 2: Abstract
This presentation serves three purposes:
  To show the challenge we face in TVWS spectrum
  To demonstrate via simulations that the 802.22b PHY proposal by document 22-12-0090-02-000b meets the TVWS spectrum mask defined by FCC with easy filter implementation
  To show the existing 802.22 PHY design meet the TVWS spectrum with more difficult filter implementation.

## Slide 3: Summary of PHY parameters
 | 802.22 | 802.22b
FFT size | 2048 | 1024
Sampling frequency (MHz) | 6.85 | 5.60
Number of null carriers | 368 | 192 (DS), 184 (US)
Number of effective carriers | 1680 | 832 (DS), 840 (US)
Occupied bandwidth (MHz) | 5.625 | 4.55 (DS), 4.59 (US)
Lower channel edge guardband (KHz) | 188.3 | 726.4 (DS), 704.4 (US)
Upper channel edge guardband (KHz) | 186.7 | 723.6 (DS), 701.6 (US)

## Slide 4: Challenges in meeting TVWS Spectrum Mask
802.22b
802.22

## Slide 5: 802.22b proposal meets the TVWS spectrum mask with filtering
Filter design:
(FIR Equirripple)
Fpass = 2.4 MHz;
Fstop = 3 MHz;
Dpass = 0.0575;
Dstop = 0.08;
Filter order = 17

## Slide 6: 802.22b proposal meets the TVWS spectrum mask with Low-order FIR filter
Order=18
Order=17
Order=16
Spectrum Mask

## Slide 7: Comparison between 802.22b proposal and 802.22
With the same filtering technique (FIR Equirripple) and the same filter order
802.22
802.22b
Spectrum
Mask

## Slide 8: Comparison between 802.22b proposal and 802.22

## Slide 9: Conclusion
From the simulations, we conclude that 802.22b PHY proposed by document 22-12-0090-02-000b satisfies the FCC spectrum mask with low-order FIR filter implementation
The filter is of low complexity and feasible in practice.
Comparatively, 802.22 base PHY required much higher order FIR filter to meet the FCC spectrum mask.