## Slide 1: January 2013 TGa Review
IEEE P802.22 Wireless RANs Date: 2013-01-12
Authors:
Notice: This document has been prepared to assist IEEE 802.22. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.22.
Patent Policy and Procedures: The contributor is familiar with the IEEE 802 Patent Policy and Procedures http://standards.ieee.org/guides/bylaws/sb-bylaws.pdf including the statement "IEEE standards may include the known use of patent(s), including patent applications, provided the IEEE receives assurance from the patent holder or applicant with respect to patents essential for compliance with both mandatory and optional portions of the standard." Early disclosure to the Working Group of patent information that might be relevant to the standard is essential to reduce the possibility for delays in the development process and increase the likelihood that the draft publication will be approved for publication. Please notify the Chair
Apurva Mody <apurva.mody@ieee.org> as early as possible, in written or electronic form, if patented technology (or technology under patent application) might be incorporated into a draft standard being developed within the IEEE 802.22 Working Group. If you have questions, contact the IEEE Patent Committee Administrator at patcom@iee.org.

## Slide 2: Abstract
To review work done to date to resolve comments in D2, review any remaining comments (and close them), and discuss moving into the final phase of balloting.

## Slide 3: Primitive Development
Development of system primitive for both M- & C-SAP have been completed
Added Clause 14.1: To describe the format of the primitives
Added Clause 14.2: Contains primitive definitions for the following SAPs:
  Added section 14.2.1 for M-SAP primitive definitions
  Added section 14.2.2 for SM-SSF-SAP primitive definitions
  Added section 14.2.3 for SM-GL-SAP primitive definitions
  Added section 14.2.4 for C-SAP primitive definitions
The next set of slides will give a description of the new primitives and reference where they can be found in the draft

## Slide 4: M-SAP Primitives (1/2)
Accounting management primitives:
  Accounting management pertains to monitoring and managing information regarding CPE data transmission usage. (added to 14.2.1.1)
Internet Protocol (IP) Management primitives:
  IP management pertains to executing primitives related to establishing IP connections using the secondary management connection during CPE intialization (see Section 7.14.2.13). (added to 14.2.1.2)
Database Service Primitives:
  The following list of messages, present in the IEEE P802.22 Standard, defines the necessary messaging to support access to the database service by the BS. These primitives existed in section 10.7.1 of the draft. The content of the primitives were updated to align with the formatting of primitives defined in 14.1. (added to 14.2.1.3)
BS Configuration and Monitoring Primitives:
  The BS SM occasionally sends the available channel list to its higher layers for additional channel classification. These primitives existed in section 10.7.2 of the draft. The content of the primitives were updated to align with the formatting of primitives defined in 14.1. (added to 14.2.1.4)

## Slide 5: M-SAP Primitives (2/2)
CPE Reports the Resulting Available WRAN Service:
  The selection of WRAN service by the CPE is performed by its higher layers. The M-SAP is an interface that provides a means of exchange information between the SA and the higher layers. These primitives existed in section 10.7.3 of the draft. The content of the primitives were updated to align with the formatting of primitives defined in 14.1. (added to 14.2.1.5)
Antenna Primitives:
  Essential antenna information is provided to the MAC by the antenna through the M-SAP. The M-SAP is an interface that provides a means of exchanging information between the SM at the BS MAC and the SSA at the CPE MAC and their respective antenna. These primitives existed in section 10.7.6 of the draft. The content of the primitives were updated to align with the formatting of primitives defined in 14.1. (added to 14.2.1.6)

## Slide 6: SM-SSF-SAP & SM-GL-SAP Primitives
Spectrum Sensing Function Primitives (SM-SSF-SAP):
  The IEEE 802.22 PHY layer shall provide local spectrum sensing services through its SSF accessed through the SM-SSF-SAP. These primitives existed in section 10.7.4 of the draft. The content of the primitives were updated to align with the formatting of primitives defined in 14.1. (added to 14.2.2.1)
Geo-location Primitives (SM-GL-SAP):
  The PHY layer provides local geo-location services through its satellite-based location acquisition unit to the SM/SSA through the SM-GL-SAP. These primitives existed in section 10.7.5 of the draft. The content of the primitives were updated to align with the formatting of primitives defined in 14.1. (added to 14.2.3.1)
In the current base standard, SM-SSF- and SM-GL-SAP were only referenced in Section 10.7.4 and 10.7.5. Text in section 5.2 “Management Reference Architecture” needs to be updated. Modification of text in section 5.2 to include a description of the SM-SSF- and SM-GL-SAP have been provided in DCN 22-12/109r0.

## Slide 7: C-SAP Primitives (1/2)
Security Management Primitives:
  Security management pertain to monitoring and managing information regarding the CPE (i.e. ‘Supplicant’) and the AAA/NCMS (i.e. ‘Authenticator’) exchanging security credentials in order to mutually authenticate each other and establish an AK at the CPE and BS. (added to 14.2.4.1)
Multicast Management primitives:
  Multicast management primitives pertain to monitoring and managing information regarding setting up multicast groups for CPEs. (added to 14.2.4.2)
Network Entry Management Primitives:
  The initialization and network entry procedures for the CPE is described in Sections 7.14.2. (added to 14.2.4.3)
CPE State Management Primitives:
  CPE State Management Primitives relate to managing the active (registration) state of the CPE. The active (registration) state of the CPE is manipulated as per Spectrum Manager policies (see 10.2.5), and during the registration process (see 7.14.2.11) during network entry/re-entry. CPE power management can be supported by properly scheduling execution CPE State Management Primitives. This is done via DREG-REQ/CMD.(added to 14.2.4.4)

## Slide 8: C-SAP Primitives (2/2)
CPE Reports the Resulting Available WRAN Service:
  The selection of WRAN service by the CPE is performed by its higher layers. The M-SAP is an interface that provides a means of exchange information between the SA and the higher layers. These primitives existed in section 10.7.3 of the draft. The content of the primitives were updated to align with the formatting of primitives defined in 14.1. (added to 14.2.1.5)
Antenna Primitives:
  Essential antenna information is provided to the MAC by the antenna through the M-SAP. The M-SAP is an interface that provides a means of exchanging information between the SM at the BS MAC and the SSA at the CPE MAC and their respective antenna. These primitives existed in section 10.7.1 of the draft. The content of the primitives were updated to align with the formatting of primitives defined in 14.1. (added to 14.2.1.3)
Radio Resource Management Primitives:
  Radio Resource Management Primitives allow the NCMS to monitor usage of radio resources in the DS and US at a particular BS. (added to 14.2.4.5)
Service Flow Management Primitives:
  Service Flow Management Primitives allow the NCMS to maintain configuration of services flows on CPEs. The are two types of reports that can be retrieved, percentage of resources allocated in the DS/US and amount of slots allocated in a DS/US region. (added to 14.2.4.6)

## Slide 9: Going Forward (?)
As of the current state of the draft, (D3), all of the technical work that we sought to accomplish with this amendment has been accomplished.
If the group is pleased with the work done, we can move forward to Sponsor Ballot phase, or initiate another Letter Ballot to allow the working group more time to review it. Either way a motion will be have to be made prior to concluding the working group session this week.

## Slide 10: References