## Slide 1: Link Budget Analysis for Devices with Low-Height Antennas
Notice: This document has been prepared to assist IEEE 802.22. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.22.
Patent Policy and Procedures: The contributor is familiar with the IEEE 802 Patent Policy and Procedures http://standards.ieee.org/guides/bylaws/sb-bylaws.pdf including the statement "IEEE standards may include the known use of patent(s), including patent applications, provided the IEEE receives assurance from the patent holder or applicant with respect to patents essential for compliance with both mandatory and optional portions of the standard." Early disclosure to the Working Group of patent information that might be relevant to the standard is essential to reduce the possibility for delays in the development process and increase the likelihood that the draft publication will be approved for publication. Please notify the Chair
Wendong Hu as early as possible, in written or electronic form, if patented technology (or technology under patent application) might be incorporated into a draft standard being developed within the IEEE 802.22 Working Group. If you have questions, contact the IEEE Patent Committee Administrator at patcom@iee.org.
Date: 2013-03-20

## Slide 2: Abstract
We provide H-CPE  L-CPE link budget analysis based on appropriate propagation model for low-height antenna devices.
Hata and Extended-Hata models were derived specifically for propagation of highly positioned antennas. In the IEEE 802.22b context it can be useful for link budget analysis of
  BS  H-CPE, BS  L-CPE,
  H-CPE H-CPE, provided that at least one H-CPE ≥ 30m

## Slide 3: Evaluated 802.22b Configuration
H-CPE  L-CPE link
H-CPE
  Personal/Portable (100mW)
L-CPE
  Personal/Portable (100mW, longer link range - evaluated)
  Sensing Only (50mW, shorter link range – not evaluated)
Gabriel Villardi (NICT)
* We consider personal/portable case only to get insight on the maximum link range

## Slide 4: Assumptions
Low-Height Antennas Propagation Model [1], [2] is considered.
H-CPE and L-CPE receiver sensitivity level [3]
  -91.3 dBm for 6 MHz bandwidth (QPSK1/2 rate with BER 2*10-4).
Device Noise Figure: 6 dB
Building penetration losses:
  5.4 dB for suburban house (Standard wood-frame house with brick veneer foil on the outside) [1], [2]
  17.7 dB for Commercial Building (Heavy Concrete Structure with steel reinforcement) [1], [2]
  9.4 dB for commercial building (Light concrete structure) [6]
H-CPE and L-CPE height above ground are as follows:
  H-CPE: 10 m
  L-CPE: 2 m
  Implementation Losses (CPE): Receiver Implementation Margin (2.1 dB), Interference Allowance (1 dB), decoder implementation margins for QPSK (1.1 dB)

## Slide 5
Link Budget
EIRP
Fading Margin
Path-Loss
Building Loss
Rx Level
Antenna
Gain
Implementation Margin
Decode Implementation
Margin
Interference Allowance
Min. Sig Level
Demodulation
Thermal Noise Floor
Noise Figure
Min. SNR

## Slide 6: Link Budget – Suburban (Rx Outdoor)
EIRP (dBm) | Fading Margin (dB) | Building Loss (dB) | Min. Signal Level (dBm) | Distance (m)
20 | 0 | 0 | -91.3 | 530
20 | 5 | 0 | -91.3 | 410
20 | 10 | 0 | -91.3 | 320
20 | 15 | 0 | -91.3 | 240
20 | 20 | 0 | -91.3 | 190
Fading Margin Range: 0 dB ~ 20 dB;
QPSK ½;
Sensitivity: - 91.3 dBm, Channel Bandwidth: 6 MHz
H-CPE: 10 m, L-CPE: 2 m;
best case

## Slide 7: Link Budget – Suburban (Rx Indoor)
EIRP (dBm) | Fading Margin (dB) | Building Loss (dB) | Min. Signal Level (dBm) | Distance (m)
20 | 0 | 5.4 | -91.3 | 400
20 | 5 | 5.4 | -91.3 | 310
20 | 10 | 5.4 | -91.3 | 240
20 | 15 | 5.4 | -91.3 | 180
20 | 20 | 5.4 | -91.3 | 140
Fading Margin Range: 0 dB ~ 20 dB;
QPSK ½;
Sensitivity: - 91.3 dBm, Channel Bandwidth: 6 MHz
H-CPE: 10 m, L-CPE: 2 m;
worst case

## Slide 8: Link Budget – Urban (Rx Outdoor)
Fading Margin Range: 0 dB ~ 20 dB
QPSK ½:
Sensitivity: - 91.3 dBm, Channel Bandwidth: 6 MHz
EIRP (dBm) | Fading Margin (dB) | Building Loss (dB) | Min. Signal Level (dBm) | Distance (m)
20 | 0 | 0 | -91.3 | 510
20 | 5 | 0 | -91.3 | 380
20 | 10 | 0 | -91.3 | 290
20 | 15 | 0 | -91.3 | 220
20 | 20 | 0 | -91.3 | 160
best case
H-CPE: 10 m, L-CPE: 2 m;

## Slide 9: Link Budget – Urban (Rx Indoor) Light Concrete Structure
Fading Margin Range: 0 dB ~ 20 dB
QPSK ½:
Sensitivity: - 91.3 dBm, Channel Bandwidth: 6 MHz
EIRP (dBm) | Fading Margin (dB) | Building Loss Light Concrete (dB) | Min. Signal Level (dBm) | Distance (m)
20 | 0 | 9.4 | -91.3 | 300
20 | 5 | 9.4 | -91.3 | 220
20 | 10 | 9.4 | -91.3 | 170
20 | 15 | 9.4 | -91.3 | 130
20 | 20 | 9.4 | -91.3 | 100
worst case
H-CPE: 10 m, L-CPE: 2 m;

## Slide 10: Link Budget – Urban (Rx Indoor) Heavy Concrete Structure
Fading Margin Range: 0 dB ~ 20 dB
QPSK ½:
Sensitivity: - 91.3 dBm, Channel Bandwidth: 6 MHz
EIRP (dBm) | Fading Margin (dB) | Building Loss Heavy Concrete (dB) | Min. Signal Level (dBm) | Distance (m)
20 | 0 | 17.7 | -91.3 | 190
20 | 5 | 17.7 | -91.3 | 140
20 | 10 | 17.7 | -91.3 | 110
20 | 15 | 17.7 | -91.3 | 80
20 | 20 | 17.7 | -91.3 | 60
worst case
H-CPE: 10 m, L-CPE: 2 m;

## Slide 11: Conclusions
Using models developed for broadcasting services, i.e., Hata and Extended-Hata models, can provide very conservative link range estimations for applications in which antennas heights are low
  H-CPE to L-CPE best case 3900 m (Tx: 10 m, Rx 2 m) [4]
  Portable CPE to portable CPE best case 2876 m (Tx: 0.5, Rx 30 m) [5]
Using a model derived for low height antennas the estimated link range significantly reduced to
  H-CPE to L-CPE best case 530 m (suburban Rx outdoors)
  H-CPE to L-CPE worst case 100 m (Urban Rx indoors – Light Concrete Structure)
  H-CPE to L-CPE worst case 60 m (Urban Rx indoors – Heavy Concrete Structure)
This strongly indicates the need for spatial diversity both at Tx and Rx to increase the link range of 802.22b based use-cases where the devices antenna AGL is low.
We believe that, especially closed loop diversity schemes, have the potential to significantly increase the link range of low-height antenna use-cases of 802.22b.

## Slide 12: References
[1] G.P. Villardi, C.S. Sum, C. Sun, Y.D. Alemseged and H. Harada, “Efficiency of Dynamic Frequency Selection Based Coexistence Mechanisms for TV White Space Enabled Cognitive Wireless Access Points”, IEEE Wireless Communications, Vol. 19, Issue 6, Dec. 2012.
[2] G.P. Villardi, C. Sun, Y.D. Alemseged and H. Harada, “Coexistence of TV White Space Enabled Cognitive Wireless Access Points,” Wireless Communications and Networking Conference (WCNC 2012), Apr. 2012.
[3] Std IEEE802.22-2011.
[4] Z. Xin, C.W. Pyo, C. Song, M. Zhou and H. Harada, “Preliminary Link Budget Analysis for IEEE 802.22b”, doc.: IEEE 802.22-12/0055r4, May 2012.
[5] S. Shigenobu and B. Zhao, “Link Budget Analysis for IEEE 802.22b”, doc.: IEEE 802.22-12/0054r0, May 2012.
[6] H.K. Kobayashi and G. Patrick, “Preliminary Building Attenuation Model”, NTIA Technical Memorandum 92-155, May 1992.