## Slide 1: IEEE 802.19.1 Overview
Stanislav Filin, NICT
Hyunduk Kang, ETRI
Steve Shellhammer, Qualcomm

## Slide 2: Outline
Background
Key parts of the draft standard
System architecture
Coexistence services
Procedures
Data types, primitives, and messages
Entity operation profiles
Coexistence algorithms
Further reading

## Slide 3: Background
Recently radio regulations in some countries allow secondary radio systems to operate in temporally unused parts of particular frequency bands, also known as white space
Several types of secondary radio systems have been developed or are under development to take advantage of the new radio regulations including
  IEEE 802.22
  IEEE 802.11af
  IEEE 802.15.4m

## Slide 4: Background
White spaces are not exclusively assigned to a particular radio system
Any system that fulfils the radio regulation can operate in such frequency bands
Correspondingly, there is a need for coexistence mechanisms between different white space radio systems

## Slide 5: Background
With understanding of the need to provide coexistence solutions for different radio systems operating in white space frequency bands, IEEE 802 committee started project 802.19.1 to develop standard for “TV White Space Coexistence Methods” in December 2009
This standard will specify radio technology independent methods for coexistence among dissimilar or independently operated TV Band Device networks and dissimilar TV Band Devices

## Slide 6: Key parts of the draft standard

## Slide 7: System architecture

## Slide 8: System architecture
The Coexistence Discovery and Information Server (CDIS) provides neighbor discovery service to the Coexistence Managers
The Coexistence Manager (CM) provides either information or management service to the white space radio systems it serves
The Coexistence Enabler (CE) provides interface between different types of white space radio systems and IEEE 802.19.1 coexistence system in a unified format

## Slide 9: Coexistence services
Service provided by CDIS to CMs
  Coexistence discovery service: CDIS informs CMs about potential neighbors of the white space radio systems served by these Coexistence Managers
Services provided by 802.19.1 coexistence system to white space radio systems
  Information service: CM provides a white space radio system information about its potential neighbors including their operating frequencies, potential interference levels etc
  Management service: CM provides a white space radio system reconfiguration requests that create such configuration of this white space radio system that its operation is improved according to some criteria

## Slide 10: Procedures
Procedures describe messages and primitives exchange among the coexistence system entities (CDIS, CM, and CE) and external entities (TVWS database and white space radio system
Examples of the procedures
  Subscription
  Registration
  Procedures for coexistence discovery
  Procedures for reconfiguration
  Procedures for negotiation between different CMs

## Slide 11: Data types, primitives, and messages
Data types, primitives, and messages are defined using ASN.1 notation
Messages are used for communication among the coexistence system entities: CDIS, CM, and CE
Primitives are used for
  Communication between CE and white space radio system
  By the coexistence system entities to access transport services, e.g., TCP/IP
Data types describe parameters used in messages and primitives

## Slide 12: Entity operation profiles
IEEE 802.19.1 draft standard defines detailed operation of its entities: CDIS, CM, and CE
Entity operation is profile-dependent
  Several profiles are defined for CDIS, CM, and CE operation
Profiles are build on the common part of the draft
  System architecture and reference model
  Procedures
  Data types
  Primitives
  Messages

## Slide 13: Entity operation profiles
Profiles are interoperable with each other
  CDIS is able to serve a CM operating according to any profile
  CMs operating according to different profiles are able to exchange information with each other

## Slide 14: Coexistence algorithms
Two classes of coexistence algorithms are defined
  Coexistence discovery algorithms
  Coexistence decision algorithms
Coexistence discovery algorithms are used by CDIS and CM to discover white space radio systems that may affect each other performance
Coexistence decision algorithms are used by a CM to make coexistence decisions related to white space radio system reconfiguration
The standard describes several algorithms of each class as implementation examples

## Slide 15: Further reading
T. Baykas et al, “Developing a standard for TV white space coexistence: Technical challenges and solution approaches,” IEEE Wireless Communications, Feb 2012
  Overview of the first stages of the IEEE 802.19.1 draft standard development
J. Wang et al, “A feasible neighbor discovery algorithm for coexistence control system over TVWS,” IEEE WCNC 2012
  Example of coexistence discovery algorithm
J. Wang et al, “Coexistence protocol design for autonomous decision-making systems in TV white space,” IEEE WCNC 2012
  Example of coexistence decision making algorithm
S. Filin and H. Harada, “Feasibility study of the IEEE 802.19.1 TVWS coexistence protocol,” IEEE 802.19-12/138r0, IEEE 802.19 Mentor
  Example of implementation of the IEEE 802.19.1 coexistence system