## Slide 1: Comment Resolution related to LCID and FID
IEEE P802.22 Wireless RANs Date: 2013-11-21
Authors:
Notice: This document has been prepared to assist IEEE 802.22. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.22.
Patent Policy and Procedures: The contributor is familiar with the IEEE 802 Patent Policy and Procedures
<http://standards.ieee.org/guides/bylaws/sb-bylaws.pdf>, including the statement "IEEE standards may include the known use of patent(s), including patent applications, provided the IEEE receives assurance from the patent holder or applicant with respect to patents essential for compliance with both mandatory and optional portions of the standard." Early disclosure to the Working Group of patent information that might be relevant to the standard is essential to reduce the possibility for delays in the development process and increase the likelihood that the draft publication will be approved for publication. Please notify the Chair Apurva Mody <apurva.mody@ieee.org> as early as possible, in written or electronic form, if patented technology (or technology under patent application) might be incorporated into a draft standard being developed within the IEEE 802.22 Working Group. If you have questions, contact the IEEE Patent Committee Administrator at <patcom@ieee.org>.

## Slide 2: Comment Resolution related to LCID (6, 80,156, 212)
ID | Comment | Suggested Remedy
6 | LCID is not necessary since this ID is not used in any operations | Delete LCID
80 | Local cell ID does not affect on communications since all devices can be idendified by SID | Remove LCID.
156 | It seems to me that the definition of "local cell" is similar to that of the "group". | If these definitions are same, merge to single terminology. The same applies to "local cell ID" and "group ID".
212 | What is the purpose of the LCID? If it's to uniquely identify a local cell at an R-CPE, then are we to suppose that an R-CPE is going to service more than one local Cell? If this is not the intention, then won't the Station ID seem sufficient to uniquely identify the R-CPE and the "local" cell it services? | If R-CPE isn't supposed to manage multiple local Cell's then remove the concept of the local Cell id from the draft.
Proposed Remedy
: Accept to remove LCID from Draft1.0

## Slide 3: Comment Resolution related to FID (81, 213, 214)
81 | FID is defined as 3 bits length in the legacy 22 standard. Then to minimize modification, it is better to keep 3 bits length of FID. | Modify 8 bits FID to 6 bits FID for which defines 3 bit for downstream and 3 bit for up stream
213 | 8bits for a FID may be excesssive. When delivering traffic in the DS or US, the station ID is provided in the MAP IE indicating where in DS/US the allocation exists (along with OFDM slots the allocation was assigned to). The CPE then grabs that allocation, decodes it, and parses it for MAC PDUs. Each MAC PDU found will have it's own GMH, that indicates which flow the PDU was for/from (e.g. basic, primary mgmt, 2ndary mgmt, BE, etc). With regards to scheduling and requesting bandwidth, the BS deals with how much bandwidth is assigned to the station and the CPE deals with requesting enough bandwidth to service the sum of its flows (as an aggregate). Either the BS or CPE, doesn't (or shouldn't) be setting grants for each individual flow. If we need to accomodate more devices and R-CPEs, then an expansion of the number of stations (SIDs) is warranted, not the # of flow IDs | Return to use of a 3bit flow ID. We may also need to have a proper discussion on addressing/address management, or order to make sure "legacy" CPEs can properly interface with the R-CPE, and MR-BS.
214 | Flow ID doesn't need to have a distinct identification to distinguish bewteen US and DS. This differentiation of scope is handled by signalling the allocation for a SID in DS-MAP and US-MAP Ies. These IEs can define where specific allocations exist. For centrally controlled R-CPEs, the MR-BS defines/sets the allocations. For distributed R-CPEs, they have their own MAPs with their on IEs defining allocations whose scope exists within the context of that R-CPEs US or DS access/relay zones. | Undo modification in this paragraph. See previous comment regarding size of 8bit FID.
Proposed Remedy
: Accept to change 8bit FID to 3bit FID defined in Std. 802.22-2011