## Slide 1: Comment Resolution related to Frame Configuration
IEEE P802.22 Wireless RANs Date: 2013-11-21
Authors:
Notice: This document has been prepared to assist IEEE 802.22. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.22.
Patent Policy and Procedures: The contributor is familiar with the IEEE 802 Patent Policy and Procedures
<http://standards.ieee.org/guides/bylaws/sb-bylaws.pdf>, including the statement "IEEE standards may include the known use of patent(s), including patent applications, provided the IEEE receives assurance from the patent holder or applicant with respect to patents essential for compliance with both mandatory and optional portions of the standard." Early disclosure to the Working Group of patent information that might be relevant to the standard is essential to reduce the possibility for delays in the development process and increase the likelihood that the draft publication will be approved for publication. Please notify the Chair Apurva Mody <apurva.mody@ieee.org> as early as possible, in written or electronic form, if patented technology (or technology under patent application) might be incorporated into a draft standard being developed within the IEEE 802.22 Working Group. If you have questions, contact the IEEE Patent Committee Administrator at <patcom@ieee.org>.

## Slide 2: Comment Resolution related to CID #85, #159
ID | Comment | Suggested Remedy
85 | "A general frame … the local cell". There is not any reason why two defferent modes is used in MR-WRAN. Add the reason. | "A centralized relay mode is …, while a distributed relay mode can extend the service coverage"
159 | Why can only the distributed scheduling R-CPE configure the local cell? Why cannot the centralized scheduling R-CPE configure the local cell under the control of MR-BS? | Clarify the functions of distributed scheduling and centralized scheduling R-CPEs in detail.

## Slide 3: Centralized Scheduling vs. Distributed Scheduling
On a distributed relay mode, a distributed scheduling R-CPE configures a local cell containing more than one S-CPE within an MR-WRAN cell, and manages the S-CPEs locally by transmitting network management information such as a local frame preamble, DRZ-FCH, DRZ-MAPs etc, which enable to reduce the network management overhead of the MR-BS as well as could extend the service coverage of MR-WRAN.
On a centralized relay mode, a centralized scheduling R-CPE relays frames including control frames or data frames received from(to) the MR-BS to(from) the S-CPE, which will enhance connection reliability between the MR-BS and S-CPEs. Moreover, a centralized scheduling R-CPE may relay network management information received from an MR-BS such as the preamble, FCH, MAPs etc to S-CPEs to assist the network management of the MR-BS, which will also extend the service coverage of MR-WRAN.

## Slide 4: Proposed Resolution for #85, #159
Modify the following sentences at 7.4b
  On the centralized relay mode, a centralized scheduling R-CPE provides relay connections for the S-CPEs under the management of the MR-BS and relays frames including control frames or data frames received from (to) the MR-BS to (from) the S-CPE, which will enhance connection reliability between the MR-BS and S-CPEs. On the distributed relay mode, on the other hand, a distributed scheduling R-CPE configures a local cell within the MR-WRAN cell, and has the similar functionality of MR-BS and manages S-CPEs within the local cell.
  On a distributed relay mode, a distributed scheduling R-CPE configures a local cell containing more than one S-CPE within an MR-WRAN cell, and manages the S-CPEs locally by transmitting network management information such as a local frame preamble, DRZ-FCH, DRZ-MAPs etc, which enable to reduce the network management overhead of the MR-BS as well as could extend the service coverage of MR-WRAN.
  On a centralized relay mode, a centralized scheduling R-CPE relays frames including control frames or data frames received from(to) the MR-BS to(from) the S-CPE, which will enhance connection reliability between the MR-BS and S-CPEs. Moreover, a centralized scheduling R-CPE may relay network management information received from an MR-BS such as the preamble, FCH, MAPs etc to S-CPEs to assist the network management of the MR-BS, which will also extend the service coverage of MR-WRAN.