## Slide 1: [Comment Resolution related to Multi-channel operation]
IEEE P802.22b Wireless RANs Date: 2014-1-22
Authors:
Notice: This document has been prepared to assist IEEE 802.22. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.22.
Patent Policy and Procedures: The contributor is familiar with the IEEE 802 Patent Policy and Procedures http://standards.ieee.org/guides/bylaws/sb-bylaws.pdf including the statement "IEEE standards may include the known use of patent(s), including patent applications, provided the IEEE receives assurance from the patent holder or applicant with respect to patents essential for compliance with both mandatory and optional portions of the standard." Early disclosure to the Working Group of patent information that might be relevant to the standard is essential to reduce the possibility for delays in the development process and increase the likelihood that the draft publication will be approved for publication. Please notify the Chair
Apurva Mody <apurva.mody@ieee.org> as early as possible, in written or electronic form, if patented technology (or technology under patent application) might be incorporated into a draft standard being developed within the IEEE 802.22 Working Group. If you have questions, contact the IEEE Patent Committee Administrator at patcom@iee.org.

## Slide 2: Abstract
This contribution presents the comment resolution related to Multi-channel operation for CID #7, #8, #9, #10, #11, #13, #14 and #37.

## Slide 3: Comment Resolution related to CID #7
Proposed Remedy: Accepted
Add extra description text in the sub-clause 7.24.1 to explain the
differences functionality between SM and CAM.

## Slide 4
Add the following sentence as shown in the proposed text
  (original text) The channel allocation manager (CAM) shown in Figure AP1 is responsible for the basic multi-channel operations such as add new operating channel operation which is described in 7.24.1.1, stop operating channel which is described in 7.24.1.3 and switch operating channel which is described in 7.24.1.4.
  (proposed text) The channel allocation manager (CAM) shown in Figure AP1 is responsible for the basic multi-channel operations such as add new operating channel operation which is described in 7.24.1.1, stop operating channel which is described in 7.24.1.3 and switch operating channel which is described in 7.24.1.4. All of the basic functions described in the CAM are necessary to support the multi-channel operation in the IEEE Std. 802.22b which is different from the single channel operation supported by the IEEE Std. 802.22-2011.

## Slide 5: Comment Resolution related to CID #8
Proposed Remedy: Accepted
Modify the description text in the sub-clause 7.24.1 to explain
that the CHU is not limited to a specific channel.

## Slide 6
Modify the description text in the sub-clause 7.24.1 as shown in the proposed text
  (original text) A channel transceiver unit (CHU) is defined as a transceiver unit for a specific channel operation which is consists of a MAC and a PHY.
  (proposed text) A channel transceiver unit (CHU) is defined as a transceiver unit that operates in a specific channel within its operating frequency which is consists of a MAC and a PHY.

## Slide 7: Comment Resolution related to CID #9
Proposed Remedy: Rejected
In multi-channel operation, the number of available operating
channels is fixed during the BS initialization procedure.
Therefore, the number of channel selected for use in not limited
by the number of BS-CHU.
Please refer to the document 22-13-0163-00-000b for detail
information for acquiring the available operating channels.

## Slide 8: Comment Resolution related to CID #10
Proposed Remedy: Rejected
The BS-CAM only consider the available operating channels
during BS initialization procedure for multi-channel operation.
Please refer to the document 22-13-0163-00-000b for detail
information for acquiring the available operating channels.

## Slide 9: Comment Resolution related to CID #11
Proposed Remedy: Rejected
In multi-channel operation, the number of available operating
channels is fixed during the BS initialization procedure.
Therefore, the number of channel selected for use in not limited
by the number of CPE-CHU.
Please refer to the document 22-13-0163-00-000b for detail
information for acquiring the available operating channels.

## Slide 10: Comment Resolution related to CID #13
Proposed Remedy: Rejected
As described in the sub-clause 7.24.1.1.1, “The BS-CAM shall
select the BS-CHU which is in the state of unused or unassigned
currently ...”. This description explained the same information as
shown in the suggested remedy.

## Slide 11: Comment Resolution related to CID #14
Proposed Remedy: Rejected
As described in the sub-clause 7.24.1.1.11, “The CPE-CAM shall
select the CPE-CHU which is in the state of unused or unassigned ”.
This description explained the same information as shown in the
suggested remedy.

## Slide 12: Comment Resolution related to CID #37
Proposed Remedy: Accepted
Modify the description text in the sub-clause 7.24.1.4.9 by referring
to the suggested remedy.

## Slide 13
Modify the description text in the sub-clause 7.24.1.4.9 as shown in the proposed text
  (original text) The BS-CHU shall switch to a new operating channel when the channel switch timer is expired which means that it has reached the frame number that is set during the start channel switch timer procedure. ... Since channel switch is performed due to the necessity of termination of operation on current channel in most of the cases, a channel switch is enforced even if the channel switch acknowledgement is not receive from neither one of the CPEs.
  (proposed text) The BS-CHU shall switch to a new operating channel when the channel switch timer is expired. The channel switch timer is expired when it has reached the frame number that is set during the start channel switch timer procedure. ... Since channel switch is performed due to the necessity of terminating current operating channel in most of the cases, a channel switch is enforced even though the channel switch acknowledgement is not received from neither one of the CPEs.