## Slide 1: Comment Resolution related to PHY Mode 2 (CID 70-77)
IEEE P802.22 Wireless RANs Date: 2014-01-21
Authors:
Notice: This document has been prepared to assist IEEE 802.22. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.22.
Patent Policy and Procedures: The contributor is familiar with the IEEE 802 Patent Policy and Procedures
<http://standards.ieee.org/guides/bylaws/sb-bylaws.pdf>, including the statement "IEEE standards may include the known use of patent(s), including patent applications, provided the IEEE receives assurance from the patent holder or applicant with respect to patents essential for compliance with both mandatory and optional portions of the standard." Early disclosure to the Working Group of patent information that might be relevant to the standard is essential to reduce the possibility for delays in the development process and increase the likelihood that the draft publication will be approved for publication. Please notify the Chair Apurva Mody <apurva.mody@ieee.org> as early as possible, in written or electronic form, if patented technology (or technology under patent application) might be incorporated into a draft standard being developed within the IEEE 802.22 Working Group. If you have questions, contact the IEEE Patent Committee Administrator at <patcom@ieee.org>.

## Slide 2: Difference between Pilot Pattern
time
frequency
Data Subcarrier
Pilot Subcarrier
PHY Mode1 PHY Mode2
DS
US
Tile configuration for more robust
for fast time-varing channel

## Slide 3: To maximize US data rate, the pilot occupancy is minimized. 4 pilot symbols per tile consisting of total 28 symbols
US
4 4 7 7 7 7 7
4
4
4
4
4
4
4
4
In DS, robustness is more important
than data rate.
DS
One example of OFDM subcarrier allocation in PHY Mode 2
time
frequency
In this example, time for US is much longer than DS to make the US data rate higher.

## Slide 4: Comment Resolution related to PHY Mode2 (CID 70)
70 | The tile configuration of the symbols/subcarriers for the downstream is defined as a 4x4 square. Since the FFT used is 1024 rather than 2048 for the base 802.22 standard, this means that the robustness for the long delayed echoes is 8 times less than for the 802.22 system (theoretically 74.5/8= 9.3 usec maximum excess delay). This PHY Mode 2 will therefore be affected by long delayed echoes and will not pass the test of most of the channel models used to develop the base 802.22 standard (22-05-0055-07-0000_WRAN_channel _Modeling.doc). It will only be useful on short distances or over somewhat longer distances if not reflective surfaces are in the surrounding (such as mountains, hills, buildings, etc.) | Review the system requirement document for the 802.22b draft standard and align the parameters with these requirements. Otherwise, align the system requirement document with the expected performances of the draft standard as proposed.
ID | Comment | Suggested Remedy
Proposed Resolution:
Guard interval of PHY Mode 2 is 22.9 micro-sec for 1/8 CP mode. This is around 2/3 compared to the legacy 802.22 guard interval (37.3 micro-sec 1/8 CP mode). In 802.22b system, the communication distance could be shorter than the 802.22 system due to relay scheme. Therefore PHY Mode 2 can support 22b systems in many cases.

## Slide 5: Comment Resolution related to PHY Mode2 (CID 71)
71 | The tile configuration of the symbols/subcarriers for the downstream is defined as a 4x4 square. For the base 802.22 Standard which relies on 1 every 7 symbols for the pilot carrier, the maximum speed that could be sustained by the terminal is 148 km/h at 700 MHz, and higher for lower frequencies (22-06-0264-14-0000_OFDMA_Parameters.xls). With the proposed 1 every 3 symbols, this woull allow a maximum speed of 344 km/h. It is not clear whether this more than doubling the robustness to terminal displacement speed is aimed at operating at higher speed or at higher frequencies. | Clarify the very high speed requirement for the terminal displacement speed in the light of the rate at which this cognitive radio has to query the WSDB to acquire the new list of available channels at its new position. Review the system requirement document for the 802.22b draft standard and align the parameters with these requirements. Otherwise, align the system requirement document with the expected performances of the draft standard as proposed.
ID | Comment | Suggested Remedy
Proposed Resolution:
In PHY Mode2, the total symbol period for 1/4 CP case is 228.6 micro-sec. According to the calculation method shown in the spread sheet (22-06-0264-14-0000_OFDMA_Parameters.xls), the maximum speed that could be sustained by the terminal is 562 km/h at 700 MHz. However, this value does not necessarily show the terminal mobility. PHY Mode 2 can support faster time-varing channel although the date rate is lower than PHY Mode 1.

## Slide 6: Comment Resolution related to PHY Mode2 (CID 72)
72 | The tile configuration of the symbols/subcarriers for the upstream is defined as a 4x7 rectangle. For the base 802.22 Standard which relies on 1 every 7 symbols for the pilot carrier, the maximum speed that could be sustained by the terminal is 148 km/h at 700 MHz, and higher for lower frequencies. The performance of the upstream for this Mode 2 will be equivalent to that of the base 802.22 standard. It is unclear, however, why the upstream and downstream performance should not be the same. | Clarify the difference in robustness requirement to the terminal displacement speed for the upstream and downstream. Review the system requirement document for the 802.22b draft standard and align the parameters with these requirements. Otherwise, align the system requirement document with the expected performances of the draft standard as proposed.
ID | Comment | Suggested Remedy
Proposed Resolution:
PHY Mode 2 is designed for higher data rate in US compared to DS because 802.22b is for “Enhancement for broadband services and monitoring applications". Therefore the number of pilots per tile is minimized in US. In DS, on the other hand, we need to consider robustness in the wireless link. That is why PHY Mode2 has different tile configuration between DS and US .

## Slide 7: Comment Resolution related to PHY Mode2 (CID 73)
73 | The tile configuration of the symbols/subcarriers is defined as a 4x4 square for the downstream and 4x7 for the upstream. These tiles will fall adjacent to each other and will carry pilots on two adjacent subcarriers. This produces an irregular sampling pattern in the frequency domain that would seem to be sub-optimal to re-constitute the channel model to train against effects of multipath. | Explain the reason for this irregular sampling pattern in the frequency domain and the impact on the performance of the system as compared to the initial performance requirement document.
ID | Comment | Suggested Remedy
Proposed Resolution:
In the case of using tile configuration, the interpolation scheme to calculate the CSI on each data symbol is always possible for both time domain and frequency domain. On the other hand, in the case of current 802.22 PHY specification, interpolation scheme to calculate the CSI on each data symbol, is not always possible. “Which PHY is better” depends on the channel environment.
BER performance comparison between PHY Mode 1 and PHY Mode 2 are found in doc.: IEEE 22-13-0013-00-000b.

## Slide 8: Comment Resolution related to PHY Mode2 (CID 74)
74 | The tile configuration of the symbols/subcarriers is defined as a 4x4 square for the downstream and 4x7 for the upstream. These tiles will fall adjacent to each other and will carry pilots on two adjacent symbols in the time domain. This produces an over-sampling and irregular sampling pattern in the time domain that would seem to be much sub-optimal to track the channel variations. | Explain the reason for this over-sampling and irregular sampling pattern in the time domain and the impact on the transmission capacity of the system as compared to the initial performance requirement document.
ID | Comment | Suggested Remedy
Proposed Resolution:
Same as CID 73

## Slide 9: Comment Resolution related to PHY Mode2 (CID 75)
75 | In the base 802.22 Standard, the data allocation in the US and DS-MAPs was one-dimensional to minimize the overhead taken by the maps. It is not clear why a two-dimensional aproach is preferred for Mode 2. | Explain why a two-dimensional data mapping is needed here.
ID | Comment | Suggested Remedy
Proposed Resolution:
2-D data allocation is based on the tile configuration.

## Slide 10: Comment Resolution related to PHY Mode2 (CID 76)
76 | The mapping of the PN sequence as indicated: " (0 mapped to +1 and 1 mapped to –1)" seems to be counter-intuitive. | Invert the mapping so that 1 corresponds to +1 and 0 corresponds to -1.
ID | Comment | Suggested Remedy
Proposed Resolution:
I agree with this comment. The text should be revised as follows.

## Slide 11: Comment Resolution related to PHY Mode2 (CID 77)
77 | Co-existence of up to 32 cells in the same area seem to be overkill for this type of transmission where all BSs will transmit at the same time. 8 co-existing cells or 16 at the most would be more realistic. | Consider decreasing the number of co-existing cells and thus the number of needed preamble modulation series.
ID | Comment | Suggested Remedy
Proposed Resolution:
Table BB1 is now being reviewed under another comment (#218) discussion. Maybe the number of cells and the number of preamble modulation series will decrease.