## Slide 1: [Comment Resolution LB2 (CID 19) ]
IEEE P802.22b Wireless RANs Date: 2014-7-16
Authors:
Notice: This document has been prepared to assist IEEE 802.22. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.22.
Patent Policy and Procedures: The contributor is familiar with the IEEE 802 Patent Policy and Procedures http://standards.ieee.org/guides/bylaws/sb-bylaws.pdf including the statement "IEEE standards may include the known use of patent(s), including patent applications, provided the IEEE receives assurance from the patent holder or applicant with respect to patents essential for compliance with both mandatory and optional portions of the standard." Early disclosure to the Working Group of patent information that might be relevant to the standard is essential to reduce the possibility for delays in the development process and increase the likelihood that the draft publication will be approved for publication. Please notify the Chair
Apurva Mody <apurva.mody@ieee.org> as early as possible, in written or electronic form, if patented technology (or technology under patent application) might be incorporated into a draft standard being developed within the IEEE 802.22 Working Group. If you have questions, contact the IEEE Patent Committee Administrator at patcom@iee.org.

## Slide 2: Abstract
This contribution presents the comment resolution LB2 related to definition of Multi-channel operation for CID #19.

## Slide 3: Comment Resolution LB2 related to CID #19
Proposed Remedy: Accepted
Modify description text in those sub-clauses and figures that
related to the A-BS definition of multi-channel operation.

## Slide 4
Modify the description text in the sub-clause 7.24 as shown in the proposed text
  (original text) In Figure AN1, it is assumed that there are 2 available operating channels within the service area of the BS. In this example, multi-channel operation on BS is illustrated where only the BS is capable of receiving and transmitting over two or more operating channels and responsible to assign the operating channel to the associated CPEs within its service area. By performing the multichannel operation on BS, the BS can utilize the available operating channels by distributing the operating channels among the associated CPEs. The multi-channel operation on BS can improve the individual CPE’s throughput by decreasing the total number of associated CPEs per operating channel. In Figure AN1, CPE 1 and CPE 2 are assigned to the operating channel (f1) to communicate with the BS while CPE 3, CPE 4 and CPE 5 are assigned to the operating channel (f2) to communicate with the BS.

## Slide 5
  (proposed text) In Figure AN1, it is assumed that there are 2 available operating channels within the service area of the A-BS. In this example, multi-channel operation on A-BS is illustrated where only the A-BS is capable of receiving and transmitting over two or more operating channels and responsible to assign the operating channel to the associated A-CPEs within its service area. By performing the multichannel operation on A-BS, the A-BS can utilize the available operating channels by distributing the operating channels among the associated A-CPEs. The multi-channel operation on A-BS can improve the individual A-CPE’s throughput by decreasing the total number of associated A-CPEs per operating channel. In Figure AN1, A-CPE 1 and A-CPE 2 are assigned to the operating channel (f1) to communicate with the A-BS while A-CPE 3, A-CPE 4 and A-CPE 5 are assigned to the operating channel (f2) to communicate with the A-BS.

## Slide 6
Modify the description text in the sub-clause 7.24 as shown in the proposed text
  (original text) In Figure AO1, it is assumed that there are 5 available operating channels within the service area of the BS. In this example, multi-channel operation on BS and CPEs is illustrated where both BS and associated CPEs are capable of receiving and transmitting over two or more operating channels. BS is responsible to assign the operating channel to the associated CPEs within the service area for the utilization of available operating channels. In Figure AO1, CPE 1 is assigned to the operating channels (f1, f2, f3) to communicate with the BS while CPE 2 is assigned to the operating channels (f4, f5) to communicate with the BS. In this example, the BS can improve the individual CPE’s throughput by increasing the number of operating channels assigned to the associated CPEs.

## Slide 7
  (proposed text) In Figure AO1, it is assumed that there are 5 available operating channels within the service area of the A-BS. In this example, multi-channel operation on A-BS and A-CPEs is illustrated where both A-BS and associated A-CPEs are capable of receiving and transmitting over two or more operating channels. A-BS is responsible to assign the operating channel to the associated A-CPEs within the service area for the utilization of available operating channels. In Figure AO1, A-CPE 1 is assigned to the operating channels (f1, f2, f3) to communicate with the A-BS while A-CPE 2 is assigned to the operating channels (f4, f5) to communicate with the A-BS. In this example, the A-BS can improve the individual A-CPE’s throughput by increasing the number of operating channels assigned to the associated A-CPEs.

## Slide 8
Modify the description text in the sub-clause 7.24.1 as shown in the proposed text
  (original text) A channel allocation manager is needed on the IEEE 802.22b devices (BS and CPEs) to perform multi-channel operations which are described in 7.24.1.1, 7.24.1.3 and 7.24.1.4.
  (proposed text) A channel allocation manager is needed on the IEEE 802.22b devices (A-BS and A-CPEs) to perform multi-channel operations which are described in 7.24.1.1, 7.24.1.3 and 7.24.1.4.

## Slide 9
Modify the description text in the sub-clause 7.24.1.1 as shown in the proposed text
  (original text) When the BS is ready to operate under the multi-channel operation, the following procedure of adding new operating channel is performed on both BS and CPE which have the capability of receiving and transmitting over two or more operating channels.
  (proposed text) When the A-BS is ready to operate under the multi-channel operation, the following procedure of adding new operating channel is performed on both A-BS and A-CPE which have the capability of receiving and transmitting over two or more operating channels.

## Slide 10
Modify the description text in the sub-clause 7.24.1.2 as shown in the proposed text
  (original text) In this operation flow, the BS-CHU and CPE-CHU shall have at least one operating channel to enable the exchange of management message between BS and CPE.
  (proposed text) In this operation flow, the BS-CHU and CPE-CHU shall have at least one operating channel to enable the exchange of management message between A-BS and A-CPE.

## Slide 11
Modify the description text in the sub-clause 7.24.1.3 as shown in the proposed text
  (original text) When the BS is operating under the multi-channel operation, the following procedure of stop operating channel is performed on both BS and CPE to stop the operating channel which is requested by the BS.
  (proposed text) When the A-BS is operating under the multi-channel operation, the following procedure of stop operating channel is performed on both A-BS and A-CPE to stop the operating channel which is requested by the A-BS.

## Slide 12
Modify the description text in the sub-clause 7.24.1.4 as shown in the proposed text
  (original text) When the BS is operating under the multi-channel operation, the following procedure of switch operating channel is performed on both BS and CPE to switch the operating channel which is requested by the BS.
  (proposed text) When the A-BS is operating under the multi-channel operation, the following procedure of switch operating channel is performed on both A-BS and A-CPE to switch the operating channel which is requested by the A-BS.

## Slide 13
A-BS
A-CPE 1
Internet
f1
f2
f1
f2
f2
A-CPE 2
A-CPE 3
A-CPE 4
A-CPE 5
WSDB
Modify the Figure AN1 in the sub-clause 7.24 as shown in the proposed Figure AN1(proposed).
Figure AN1 (proposed)

## Slide 14
Modify the Figure AO1 in the sub-clause 7.24 as shown in the proposed Figure AO1(proposed).
Figure AO1 (proposed)
WSDB
A-BS
A-CPE 1
Internet
f1
f5
f2
f4
f3
A-CPE 2