## Slide 1: Proposed Work Streams
IEEE P802.22 Wireless RANs Date: 2016-03-15
Authors:
Notice: This document has been prepared to assist IEEE 802.22. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.22.
Patent Policy and Procedures: The contributor is familiar with the IEEE 802 Patent Policy and Procedures http://standards.ieee.org/guides/bylaws/sb-bylaws.pdf including the statement "IEEE standards may include the known use of patent(s), including patent applications, provided the IEEE receives assurance from the patent holder or applicant with respect to patents essential for compliance with both mandatory and optional portions of the standard." Early disclosure to the Working Group of patent information that might be relevant to the standard is essential to reduce the possibility for delays in the development process and increase the likelihood that the draft publication will be approved for publication. Please notify the Chair
Apurva Mody <apurva.mody@ieee.org> as early as possible, in written or electronic form, if patented technology (or technology under patent application) might be incorporated into a draft standard being developed within the IEEE 802.22 Working Group. If you have questions, contact the IEEE Patent Committee Administrator at patcom@iee.org.

## Slide 2: Abstract
Submission on proposed sub-groups and desired outcomes of 802.22.3 task group with estimates of milestones.

## Slide 3: Golden Rule of White Space Regulation
“Operation of an unlicensed, secondary device in TVWS may only be permitted if it does not interfere with incumbent services”
or
“Thou Shalt Not Be Where the Incumbent Is”
- Problematic, as it assumes you know where the incumbent is, and will be
- Problematic, as it does not address other band users

## Slide 4: New Golden Rule of White Space Regulation
Thou Shalt Be Where the Incumbent Isn’t
- An appropriate mix of White Space Database and SCOS

## Slide 5: Use cases for SCOS
Within a White Space radio system with built-on scanning
  802.22 uses a scanning subsystem (which is being liberally borrowed from for this TG)
With a Cognitive Radio system without sensing capability
  802.11af has no sensing capability of its own, dependent on a WSDB to allocate channels correctly
For use in future real-time spectrum assignment systems
  Especially in remote rural areas, there is considerable scope for opportunistic use of spectrum
For use by regulators, network operators and law enforcement
  Real-time spectrum management by operators and regulators
  Detection of anomalous radio activity, especially criminal activity (e.g. remote jammers)

## Slide 6: How should we sense?
On exception
On schedule
Continuous
  An open question – the answer to which is driven by what data the radios need
    Is it tactical (e.g. for meshed IoT device communication)
    Is it strategic (e.g. for spectrum management purpose)

## Slide 7: 802.22.3 minimum functional requirements
  Radio spectrum is sensed according to an accepted technique by a Spectrum Sensing Device within established hardware parameters
  This sensing data is packaged along with key metadata
    e.g. scan time, scan duration, scan location, device identifiers…
  The package is (a) transmitted to a remote system that (b) ingests and validates data, and (c) stores for further processing
  The back-end management system exchanges control information with SSDs
    e.g. device management, operation validation, integrity of information chain verification, maintenance tasks

## Slide 8: Sensing Chain
Amplifier, Tuner, Filter
SDR
DAC
Signal Processing
Packaging
Transmission
Message Queue
Ingest
Data Store
Other SSDs
SSD
Best Effort IP link

## Slide 9: SCOS Minimum Functional Spec – 1 Sensing
  Radio spectrum is sensed according to an accepted technique by a Spectrum Sensing Module and within hardware parameters
    What sensing library is being used (standardised, authorised for use in SSM, signed)
    Accepted standard for hardware/OS implementation – defined in terms of performance parameters for scanning system (there could be many permutations for hw, sw and architectures)
    Standardisation of hardware metrics in scanning chain – antenna, cables, radio receiver
    Type-approval and calibration standards
    Standards for signal processing in amplifiers, filters, FFT, etc
    Signed verification of current calibration certificate (or none)

## Slide 10: SCOS Minimum Functional Spec – 2 Packaging
  This sensing activity is packaged along with key metadata
    Scan time, duration, location, device identifiers
    Define scan parameters from radio front end – not processing subsystem (closest time between actual radio event & sample taken)
    Location information must include current GPS at the time of scan (not processing)
    If device is mobile, speed of movement must factor into minimum position error
    Position stored as actual GPS co-ordinate (NMEA0183?)
    Device status information to include – calibration/authorisation certificates, package sequence numbers, hardware state (GPS satellite lock, position uncertainty), …more
    Compressed, encrypted, signed, queued

## Slide 11
  The package is transmitted to a remote system that ingests and validates data, and stores for further processing
    Package enters device transmission queue with transmission control (package sequence)
    Package Class of Service
      Package TTL, and number of retries (and audit chit if dropped)
      Package CoS dependent on package type (scan data packages have priority over management status packages)
    Package routing
      Transmission can depend on available network interface (primary, failover)
      Depending on available interface, packages obey CoS
SCOS Minimum Functional Spec – 3a
Transmission

## Slide 12
  Package must be reliably, securely and scaleably received and transmitted to data store
    Packages ingested depending on CoS and type
      Distribute ingestion across multiple servers for redundancy (i.e. packages could be sent as IP multicast)
      Allow for ingestion based on topic to separate functional areas (scans vs status)
  Manage completeness of data received
      Ingest function has sequence monitoring on packages, forward to data store as complete scans (e.g. may need windowing if scan data is fragmented from SSD)
      Monitor audit chits for dropped transmissions (and request re-tries?)
      Flag missing scan packages and status packages for scheduling of retransmit requests to SSD
SCOS Minimum Functional Spec – 3b
Ingest

## Slide 13
  Data moved into structured database
    Data store parameters
      Scan data (split out static and mobile SSMs?)
      Goodness metric on data
    Three groups of scan data that should not be mixed
      Scheduled sample (i.e. building up a history of samples)
      Unscheduled sample (i.e. taken at time/place with decaying goodness metric)
      Exceptions bin (where scan data is incompletely received, discrepancies across SSDs, SSDs triggered by anomaly)
    Data governance layers
      Security, redundancy, non-tampering
      What interfaces are opened to querying applications
SCOS Minimum Functional Spec – 3c
Storage

## Slide 14
  The back-end management system exchanges control information with SSDs
  Manage them
    Device health reports – power, temperature, location, GPS health, OS/environment health, network health, storage health, scheduled and by query
    Manage by device, group, Class of device
  Validate their operation
    Run test scans against known data points (e.g. from WSDB)
  Verify integrity of information chain
    Software tools to validate process chain
  Perform maintenance
    Push updates to devices (software, OS, firmware, certifications)
    Perform remote reboots, resets
    Shell into device to do diagnostics
SCOS Minimum Functional Spec – 4
Management and Maintenance

## Slide 15: Other Considerations
How much can we do on SSM, to reduce transmission and back end load?
How is this transmitted to back end, and how does back end resolve differences of opinion? Kick off raw scan gathering and comparison by server side AI
How can other systems request scan resources?
Define an API to allow remote fetches of scans – does it go via RSMS? Can it go directly to SSM, under what case?
What about CPE or BS devices that do sensing – can they feed into .22.3?
Mobile phone handsets and base stations
Wi-Fi devices (802.11ac)
802.22 devices

## Slide 16: Other Considerations
SSD Synchronisation
It may be advantageous if SSDs can be synchronised to perform scans simultaneously in certain case
Read time from NTP server, conduct schedule scans in defined time multiples – data between SSMs correlate by time

## Slide 17
Quick view what’s in 802.22 that can be pulled out:
  5.1.3.2 Spectrum Sensing Automation
  5.1.3.3 Security sublayer 2
  7 Management messages, esp
    7.1.1.1.1 NMEA location
    7.1.1.1.2 IP version
    7.1.1.1.3 Spectrum sensing capability
      Antenna model
      Antenna gain
      Sensor ID
      Operational Capability
      Registration timer (use for WSDB to SSD, not CPE/BS
    7.1.6 Measurement management
    7.2 MAC PDU
    7.3 Initialisation, authentication, registration
  8 Security sublayer
  9 some may be relevant in antenna, receiver spec
  10.1 and 2 Spectrum Manager falls out of scope – back end function
  10.3 SSA
  10.4 Spectrum Sensing Funtion
  10.5 Geolocation
  10.6 Database service
  10.7 Primitives largely falls outside scope (Cognitive Radio control) until 10.7.4

## Slide 18: Next Steps
Extraction of sensing standards defined in 802.22
There’s a lot in the standard that can be forklifted into 802.22.3
Define a framework to can accommodate many sensing methods
SDR means sensing technique is a software library – how many is enough?
Identify sensing techniques and if there are existing software implementations
Identify hardware (now and coming) to establish possible sensing band at low cost
Antenna, RF front end, SDR
Review of bigger picture requirements
How do we ensure relevance across many standards and regimes
How do we connect what we’re doing to 802.18, .24

## Slide 19: References
IEEE Standard 802.22.3-Draft0.1