## Slide 1: MSOD Architecture
IEEE P802.22 Wireless RANs Date:2016-5-06
Authors:
Notice: This document has been prepared to assist IEEE 802.22. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.22.
Patent Policy and Procedures: The contributor is familiar with the IEEE 802 Patent Policy and Procedures http://standards.ieee.org/guides/bylaws/sb-bylaws.pdf including the statement "IEEE standards may include the known use of patent(s), including patent applications, provided the IEEE receives assurance from the patent holder or applicant with respect to patents essential for compliance with both mandatory and optional portions of the standard." Early disclosure to the Working Group of patent information that might be relevant to the standard is essential to reduce the possibility for delays in the development process and increase the likelihood that the draft publication will be approved for publication. Please notify the Chair
Apurva Mody <apurva.mody@ieee.org> as early as possible, in written or electronic form, if patented technology (or technology under patent application) might be incorporated into a draft standard being developed within the IEEE 802.22 Working Group. If you have questions, contact the IEEE Patent Committee Administrator at patcom@iee.org.

## Slide 2: Abstract
This presentation outlines the NIST/NTIA Measured Spectrum Occupancy Database (MSOD).

## Slide 3: Purpose
Spectrum usage measurement for LTE and Radar.
  Provides historical and Real-time data (for LTE).
Spectrum monitoring and signal identification for spectrum sharing violations.

## Slide 4: What I am going to present
Client/Server architecture for MSOD.
  How data is stored / visualized.
  How servers federate.
Sensor Management:
  How sensors are registered with the server.
  How data is sent to the server from a sensor.
  Sensor processing pipeline.
  I/Q data capture, storage and analysis:
    Signaling from server to sensor to effect I/Q capture.
  Occupancy Alerts
User Management

## Slide 5: Client/Server Architecture
Server
Server
LTE
LTE
Browser
Radar
LTE
Meta Data
Data Access Client
Occupancy Alert
Secure
Socket
HTTP
POST
HTTP
POST

## Slide 6: Transports for Measured Data
HTTP POST: Supports disconnected operation.
  Metadata + Data can be sent periodically and asynchronously.
Streaming: Continuous connection via a Secure TCP socket.
  Meta data + stream of data.

## Slide 7: Types of Data
Meta-data for location, system, federation.
Meta-data + power measurement.
I/Q data:
  Only stored on sensor host.
  Server can trigger capture and analysis of I/Q data on sensor.

## Slide 8: Meta-data
Three message types for messages sent from Sensor to Server:
  System Messages : Sent as soon as sensor connects/reconnects. Tells the server system and calibration parameters.
  Location Messages: Sent after system message.
  Data Message – describes the measurement parameters and frequency band.
  Each Message includes a sensor name and sensor key that is verified at the server.
Servers federate with each other:
  Meta-data containing summary of data stored at a server is sent to peers.
  Simple sharing model:
    Non-secure servers export meta-data to peers.
    Secure servers do not export any data (only accept data).
    Each server has a key which can be verified by any peer to which it sends metadata.
All meta-data is JSON.

## Slide 9: Power Measurements
Data Message describing measurement parameters and Frequency Range followed by power data.
  Power measurements are channelized (e.g. 180 KHz channels for LTE).
  Per band occupancy power threshold – determine whether or not a channel is occupied.
  For a streaming connection, there is one data message, followed by a persistent stream of measurements. For POSTed data, each POST is preceded by a Data message.
  For a POST message – Data Sent asynchronously as power vectors using HTTP POST transport along with Data Message.

## Slide 10: How Sensors are Managed
Sensors are configured at the server.
Sensors have system wide unique names.
Each sensor is assigned a key (password) that is included with metadata that it sends.
Sensor reads its configuration from the server before it starts to run. (Optional)
Sensor sends enough information in the Data Message for the server to be able to verify that its settings are correct.
If settings do not match, server rejects the sensor’s data causing the sensor to re-read settings and restarting itself.
If setting change during streaming, server drops connection.
  If 4 is implemented this causes the sensor to re-read settings and reconnecting.
No inbound connections to sensors (may be behind firewalls).
No inter-sensor communication.

## Slide 11: Signaling IQ Capture and analysis
Complex Baseband Source
serial/
vector
FFT
Channelize
Time Avg/Peak
SSL Socket Sink
Vector /
serial
float/int8
I/Q Capture
Block
Energy Detection
Capture File
MongoDb
Meta Data
v
Meta Data + Data Stream
(aggregated over 1 sec interval)
MSOD
v
Arm/disarm
Control Wrapper Python Script
GET : Sensor Config.
MongoDb
Meta Data
Capture File
Offline analysis
Start/Stop
Capture
Analyze data
SSL Socket
HTTPs
Trigger
I/Q
I/Q
LTE Sensor
HTTP POST: Analysis results

## Slide 12
Sensor
memcache
Occupancy Alert Server
Stream server
Occupancy
Subscriber
Web Browser
Database
Web Server
Subscribe
Notify
Web Socket
Power Spectrum Vectors
Capture
Publish
Aggregate
Providing Occupancy Alerts
Provides clients an occupancy alert whenever occupancy of observed spectrum changes.

## Slide 13: External interactions with Users
Server may support logins (Optional).
Once a user is logged into a server, he is able to download data stored by a sensor or visualize it by occupancy.
  API is defined for these interactions.
  Web browser client uses this API for data visualization.
Administrative users must log in to administer the server.
Admin login is password based.
Administrators may add and configure sensors, configure the server and manage users.
  Admin interface to support administrative actions.
  All interactions via REST API to server.