## Slide 1: 802.24.1 Smart Grid TAG Consolidated White Paper Presentation
Date: 2014-11-04
Authors:

## Slide 2: Key Standards for Integrated Grid Communications Networks
LAN
WAN
FAN
Devices
NAN
IEEE 802.3 Ethernet IEEE 802.11 Wi-Fi
Ethernet 1000BASE-X
IEEE 802.16 WiMAX IEEE 802.11 Mesh
RF Mesh: 802.15.4g WiSUN IEEE 802.11ah
IEEE 802.11 Wi-Fi IEEE 802.15.4 ZigBee

## Slide 3
Examples of utility communications protocols
Re-Do and correct- make a slide like this

## Slide 5: IEEE-SA Smart Grid

## Slide 6: The Smart Grid = Electric Grid + Intelligence
Concern over the environment (CO2 emissions), scarcity of resources (fossil fuels), safety (nuclear plants) are precipitating a universal move to re-examine the Electric Gird.
The Smart Grid is defined as a radical evolution of the energy supply and consumption infrastructure that will provide providers and consumers with unprecedented levels of reliability and control while reducing the adverse environmental impact of energy generation and consumption.
A smart grid delivers electricity from suppliers to consumers using two-way digital technology to control appliances at consumers' homes to save energy, reduce cost and increase reliability and transparency.
Smart meters are part of a smart grid, but alone do not constitute a smart grid.
Notes: Clarify the meaning of “intelligence” with a new bullet

## Slide 7: Smart Grid
Smart Grid is defined as:
  Providing bidirectional communication of power quality, supply, and demand across the power grid to utilize electricity more dynamically resulting in increased energy efficiency and power grid reliability. This change is necessary to manage the increased variability caused by renewable resources, the increased peak demand created by energy intensive consumers such as electric vehicles, and to minimize the environmental impact of ever increasing aggregate demand for electrical power.
IEEE 802 networking technologies bring the following advantages to Smart Grid communications:
  Enterprise grade security compatibility
  Huge ecosystem (billions of products, hundreds of manufacturers)
  Long-term (20 year), battery-powered operation
  Continued operation during line fault events when using wireless media
  Wide choice of products across the spectrum of power versus performance
  Ability to be implemented in resource-constrained devices
  Ongoing development of standards to address changing environment and technology
  Wireless standards that operate in a licensed and license-exempt spectrum
  Offers a rich set of data rate/range/latency tradeoffs
  Common upper layer interface to seamlessly integrate into existing IT systems

## Slide 8: SG Network Architecture
High level example of an AMI system
Detailed View:

## Slide 9: Layering of M2M technology
Underlying Network Layer
Common Service Layer
Application Layer
IEEE 802 standards provide underlying networks with enhanced coverage and accessibility, quality of service, security (such as authentication and encryption), and reliability (high availability of network infrastructure).

## Slide 10
Something on cyber security and IEEE 802

## Slide 11
Example applications that take advantage of low power operation, (water, oil/gas, line sensors)
Example of “constrained” types of devices

## Slide 12
Comparison with PLC – advantage of operation even if power line is damaged

## Slide 13
Graphic / example of a mesh network

## Slide 14
Examples of how higher layer protocols such as IEC 61850, 61968, DLMS/COSEM, can operate over IEEE 802 and take advantage of its features.

## Slide 15: IEEE 802.11 standards hierarchy
IEEE
11ac
11ad
11ae
11af
11ah
802.11a through 802.11z: Completed
Higher rate in 5GHz band
11ai
11ak
Higher rate in 60GHz band
Prioritization of management frames
TV White Space
915MHz Band operation (sub 1GHz)
Fast Initial Association
Pre-Association Discovery Task Group
11aj
China Millimeter Wave Task Group
Completed
Active: More Grid relevant
Active: Less Grid relevant
11aq
General Link (full bridging over WLAN) joint with 802.1
802.3
802.11
802.15
802.16
802.22
802.21
11ax
High Efficiency WLAN (HEW)

## Slide 16: 802.11 – Spectrum / Rate view
802.11ac
802.11n
1GHz
10GHz
500MHz
2GHz
5GHz
802.11g
802.11a
.11ah
.11af
.11y
10Mbps
100Mbps
.11ad
500Mbps
.11p
.11j
60GHz
802.11
802.11b
802.11n
1Mbps

## Slide 17: IEEE 802.15 standards hierarchy
802.15.10
Layer 2 Routing Task Group
IEEE
4r
4e
4g
4k
4m
4n
4q
Smart Utility Networks (WiSUN) AMI
LECIM
AMI for TV White Space
802.3
802.11
802.16
802.22
802.21
802.15
Key Management Protocol Task Group
Completed
Active – More Grid relevant
Active – Less Grid relevant
802.15.4
802.15.9
ZigBee

## Slide 18: 802.15.4 PHY Overview (data rate vs frequency)
1GHz
500MHz
2GHz
5GHz
10Kbps
100Kbps
1Mbps
BPSK DSSS
O-QPSK
O-QPSK, ASK
O-QPSK, ASK
BPSK DSSS
BPSK DSSS
868
915
950
CSS
GFSK
O-QPSK, ASK
780
863
4g O-QPSK
4g ODFM
4g ODFM
4g ODFM
4g O-QPSK
4g 2FSK
4g 2FSK
4g 4FSK
4g O-QPSK
4g 2FSK
4g ODFM
4g 2FSK
4g 4FSK
4g 2FSK
4g 2FSK
4g 4FSK
4g 2FSK
4g 2FSK
4g 4FSK
4g 2FSK
4g ODFM
O-QPSK CSS
MPSK

## Slide 19: IEEE 802.16 standards hierarchy
802.3
802.11
802.15
802.22
802.21
IEEE
Completed – Less Relevant
Completed – Grid Relevant
Active – Limited grid relevance
1a
1b
802.16.1
16n
16p
High Reliability
Machine to Machine
WiMAX
WiMAX 2
802.16-2012
802.16
16q
Small Cell Backhaul
16r
Multi-Tier Networks
Performance Metrics
802.16.3