## Slide 1: 802.24.1 Smart Grid TAG Consolidated White Paper Presentation
Date: 2014-11-04
Authors:

## Slide 2: Note – this is a draft: work in progress…

## Slide 3: IEEE-SA Smart Grid

## Slide 4: Smart Grid
Smart Grid is defined as:
  Providing bidirectional communication of power quality, supply, and demand across the power grid to utilize electricity more dynamically resulting in increased energy efficiency and power grid reliability. This change is necessary to manage the increased variability caused by renewable resources, the increased peak demand created by energy intensive consumers such as electric vehicles, and to minimize the environmental impact of ever increasing aggregate demand for electrical power.
Notes: Split into two.

## Slide 5: IEEE 802 and Smart Grid
IEEE 802 networking technologies bring the following advantages to Smart Grid communications:
  Enterprise grade security compatibility
  Huge ecosystem (billions of products, hundreds of manufacturers)
  Long-term (20 year), battery-powered operation
  Continued operation during line fault events when using wireless media
  Wide choice of products across the spectrum of power versus performance
  Ability to be implemented in resource-constrained devices
  Ongoing development of standards to address changing environment and technology
  Wireless standards that operate in a licensed and license-exempt spectrum
  Offers a rich set of data rate/range/latency tradeoffs
  Common upper layer interface to seamlessly integrate into existing IT systems

## Slide 6: The Smart Grid = Electric Grid + Intelligence
Notes: Clarify the meaning of “intelligence” with a new bullet
Remove or clean-up figure. Larger text.

## Slide 7: Key Standards for Integrated Grid Communications Networks
LAN
WAN
FAN
Devices
NAN
IEEE 802.3 IEEE 802.11
IEEE 802.3 1000BASE-X
IEEE 802.22 IEEE 802.16 IEEE 802.11 (Mesh Topology)
IEEE 802.15.4: (SUN, LECIM, TVWS) IEEE 802.11ah, 802.11af
IEEE 802.11 IEEE 802.15.4
Notes: PEV to “PHEV”
Fix background/master page
Merge FAN and NAN into FAN/NAN

## Slide 8: Examples of utility communications protocols
IPv6/IPv4
TCP
IEEE 802.15.4e MAC enhancements
IPv6 RPL
Web Services, EXI, SOAP,
RestFul,HTTPS/CoAP
802.1x / EAP-TLS & IEEE 802.11i based Access Control
Physical
Layer
IEEE 802.15.4g
2.4GHz, 915, 868MHz
DSSS, FSK, OFDM
IEEE 1901.2
NB-PLC
OFDM
IEEE 802.11
Wi-Fi
2.4, 5 GHz, Sub-GHz
IEEE 802.3
Ethernet
UTP, FO
2G, 3G, LTE
Cellular
IEEE 802.16
WiMAX
1.x - 3.x GHz
Data
Link
Layer
IEEE 802.15.4
including FHSS
IEEE 1901.2
802.15.4 frame
format
IEEE 802.11
Wi-Fi
IEEE 802.3
Ethernet
2G, 3G, LTE
Cellular
IEEE 802.16
WiMAX
6LoWPAN (RFC 6282)
IPv6 over Ethernet (RFC 2464)
IPv6 over PPP
(RFC 5072)
IP or Ethernet
Convergence SubL.
Network
Layer
Transport
Layer
Application
Layer
Addressing, Routing, Multicast, QoS, Security
Security (DTLS/TLS)
DNS, NTP, IPfix/Netflow, SSH
RADIUS, AAA, LDAP, SNMP,…
(RFC 6272 IP in Smart Grid)
Metering
IEC 61968 CIM, ANSI C12.22,
DLMS/COSEM,…
SCADA
IEC 61850, 60870
DNP3/IP, Modbus/TCP,…
LLC
M
A
C
Mgmt
IEEE 802.22
TV White Space
IEEE 802.22
WRAN
802.15.9 KMP
Notes: Remove UDP from TCP/UDP layer
Change IIEEE to IEEE.
Add 802.22
EXI/ HTTPS/ CoAP are not app layer themselves. Move App layer up and put these in below
Is EAP-TLS above IP? Move 2G/3G/Cellular out to right, and bypass 802.1x layer.
Split 6lowpan to show 802.15.9
Move Network Functionality bottom line at bottom of IP layer

## Slide 9: SG Network Architecture
High level example of an AMI system
Detailed View:
Notes: Put detailed diagram into a backup section – only used by those who are have the background.

## Slide 10
Something on cyber security and IEEE 802
Notes: References to FIPS, 2006 version, and later versions.
We would like to show how IEEE 802 fits into a comprehensive security architecture.
Generally 802 provides layer 2 authentication and encryption. Show key management interfaces and mechanisms. Cypher suites
NISTIR (Phil Beecher to provide this)
X – Y chart showing NISTIR requirements in rows, and 802 protocols in columns

## Slide 11
Example applications that take advantage of low power operation, (water, oil/gas, line sensors)
Example of “constrained” types of devices
Notes: Ben Rolfe will create this

## Slide 12
Comparison with PLC – advantage of operation even if power line is damaged
Notes: Jeritt Kent will provide

## Slide 13: Example of Mesh Network
http://upload.wikimedia.org/wikipedia/commons/c/c5/17_node_mesh_network.png
Notes: Look in L2R contributions.

## Slide 14: IEEE 802.11 standards hierarchy
IEEE
11ac
11ad
11ae
11af
11ah
802.11a through 802.11z: Completed
Higher rate in 5GHz band
11ai
11ak
Higher rate in 60GHz band
Prioritization of management frames
TV White Space
915MHz Band operation (sub 1GHz)
Fast Initial Association
Pre-Association Discovery Task Group
11aj
China Millimeter Wave Task Group
Completed
Active: More Grid relevant
Active: Less Grid relevant
11aq
General Link (full bridging over WLAN) joint with 802.1
802.3
802.11
802.15
802.16
802.22
802.21
11ax
High Efficiency WLAN (HEW)

## Slide 15: 802.11 – Spectrum / Rate view
802.11ac
802.11n
1GHz
10GHz
500MHz
2GHz
5GHz
802.11g
802.11a
.11ah
.11af
.11y
10Mbps
100Mbps
.11ad
500Mbps
.11p
.11j
60GHz
802.11
802.11b
802.11n
1Mbps

## Slide 16: IEEE 802.15 standards hierarchy
802.15.10
Layer 2 Routing Task Group
IEEE
4r
4e
4g
4k
4m
4n
4q
Smart Utility Networks (WiSUN) AMI
LECIM
AMI for TV White Space
802.3
802.11
802.16
802.22
802.21
802.15
Key Management Protocol Task Group
Completed
Active – More Grid relevant
Active – Less Grid relevant
802.15.4
802.15.9
ZigBee

## Slide 17: 802.15.4 PHY Overview (data rate vs frequency)
1GHz
500MHz
2GHz
5GHz
10Kbps
100Kbps
1Mbps
BPSK DSSS
O-QPSK
O-QPSK, ASK
O-QPSK, ASK
BPSK DSSS
BPSK DSSS
868
915
920
CSS
GFSK
O-QPSK, ASK
780
863
4g O-QPSK
4g ODFM
4g ODFM
4g ODFM
4g O-QPSK
4g 2FSK
4g 2FSK
4g 4FSK
4g O-QPSK
4g 2FSK
4g ODFM
4g 2FSK
4g 4FSK
4g 2FSK
4g 2FSK
4g 4FSK
4g 2FSK
4g 2FSK
4g 4FSK
4g 2FSK
4g ODFM
O-QPSK CSS
MPSK

## Slide 18: IEEE 802.16 standards hierarchy
802.3
802.11
802.15
802.22
802.21
IEEE
Completed – Less Relevant
Completed – Grid Relevant
Active – Limited grid relevance
1a
1b
802.16.1
16n
16p
High Reliability
Machine to Machine
WiMAX
WiMAX 2
802.16-2012
802.16
16q
Small Cell Backhaul
16r
Multi-Tier Networks
Performance Metrics
802.16.3