## Slide 1: 802.24 Vertical Applications TAG
Cross-cutting vertical opportunity for EV Charging AFV* (EV and H2V) Fueling
Craig Rodine
Renewable and Distributed Systems Integration
Sandia National Laboratories Albuquerque, NM, USA
Nov 2022 IEEE 802 Plenary Session
Bangkok, Thailand (and remote)
* Alternative Fuel Vehicle
Sandia National Laboratories is a multimission laboratory managed and operated by National Technology & Engineering Solutions of Sandia, LLC, a wholly owned subsidiary of Honeywell International Inc., for the U.S. Department of Energy’s National Nuclear Security Administration under contract DE-NA0003525.

## Slide 2: Agenda
Summary of 24-22-0016-01-0000 (Sept 2022)
  Summary of the opportunities for IEEE 802
  Example w/less use cases for EV charging (one new)
A brief look at Hydrogen Surface Vehicle fueling
Preview: discussion with 802.1 TSN (Thu 11/17 AM2)
Discussion and next steps

## Slide 3: Opportunity for IEEE 802 vertical application
Explore a ‘Secure L2 EV charging comms fabric’
  Develop LAN architecture/s supporting site-level (depot, public fuleing) operations
  Towards a secure, cohesive, extensible ‘EV charging AFV fueling edge’
  Draw on existing and coming 802.1/.3/.11 standards
Explore how 802 services for e.g. TSN, location, and privacy could enhance site operations and systems integration
Example next-generation (esp. fleet) EV charging uses cases
  Use Wi-Fi for transactions, robotics, AV control
  Use SPE for control and management of high-power EV charging, integrating building/site DERs and the electrical utility edge
  Use VLANs to provide security and QOS for high-data-volume EV/AV applications, e.g. GIS data, route and schedule optimization, media services, trusted vehicle ECU/DCU FW/SW updates

## Slide 4: Concrete, near-term example #1 (new)
Use Wi-Fi® for large-scale EV (AC) charging
800 parking spots, 400 AC charging stations (6.6 kW)
Medium/long dwell (4-10 hour) charging
Obvious opportunities
  Replace PLC (L1/L2)
  Managed charging
  Data (logistics & tracking)
  EV (ECU) maintenance

## Slide 5: Concrete, near-term example #2 (expanded)
Use Wi-Fi for “over-the-top” transaction services
EV joins site Wi-Fi network, negotiates fueling service parameters
On-site edge (+cloud) services platform directs AFV to fueling bay
Coupling to fueling device could be robotic, controlled via Wi-Fi
Fueling control could be via Wi-Fi as well

## Slide 6: A brief look at H2 (HSV) fueling
Current system uses IrDA standards for one-way communication
  SAE J2799/J2600/J2601
  Vehicle sends fixed fueling parameters (V, T, p)
  Dispenser performs accordingly (“parameter-driven”)
  Overly large margins for physical and functional safety
  Doesn’t support higher fill rates, tank temp ranges
  IrDA not very reliable (sunlight, fogging); easily damaged
Opening for standards-based w/less comms
  2-way: tank characteristics; pre-cooling; dynamic control
  Needed for higher-speed fueling (larger tank HSVs)
  EU Project Prhyde -> ISO 19885-2/-3 (TC 297)
  Contemplating transactional services (e.g. payment, loyalty points) and fleet management (fueling logs, maintenance)
  Developing requirements for trust and security (PKI)
  Interested in using Secure Layer 2 (802.1/802.11)

## Slide 7: Preview: discussion with 802.1 TSN (Thu 11/17 AM2)
How could 802.1 and 802.3 standards support AFV fueling?
  Convergence/concentration of energy & data for transportation
  Support for fueling, power/energy distribution, logistics, operations
  Sites/locale: depots, ‘truck stops’, public transport hubs (LAN/MAN)
Architecture
  Distributed energy, computing, control
  Coordinated security contexts
    Fueling: vehicle, dispenser, energy sources and sinks; safety-critical?
    Data: public/private, site/region, cooperating entities; trust domains
  Orchestration of workloads between edge/cloud
Applications:
  SPE in EV charging cables/couplers, for sensors (situational awareness)
  Power system controls (e.g. protection, UPS, load management)
  Data services (Internet/media, goods tracking, mobility services)
Inspiration: Nendica Reports (Flex Factory IOT, Intelligent LDCN)

## Slide 8: Discussion, next steps
Thank you very much!
c.rodine@ieee.org
crrodin@sandia.gov