## Slide 1
  OmniRAN Specification – Structuring the effort
Document Number:
  Omniran-13-0004-00-0000
Date Submitted:
  2013-01-14
Source:
  Max Riegel E-mail: maximilian.riegel@nsn.com
  Nokia Siemens Networks
  *<http://standards.ieee.org/faqs/affiliationFAQ.html>
Re:
  -
Base Contribution:
  omniran-12-0002-02-ecsg-omniran-overview-and-status.pdf
Purpose:
  The presentation provides different proposals for structuring the specification effort for OmniRAN to get establish useful results early.
Notice:
  This document does not represent the agreed views of the IEEE 802 OmniRAN EC Study Group. It represents only the views of the participants listed in the “Source(s)” field above. It is offered as a basis for discussion. It is not binding on the contributor(s), who reserve(s) the right to add, amend or withdraw material contained herein.
Copyright Policy:
  The contributor is familiar with the IEEE-SA Copyright Policy <http://standards.ieee.org/IPR/copyrightpolicy.html>.
Patent Policy:
  The contributor is familiar with the IEEE-SA Patent Policy and Procedures:
      <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>.
  Further information is located at <http://standards.ieee.org/board/pat/pat-material.html> and <http://standards.ieee.org/board/pat >.

## Slide 2: OmniRAN Specification Structuring the efforts
Max Riegel
(NSN)

## Slide 3: Proposed Scope of OmniRAN
Network detection and selection
  Finding the most appropriate network when multiple networks are available
Setting up the access link
  Scope of individual IEEE 802.xx specifications
Authentication
  Framework, based on IEEE 802.1X
Setting up the e2e communication link
  Authorization, Service management
Management of user data connection
  mobility support to maintain connectivity
Usage and inventory reporting
  accounting, monitoring, location
Subscription management
  Adding new users to a network
  Maintaining subscriptions
Station management
  Initial configuration of new terminals
  Provisioning and update of policies

## Slide 4: OmniRAN Architecture Overview

## Slide 5: Proposed OmniRAN Interfaces
R1: Access link, technology specific
R2: User & terminal authentication, subscription & terminal management
R3: Authorization, service management, user data connection, accounting, monitoring
R4: Inter-access network coordination and cooperation, fast inter-technology handover
R5: Inter-operator roaming control interface

## Slide 6: OmniRAN Reference Point Structure
Reference points represent a set of protocols between peer entities
  Similar to a real IP network interface
Not all protocols of a reference point must always be implemented.
  However, if a particular protocol is present, it must conform to the specification
MS
Access
Network
Core
Network
Authentication
Authorization
Pag. & Loc
QoS Ctrl
DataPath
Mob Mgmt
Authentication
Authorization
Pag. & Loc
QoS Ctrl
Mob Mgmt
R3
DataPath
R1
HO
QoS
PKM
Pg/SM
Pg/SM
PKM
QoS
HO
Encaps
Encaps
Encaps

## Slide 7: Getting useful results early
Creating an complete OmniRAN specification may require too much effort to fit within a reasonable project
Limiting the efforts by leveraging existing solutions when feasible is desirable
  IETF protocols
  Wi-Fi Alliance solutions
  WiMAX specifications
  ZigBee specifications
Step-wise development of the specification might provide valuable results earlier
  Different approaches possible, see next slide

## Slide 8: Step-wise development approaches
Reference point by reference point
  e.g. starting with R1, R2, R3, adding R4 and R5 later
Function by function
  e.g. starting with authentication, setting up e2e communication link and usage and inventory reporting, adding mobility management, station management and subscription management later
Protocol by protocol
  e.g. starting with RADIUS, adding other protocols later
Phased mobility support
  e.g. starting with fixed, then nomadic and later mobile

## Slide 9: Conclusion
There is not the obvious solution for phasing the OmniRAN development effort
Different approaches possible, which can be combined to further lower the effort for the first release of the specification
Development in releases requires careful considerations on release management and means to maintain compatibility