## Slide 1: OmniRAN Introduction and Way Forward
2013-02-27
Max Riegel
(OmniRAN SG Chair)

## Slide 2: OmniRAN
OmniRAN is about attaching terminal devices deploying IEEE 802 technologies to communication networks.
OmniRAN defines interfaces and generic network functions for access networks based on IEEE 802 technologies
  including IEEE 802.3!
BTW: What does OmniRAN stand for?
  Open mobile network interface for omni-Range Area Networks

## Slide 3: Dynamic attachment of terminals to networks
Communication networks supporting dynamic attachment of terminals are usually structured into
  Access Network
    Distributed infrastructure for aggregation of multiple network access interfaces into a common interface
  Core Network
    Infrastructure for control and management of network access and end-to-end IP connectivity
  Services
    Infrastructure for providing services on top of established IP connectivity
Internet
Terminal
Access Network
Services
Core Network

## Slide 4: Functions for establishment of end-to-end IP Connectivity
Access Network
Network advertisement
IEEE 802.xx PHY and MAC
Authentication, authorization and accounting client
L2 session establishment
  w/ QoS and Policy Enforcement
L2 mobility management inside and across access networks
Local Mobility Anchor (LMA)
Traffic forwarding to core
Core Network
Authentication, authorization and accounting server
IP address management
Policy & QoS management based on a SLA
Mobility among multiple access networks (MAG)
IP connectivity establishment to Internet and services
Roaming via other core networks
Technical issues solved for legacy communication networks. Open issues might exist for heterogeneous networks and new domains of communication network deployments.

## Slide 5: Legacy Communication Networks
Close relationship between user terminal, access network and service provider
  Single interface in terminal
  Single access network topology
  Single operator
    single entity (operator, IT department) controls complete service chain
Operators with long-term experience in network operation.
Access
Core

## Slide 6: OmniRAN for Hetereogeneous Networks
User-Terminals have to support
  multiple network interfaces
    e.g. Cellular, IEEE 802.3, IEEE 802.11, …
  multiple access network topologies
    e.g. IEEE802.11 in residential, corporate and public
  multiple network subscriptions
    e.g. multiple subscriptions for same interface
Generic solution to cope with complexity
Cellular
802.11
802.15

## Slide 7: OmniRAN for Emerging Networking Markets
Many more (huge) networks are coming up by everything gets connected
  e.g. SmartGrid, HomeAutomation, Car, …
Many new markets for IEEE 802 access technologies
  e.g. factory automation, in-car communication
New deployments often suffering by the same old networking issues
  e.g. service control, security, provisioning
  new operators lacking long-term experience
Generic solution to foster market growth

## Slide 8: Functional Scope of OmniRAN
Network detection and selection
  Finding the most appropriate network access
Setting up the access link
  Scope of individual IEEE 802.xx specifications
Authentication
  Framework, based on IEEE 802.1X
Setting up the e2e communication link
  Authorization, service management
Maintaining the user data connection
  Mobility support to maintain connectivity when changing access points
Usage and inventory reporting
  Accounting, service monitoring, location
Subscription management
  Adding new users to a network and maintaining existing subscriptions
Management of terminals
  Initial configuration and provisioning and update of policies

## Slide 9: OmniRAN Architecture and Reference Points
Access
Core
Internet
R1
R3
R2
R4
Access
R3
Access
Core
Internet
R3
R5
Terminal
R3
Authentication
Authorization
Accounting
Location
CoA
Mobility
Encapsulation
Authentication
Authorization
Accounting
Location
CoA
Mobility
Encapsulation
DataPath
Access
Core
Transport
Reference Points represent a bundle of protocols between peer entities
  - Similar to real IP network interfaces

## Slide 10: OmniRAN Interfaces
R1: Access link, technology specific
R2: User & terminal authentication, subscription & terminal management
R3: Authorization, service management, user data connection, mobility support, accounting, location
R4: Inter-access network coordination and cooperation, fast inter-technology handover
R5: Inter-operator roaming control interface
All interfaces may comprise a number of different protocols. However, only the protocols related to required functionality have to be present on the interfaces.
  Approach allows for a common specification framework for various applications covering very simple to extremely complex network functionality.

## Slide 11: Heterogeneous Networking w/ OmniRAN

## Slide 12: What OmniRAN would provide to 3GPP
SaMOG is defining a gateway controlling the Trusted Non-3GPP access network by the EPC
OmniRAN would provide an interface (R3) to which 3GPP would be able to reference.
  Expanded beyond IEEE 802.11/802.16
R3

## Slide 13: No desire to re-invent the wheel… Limiting the effort to create beneficial results
There are plenty of specifications available which OmniRAN can leverage
  IETF protocols
  WiMAX specifications
  Wi-Fi Alliance solutions
  ZigBee specifications
  …
Step-wise development allows to provide valuable results early, e.g.:
  Interface by interface
    e.g. starting with R1 and R2, then R3, adding R4 and R5 later
  Functional complexity
    e.g. starting with simple nomadic scenario, adding dynamic service control, later L3 mobility management and inter-AN optimizations
  …
OmniRAN EC SG is searching for the single most wanted access network function to be specified for IEEE 802.

## Slide 14: Plan for the initial OmniRAN PAR
OmniRAN EC SG had its initial meeting in January 2013
  Good participation throughout the industry
  Call for contributions for use cases document issued.
Plan for creation of initial PAR proposal until July 2013:
  Creation of use cases document illustrating the most important deployments of OmniRAN
  Circulating the use cases document among stakeholders for comments and confirmation
  Deriving common functional requirements from the agreed use cases document
  Prioritization of the derived functional requirements
  Gap analysis to existing solutions starting from the most prior functional requirements
  Decision about topic to be addressed first based on scope, purpose, need and support of stakeholders
  Submission of PAR proposal to IEEE 802 EC

## Slide 15: Planned Timeline of OmniRAN EC SG
Initial meeting
Jan
Feb
Mar
Apr
May
Jun
Jul
F2F meeting
Conf Call
Draft Use cases document
Call for comments on Use cases document
Use cases contributions
Classification of functional requirements
Gap analysis to existing solutions
Finalization of PAR proposal
Decision about initial topic
Draft PAR proposal
Use cases document finalization
Prioritization of functional requirements
?
?
?
?

## Slide 16: Questions & Comments from IETF
Our Questions to the IETF:
Which IETF WGs are related to OmniRAN?
Can IETF add to the decision process to determine most urgent issue in IEEE 802 access networks?
Recommendations on the network specifications to leverage for OmniRAN?