## Slide 1
OmniRAN SaMOG Use Case |  |  | 
Date: 2013-03-16 |  |  | 
Authors: |  |  | 
Name | Affiliation | Phone | Email
Max Riegel | NSN | +49 173 293 8240 | maximilian.riegel@nsn.com
Notice: This document does not represent the agreed view of the OmniRAN EC SG. It represents only the views of the participants listed in the ‘Authors:’ field above. It is offered as a basis for discussion. It is not binding on the contributor, who reserve the right to add, amend or withdraw material contained herein. |  |  | 
Copyright policy: The contributor is familiar with the IEEE-SA Copyright Policy <http://standards.ieee.org/IPR/copyrightpolicy.html>. |  |  | 
Patent policy: The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. |  |  | 
Abstract
The presentation shows the applicability of OmniRAN for the specification work of 3GPP on WLAN access to EPC. It derives requirements for the reference points of the OmniRAN architecture out of the functional and architectural assumptions stated in the 3GPP SaMOG study TR 23.852 v1.4.1 (2013-02).

## Slide 2: 3GPP SaMOG Use Case
OmniRAN use case contribution
Max Riegel, NSN

## Slide 3: Deployment Domain: WLAN access to EPC
SaMOG is defining a gateway controlling the Trusted Non-3GPP access network by the EPC
OmniRAN would provide specified interfaces for a trusted IEEE 802 Network to which 3GPP would be able to reference.

## Slide 4: Use case description: Joe’s Thoughtful Cellular Provider
Joe is owner of a recent smartphone model with both cellular and Wi-Fi interfaces build in. He is not only an extensive user of web-based social applications, streaming video and his company’s VPN access but also uses his cellular provider’s special phone book application and mail service. The special services of the cellular provider are only available by direct access to the cellular network.
To enable best service quality with low subscription rates, Joe’s cellular provider has established Wi-Fi access either by own infrastructure or by sharing agreements with other operators in the area Joe is living. As both, access to the Internet as well as access to the provider’s own services are demanded, the provider deploys 3GPP’s model of WLAN access to the EPC and allows Joe to make seamlessly use of his cellular subscription for enjoying high speed Wi-Fi access especially indoors and in extremely crowded areas.

## Slide 5: WLAN access to EPC: Scenarios considered by 3GPP TR 23.852
Phase 1: Solutions without UE impact (R11)
  Support for non-seamless WLAN offload (NSWO) or single PDN connection selected by the network without IP address preservation
  Solution 1:
    S2a bearer creation and deletion based on L3 triggers from UE
    Sta, S2a reference points supported by Trusted WLAN Access Network
  Solution 2:
    S2a bearer creation and deletion based on EAP and AAA signaling
    Definition of a Trusted WLAN AAA Proxy (TWAP) and Trusted WLAN Access Gateway (TWAG) and reference points Ta, Tn. Tg, Tu and Tw for the Trusted Non-3GPP WLAN Access (see next slides)
  3GPP decided to base normative specification on Solution 2
Phase 2: Solutions with UE impact (R12)
  Support for multiple PDN connections selected by the UE together with non-seamless WLAN offload and IP address preservation when requested by UE
  10 different solution proposals currently under consideration by 3GPP

## Slide 6: More information on Solution 2 of Phase 1
Basic assumptions:
  Air interface between UE and access network according to IEEE 802.11
  Point-to-point connectivity behavior expected between UE and TWAG
  Mutual authentication between UE and EPC according to TS 33.403
  IPv4 and/or IPv6 support according to RFC791 (IPv4)/RFC2131 (DHCPv4) and/or RFC2460 (IPv6) /RFC4861 (ND) /RFC4862 (SLAAC)
Reference Model:
    Non-roaming reference model

## Slide 7: More information on Solution 2 of Phase 1
Trusted WLAN AAA Proxy
  Relaying and protocol conversion of the AAA information between the WLAN Access Network and the 3GPP AAA Server
  Establishing Binding of UE IMSI with UE MAC address on the WLAN Access Network into (IMSI, MAC) tuple via snooping on the AAA protocol carrying EAP-AKA exchange.
  Detecting L2 Attach out of EAP-Success message and signaling it to TWAG
  Detecting L2 Detach out of Accounting-Request STOP message and signaling it to TWAG
  signaling of UE L2 datapath/tunnel identifier (e.g. 802.1Q VLAN tag or MPLS label) towards TWAG
Trusted WLAN Access Gateway
  For IPv4:
    DHCP proxy/relay for IP address assigned by the PDN GW to UE.
  For IP version 6:
    Default IPv6 Router according to IETF RFC 4861
  L2 based data forwarding towards UE
  Packet forwarding between the UE MAC address and related GTP/PMIP tunnel

## Slide 8: Potential Specification Issues in TR 23.852 v1.4.1 for Solution 2 of Phase 1
Non-seamless WLAN offload (NSWO)
  Solution 2 of Phase 1 does not show direct connectivity to the Internet
    However Solution 1 of Phase 1 does!
  No information given about necessary functions in TWAG
Definition of Trusted WLAN Access Gateway
  TS 23.852 states that default router is located in TWAG
  Conflicts with the definition of L2 forwarding towards PDN-GW
Definition of TW reference point between UE and WLAN access
  As stated, authentication signaling is done between UE and 3GPP AAA server, not between UE and WLAN access network
  A reference point indicating the exchange of authentication between UE and 3GPP AAA server is missing.
Definition of Tu reference point between UE and TWAG
  As user data is transferred according to IEEE 802.11 between STA (UE) and AP in the WLAN access network, there is no end-to-end encapsulation between UE and TWAG.
  However forced forwarding in the WLAN access network may realize point-to-point behavior. Such behavior has to be explicitly specified, as it is not present in the IEEE 802.11 standard.

## Slide 9: OmniRAN Architecture Mapping
Reference Point mapping
  R1, R2, R3 of the OmniRAN architecture can be directly mapped to SaMOG reference points
Access
Core
R1
R3
Terminal
R2

## Slide 10: Requirements for OmniRAN derived from TR 23.852 v1.4.1
Functional requirements for R1:
  The Tw reference point connects the UE to the WLAN Access Network per IEEE 802.11 specifications. The definition of IEEE Physical and Medium Access Control layers protocols is out of the scope of 3GPP.
Functional requirements for R2:
  Parameters for authentication signaling between the 3GPP AAA Server and the UE
  Additional parameters potentially coming, e.g. handover indicator
Functional requirements for R3:
  Forwarding the authentication signaling between UE and 3GPP Network; As a side effect, allowing the Trusted WLAN AAA Proxy to detect L2 attach of the UE.
  Authorization (including the authorization information update) signaling between WLAN Access Network and 3GPP Network.
  Accounting per UE, e.g. for charging purposes; As a side effect, allowing the Trusted WLAN AAA Proxy to detect L2 detach of the UE.
  Keying data for the purpose of radio interface integrity protection and encryption;
  Information of WLAN Access Network of per-UE L2 encapsulation information to be used with the Trusted WLAN Access Gateway.
  Purging a user from the WLAN Access Network for immediate service termination.
  Per-UE user plane encapsulation between the WLAN Access Network and the Trusted WLAN Access Gateway.
  Mobility support ?

## Slide 11: Conclusion
The OmniRAN architecture fits well to the architectural models discussed for SaMOG in 3GPP
Functional requirements for R1, R2 and R3 can be derived from the specification work of 3GPP
Some ambiguities exist in the TR 23.852 regards definition of reference points and functionality of the TWAG, which should be clarified with 3GPP.