## Slide 1
Wi-Fi Hotspot Roaming Use Case |  |  | 
Date: 2013-05-15 |  |  | 
Authors: |  |  | 
Name | Affiliation | Phone | Email
Max Riegel | NSN | +49 173 293 8240 | maximilian.riegel@nsn.com
Notice: This document does not represent the agreed view of the OmniRAN EC SG. It represents only the views of the participants listed in the ‘Authors:’ field above. It is offered as a basis for discussion. It is not binding on the contributor, who reserve the right to add, amend or withdraw material contained herein. |  |  | 
Copyright policy: The contributor is familiar with the IEEE-SA Copyright Policy <http://standards.ieee.org/IPR/copyrightpolicy.html>. |  |  | 
Patent policy: The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. |  |  | 
Abstract
The presentation addresses the deployment of the OmniRAN architecture for the specification of open interfaces for roaming between Wi-Fi hotspot operators.
The possibility to get access to communication services in other service providers’ networks has been one of the main reasons for the overwhelming success of cellular communication and is considered as necessary function also for public Wi-Fi access networks.

## Slide 2: Wi-Fi Hotspot Roaming Use Case
OmniRAN use case contribution
Max Riegel, NSN

## Slide 3: Deployment Domain
Wi-Fi Hotspot Roaming Use Case

## Slide 4: Deployment Domain: Wi-Fi Roaming
Roaming is a well know functionality in cellular networks allowing us to use our cellular phones worldwide without hassle.
Roaming among Wi-Fi hotspots belonging to different operators is seen a prerequisite to further develop Wi-Fi access service to a cellular like experience
Wireless ISPs
AC
3GPP2
MNO
HLR
3GPP
MNO
Home
ISP
Roaming
Broker
Users

## Slide 5: USE Case description
Wi-Fi Hotspot Roaming Use Case

## Slide 6: Use case description: Joe’s Convenient Wi-Fi Service
Joe is a road worrier always keen to make best use of the time he has to spend for traveling and sitting around waiting for the next flight or ride. Therefore he has a subscription with a local Wi-Fi service provider which has best coverage throughout his home town due to a plethora of Wi-Fi APs installed in nearly every public place in town including the airport and public transport vehicles, which Joe frequently uses.
As Joe is regularly using Wi-Fi for making phone calls and participating in conference calls, he went for the premium subscription option providing him a prioritized traffic path over Wi-Fi to his VoIP provider.
Luckily his Wi-Fi provider is early adopter of the Hotspot 2.0 technology providing not only secured air links but also convenient service experience when moving around in his home town. Due to the many roaming contracts, which Joe’s local Wi-Fi operator has established some major Wi-Fi operator and huge Wi-Fi roaming consortia, Joe’s convenient Wi-Fi service does not break when he is out of town.
Usually his Wi-Fi devices just automatically connect to available Wi-Fi by making use of the enhanced network detection and selection features of Hotspot 2.0 and the credentials, he got from his Wi-Fi service provider, for automatic log-on. Even more, Joe enjoys the same high quality VoIP connectivity when he is roaming into the networks of the major Wi-Fi operators with direct contracts to his home Wi-Fi service provider.

## Slide 7: Wi-Fi Roaming Scenarios
The following roaming scenarios are considered:
Home operator has roaming agreement with other operator. Traffic is routed via other operator’s core into the Internet
Home operator has roaming agreement with other operator. Traffic is routed back to the home operator’s core network.
Home operator has Wi-Fi access sharing agreement with other operator allowing to serve customers like within the own access infrastructure
Home operator has agreement with roaming consortia which enables to use credentials for access to all other operators’ Wi-Fi access, which belong to the roaming consortia.

## Slide 8: Mapping to OmniRAN
Wi-Fi Hotspot Roaming Use Case

## Slide 9: Topology view on OmniRAN architecture and reference points
Access
Core
Internet
R1
R3
R4
Access
Core
Internet
R3
R5
Terminal
R3
Authentication
Authorization
Accounting
Location
CoA
Mobility
Encapsulation
Authentication
Authorization
Accounting
Location
CoA
Mobility
Encapsulation
DataPath
Access
Core
Transport
Reference Points represent a bundle of protocols between peer entities
  - Similar to real network interfaces
R2
Access
R3

## Slide 10: OmniRAN Architecture Mapping
Core
Internet
R1
R3
Terminal
R2
Access
Home Operator
Core
Internet
R3
R5
Access
Other Operator w/ own core
Access
Access Operator
R3

## Slide 11: 1. Home operator has roaming agreement with other operator. Traffic is routed via other operator’s core into the Internet
Core
Internet
R1
R3
Terminal
R2
Access
Home Operator
Core
Internet
R3
R5
Access
Other Operator w/ own core
R2
only control

## Slide 12: 2. Home operator has roaming agreement with other operator. Traffic is routed back to the home operator’s core network.
Core
Internet
R1
R3
Terminal
R2
Access
Home Operator
Core
Internet
R3
R5
Access
Other Operator w/ own core
R2

## Slide 13: 3. Home operator has Wi-Fi access sharing agreement with other operator allowing to serve customers like by the own access infrastructure
Core
Internet
R1
R3
Terminal
R2
Access
Home Operator
Access
Access Operator
R3

## Slide 14: 4. Home operator has agreement with roaming consortia which enables to use credentials for access to all other operators’ networks belong to the roaming consortia.
Core
Internet
R1
R3
Terminal
R2
Access
Home Operator
Core
Internet
R3
R5
Access
Other Operator w/ own core
Core
R5
Roaming Consortia

## Slide 15: Requirements for OmniRAN:
All different flavors of Wi-Fi roaming can be handled with just 2 Reference Points of the OmniRAN architecture:
  R3, when terminal is anchored in the home network
    Default router in the home network
  R5, when terminal is anchored in the visited network
    Default router in the visited network
A Roaming Consortium usually deploys R5 for inter-connection of all the involved operators only containing AAA attributes.

## Slide 16: GAPS To EXISTING IEEE 802 Functionality
Wi-Fi Hotspot Roaming Use Case

## Slide 17: Conclusion
R5 is mainly a AAA interface designed for inter-operator roaming.
R3 can be used when forced traffic forwarding into the home is required.
As only AAA attributes are in scope of IEEE 802 and link specific attributes on R5 are the same as on R3, there is hardly anything left for IEEE 802 to specify for R5.
The Wi-Fi Roaming use case seems not to add to the normative specification domain of OmniRAN.