## Slide 1
3GPP Trusted WLAN Access to EPC Use Case Analysis |  |  | 
Date: 2013-05-15 |  |  | 
Authors: |  |  | 
Name | Affiliation | Phone | Email
Max Riegel | NSN | +49 173 293 8240 | maximilian.riegel@nsn.com
Notice: This document does not represent the agreed view of the OmniRAN EC SG. It represents only the views of the participants listed in the ‘Authors:’ field above. It is offered as a basis for discussion. It is not binding on the contributor, who reserve the right to add, amend or withdraw material contained herein. |  |  | 
Copyright policy: The contributor is familiar with the IEEE-SA Copyright Policy <http://standards.ieee.org/IPR/copyrightpolicy.html>. |  |  | 
Patent policy: The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. |  |  | 
Abstract
This slideset presents the analysis of the 3GPP Trusted WLAN Access to EPC over S2a.
It comprises a generic definition of the use case accompanied with an illustrative description of an deployment example, an introduction into the specification contained in TS 23.402, a mapping and comparison to the OmniRAN architecture listing the functional requirements and the result of the gap analysis to existing IEEE technologies.
Reference: 3GPP TS 23.402 V11.6.0 (2013-03)

## Slide 2: 3GPP Trusted WLAN Access to EPC Use Case
Introduction, Architectural Comparison and Functional Requirements

## Slide 3: Deployment Domain
3GPP Trusted WLAN Access to EPC

## Slide 4: WLAN access to EPC over S2a
TS 23.402 is defining a gateway controlling the Trusted Non-3GPP access network by the EPC
OmniRAN can provide specifications for an IEEE 802 based access network to which 3GPP would be able to reference.

## Slide 5: USE Case description
3GPP Trusted WLAN Access to EPC

## Slide 6: DEPLOYMENT ILLUSTRATION Joe’s Thoughtful Cellular Provider
Joe is owner of a recent smartphone model with both cellular and Wi-Fi interfaces build in. He is not only an extensive user of web-based social applications, streaming video and his company’s VPN access but also uses his cellular provider’s special phone book application and mail service. The special services of the cellular provider are only available by direct access to the cellular network.
To enable best service quality with low subscription rates, Joe’s cellular provider has established Wi-Fi access by own infrastructure as well as by sharing agreements with other operators in the area Joe is living. As both, access to the Internet as well as access to the provider’s own services are provided over Wi-Fi, the provider deploys 3GPP’s model of WLAN access to the EPC. It allows Joe to make use of his cellular subscription for high speed Wi-Fi access to the Internet and his phone book application and mail service in the providers network.

## Slide 7: TS 23.402 V11.6.0 (2013-03) Solution without UE Impact
Support for non-seamless WLAN offload (NSWO) or single PDN connection selected by the network without IP address preservation
S2a bearer creation and deletion based on EAP and AAA signaling
Definition of a WLAN Access Network, a Trusted WLAN AAA Proxy (TWAP) and a Trusted WLAN Access Gateway (TWAG) providing the reference points SWw, Sta and S2a for the Trusted Non-3GPP WLAN Access
Reference Model:

## Slide 8: Functional Summary
Basic assumptions:
  Air interface between UE and access network according to IEEE 802.11
  Point-to-point connectivity behavior expected between UE and TWAG
  Mutual authentication between UE and EPC according to TS 33.403
  IPv4 and/or IPv6 support according to RFC791 (IPv4)/RFC2131 (DHCPv4) and/or RFC2460 (IPv6) /RFC4861 (ND) /RFC4862 (SLAAC)
Trusted WLAN AAA Proxy
  Relaying and protocol conversion of the AAA information between the WLAN Access Network and the 3GPP AAA Server
  Establishing Binding of UE IMSI with UE MAC address on the WLAN Access Network into (IMSI, MAC) tuple via snooping on the AAA protocol carrying EAP-AKA exchange.
  Detecting L2 Attach out of EAP-Success message and signaling it to TWAG
  Detecting L2 Detach out of Accounting-Request STOP message and signaling it to TWAG
  signaling of UE L2 datapath/tunnel identifier (e.g. 802.1Q VLAN tag or MPLS label) towards TWAG
Trusted WLAN Access Gateway
  For IPv4:
    DHCP proxy/relay for IP address assigned by the PDN GW to UE.
  For IP version 6:
    Default IPv6 Router according to IETF RFC 4861
  L2 based data forwarding towards UE
  Packet forwarding between the UE MAC address and related GTP/PMIP tunnel

## Slide 9: Mapping to OmniRAN
3GPP Trusted WLAN Access to EPC

## Slide 10: Reference Point mapping
Access
R1
R3
Terminal
R2
Core
R1 maps directly to the SWw reference point of 3GPP
R2 and R3 would provide specified interfaces for Trusted WLAN AAA Proxy and Trusted WLAN Access Gateway, which are not addressed by 3GPP by definition
3GPP does not provide details for direct Internet access.
Internet

## Slide 11: Functional Requirements
Functional requirements for R1:
  The Tw reference point connects the UE to the WLAN Access Network per IEEE 802.11 specifications. The definition of IEEE Physical and Medium Access Control layers protocols is out of the scope of 3GPP.
Functional requirements for R2:
  Parameters for authentication signaling between the 3GPP AAA Server and the UE
  Additional parameters potentially coming, e.g. handover indicator
Functional requirements for R3:
  Forwarding the authentication signaling between UE and 3GPP Network; As a side effect, allowing the Trusted WLAN AAA Proxy to detect L2 attach of the UE.
  Authorization (including the authorization information update) signaling between WLAN Access Network and 3GPP Network.
  Accounting per UE, e.g. for charging purposes; As a side effect, allowing the Trusted WLAN AAA Proxy to detect L2 detach of the UE.
  Keying data for the purpose of radio interface integrity protection and encryption;
  Information of WLAN Access Network of per-UE L2 encapsulation information to be used with the Trusted WLAN Access Gateway.
  Purging a user from the WLAN Access Network for immediate service termination.
  Per-UE user plane encapsulation between the WLAN Access Network and the Trusted WLAN Access Gateway.
  Mobility support ?

## Slide 12: GAPS To EXISTING IEEE 802 Functionality
3GPP Trusted WLAN Access to EPC

## Slide 13: IEEE 802 Bridged Networks
Setting up and maintaining a point-to-point link across a bridged infrastructure
  Initializing the point-to-point link under AAA based access control
  Maintaining the point-to-point link when STA roams to another AP
Link state signaling at the edge of the bridged infrastructure
  3GPP expects an trigger for setting up S2a context when link in IEEE 802 is established