## Slide 1
SDN-based OmniRAN Use Cases Summary |  |  | 
Date: 2013-05-16 |  |  | 
Authors: |  |  | 
Name | Affiliation | Phone | Email
Antonio de la Oliva | UC3M | +34 657079687 | aoliva@it.uc3m.es
Juan Carlos Zúñiga | InterDigital | +1 514 904 6300 | j.c.zuniga@ieee.org
Roger Marks | EthAirNet | +1 619 393 1913 | roger@EthAir.net
Notice: This document does not represent the agreed view of the OmniRAN EC SG. It represents only the views of the participants listed in the ‘Authors:’ field above. It is offered as a basis for discussion. It is not binding on the contributor, who reserve the right to add, amend or withdraw material contained herein. |  |  | 
Copyright policy: The contributor is familiar with the IEEE-SA Copyright Policy <http://standards.ieee.org/IPR/copyrightpolicy.html>. |  |  | 
Patent policy: The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. |  |  | 
Abstract
This presentation summarizes the description, derived requirements and gap analysis for the SDN-based Use Cases previously introduced in the OmniRAN 802 EC Study Group.

## Slide 2: SDN-based OmniRAN Use Cases Summary
OmniRAN use cases contribution
Antonio de la Oliva, UC3M
Juan Carlos Zuniga, InterDigital
Roger Marks, EthAirNet Associates

## Slide 3: Deployment Domain
SDN-based OmniRAN Use Cases

## Slide 4: OmniRAN Architecture
sdf
Terminal
Access 1
Access 3
Internet
Access
Access Network Operator
Core Operator
Core
Access 2

## Slide 5: OmniRAN Architecture with multiple Cores
sdf
Terminal
Access 1
Access 3
Internet
Access
Access Network Operator
Access 2
Core Operator A
Core
Core Operator B
Core
Core Operator C
Core

## Slide 6: USE Case description
SDN-based OmniRAN Use Case

## Slide 7: SDN-based OmniRAN Use Cases Scenario
Centrally controlled configuration, from Core to Terminal, of heterogeneous IEEE 802 links
Dynamic creation of data paths with dynamic reconfiguration and mapping to the terminal at flow granularity
Clean separation of data and control planes

## Slide 8: SDN-based OmniRAN Architecture
Terminal
Internet
Core
Operator A
Core Operators
Core
Operator B
Core
Operator C
Access Network Operator
Backhaul
SDN
Controller
Data path
Control path
Access 1
Access 3
Access 2
Access Abstraction
Access Abstraction
Access Abstraction
Multiple Cores sharing Access Network
Access Abstraction
Data and Control plane separation
Central control
Access Abstraction

## Slide 9: Mapping to OmniRAN
SDN-based OmniRAN Use Cases

## Slide 10: SDN-based OmniRAN Use Cases Reference Point Mappings
Terminal
Internet
Core Operators
Core
Operator C
Access Network Operator
Backhaul
SDN
Controller
Data path
Control path
Access 3
Access Abstraction
Access Abstraction
Access Abstraction
Multiple Cores sharing Access Network
Access Abstraction
Data and Control plane separation
Central control
R1
R3
R2
AAA
Core
Operator B
Core
Operator A
Access Abstraction
Access 1
Access 2
R4
R5
R5

## Slide 11: Functional Requirements
R1: Access link
  SDN-based configuration/interaction between infrastructure and Terminal
    Remote configuration/management mechanisms for 802 radio links, including terminal and access network side.
    SDN-based configuration of 802 links, including QoS, setup, teardown, packet classification
    User plane management of the multiple-interfaced Terminal (e.g. generic 802-based logical interface to present to L3)
R2: User & terminal authentication, subscription & terminal management
  Control path from Terminal to the corresponding Core operator
    Setting up control path between Terminal and AAA Proxy server
    Setting up control path between AAA Proxy server and AAA server of corresponding operator
    Identification and mapping of user’s traffic data paths/flows
    Dynamic modification of control path (e.g. SDN-based actions based on packet content)
    Per-user radio statistics for terminal management

## Slide 12: Functional Requirements
R3: User data connection, service management
  SDN controller configuring user data path (end-to-end forwarding) and mobility update, real-time flow-based counter monitoring, queue control, link connection control, heterogeneous access network control
    Southbound interface for configuration/management of heterogeneous 802 links in the backhaul
    Generalized data plane with common behavior for 802 technologies
    Provisioning of data paths across heterogeneous 802 links with QoS support
    Per-user counters for accounting
R4: Inter-access network coordination and cooperation, fast inter-technology handover
  SDN-based forwarding state updates across different access networks
    SDN-based reconfiguration of data path
R5: Inter-operator roaming control interface
  Inter-operator roaming outside access network
    Subscription information exchange between service operators

## Slide 13: GAPS To EXISTING IEEE 802 Functionality
SDN-based OmniRAN Use Cases

## Slide 14: Gaps to existing IEEE 802 technologies
Control of data forwarding plane, common to 802 technologies
  Southbound interface enabling the communication between the 802 technologies and the central controller (e.g. access abstraction)
  Clearly defined interfaces, SAPs and behaviors
  Ability to modify data path based on arbitrary but bounded selection parameters
    Packet classification mechanisms based on templates (á la OpenFlow)
    End-to-end packet flow and QoS
Radio configuration mechanism for access and backhaul links
  With defined metrics and reporting
Data plane management of the multiple-interface Terminal
  Notion of 802 logical interface facing L3
Generic 802 access authorization and attachment