## Slide 1
Proposed OmniRAN SDN Use Case for External Communication |  |  | 
Date: 2013-08-07 |  |  | 
Authors: |  |  | 
Name | Affiliation | Phone | Email
Roger Marks | EthAirNet | +1 619 393 1913 | roger@EthAir.net
Antonio de la Oliva | UC3M | +34 657079687 | aoliva@it.uc3m.es
Juan Carlos Zúñiga | InterDigital | +1514 904 6300 | j.c.zuniga@ieee.org
Notice: This document does not represent the agreed view of the OmniRAN EC SG. It represents only the views of the participants listed in the ‘Authors:’ field above. It is offered as a basis for discussion. It is not binding on the contributor, who reserve the right to add, amend or withdraw material contained herein. |  |  | 
Copyright policy: The contributor is familiar with the IEEE-SA Copyright Policy <http://standards.ieee.org/IPR/copyrightpolicy.html>. |  |  | 
Patent policy: The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. |  |  | 
Abstract
This presentation proposes a summary of an OmniRAN SDN use case suitable for communication to external organizations such as the Open Networking Foundation (ONF).

## Slide 2: IEEE 802 OmniRAN Study Group: SDN Use Case
OmniRAN Executive Committee Study Group (ECSG) of IEEE 802
2013-08-07

## Slide 3: OmniRAN Study Group: Overview
The IEEE 802 Executive Committee (EC) originally chartered the OmniRAN EC Study Group (ECSG) in November 2012
  Currently planning to conclude activities in November 2013
OmniRAN: Open Mobile Network Interface for omni-Range Access Networks
Moving to propose initiation of standardization activity by end of 2013

## Slide 4: Access Network Abstraction by OmniRAN
Scope of IEEE 802
Medium
Medium
Data Link
Physical
Network
Transport
Application
Data Link
Physical
Data Link
Physical
Data Link
Physical
Network
Transport
Application
Network
Network
Medium
Medium
Data Link
Physical
Data Link
Physical
Data Link
Physical
Data Link
Physical
OmniRAN provides a generic model of an access network based on IEEE 802 technologies
Access Network
Terminal
Ctrl
Service
Ctrl
Srv
R2
R1
R3
OmniRAN Network Reference Model
Access Network
Terminal

## Slide 5: OmniRAN allows for mapping of complex IEEE 802 network infrastructures
Access
Ctrl
Internet
R1
R3
R4
Access
Ctrl
Internet
R3
R5
Terminal
R3
Authentication
Authorization
Accounting
Location
CoA
Mobility
Encapsulation
Authentication
Authorization
Accounting
Location
CoA
Mobility
Encapsulation
DataPath
Access
Core
Transport
Reference Points represent a bundle of functions between peer entities
  Similar to real network interfaces
Functions are extensible but based on IEEE 802 specific attributes
R2
Access
R3

## Slide 6: OmniRAN EC SG Results: Topics for Standardization in IEEE 802
Discovered gaps in existing IEEE 802 technologies should be addressed by the related IEEE 802 WGs
Establishing a common approach of specifying ‘external’ control into IEEE 802 technologies would require:
  specifications of the control attributes for the individual IEEE 802 technologies by their working groups
    (mostly normative, in annex of related specifications to ensure consistency)
  a specification describing the ‘OmniRAN’ Network Reference Model and listing the DL and PHY control functions demanded for access networks and SDN
    (mostly informative)
  a specification on the usage of protocols for the transport of IEEE 802 attributes and the definition of IEEE 802 attributes for such protocols
    (mostly informative for IEEE 802, probably in cooperation with other SDOs)
The discussions in the July 2013 session addressed partially the progressing of the standardization topics mentioned above.

## Slide 7: SDN-based OmniRAN Use Case

## Slide 8: Deployment Domain
SDN-based OmniRAN Use Cases

## Slide 9: OmniRAN Architecture
sdf
Terminal
Access 1
Access 3
Internet
Access
Access Network Operator
Core Operator
Core
Access 2

## Slide 10: OmniRAN Architecture with multiple Cores
sdf
Terminal
Access 1
Access 3
Internet
Access
Access Network Operator
Access 2
Core Operator A
Core
Core Operator B
Core
Core Operator C
Core

## Slide 11: USE Case description
SDN-based OmniRAN Use Case

## Slide 12: SDN-based OmniRAN Use Cases Scenario
Centrally controlled configuration, from Core to Terminal, of heterogeneous IEEE 802 links
Dynamic creation of data paths with dynamic reconfiguration and mapping to the terminal at flow granularity
Clean separation of data and control planes

## Slide 13: SDN-based OmniRAN Architecture
Terminal
Internet
Core
Operator A
Core Operators
Core
Operator B
Core
Operator C
Access Network Operator
Backhaul
SDN
Controller
Data path
Control path
Access 1
Access 3
Access 2
Access Abstraction
Access Abstraction
Access Abstraction
Multiple Cores sharing Access Network
Access Abstraction
Data and Control plane separation
Central control
Access Abstraction

## Slide 14: Mapping to OmniRAN
SDN-based OmniRAN Use Cases

## Slide 15: SDN-based OmniRAN Use Cases Reference Point Mappings
Terminal
Internet
Core Network(s)
Core
Operator C
Access Network
Backhaul
SDN
Controller
Data path
Control path
Access 3
Access Abstraction
Access Abstraction
Multiple Cores sharing Access Network
Access Abstraction
Data and Control plane separation
Central control
R1
R3
R2
AAA
Core
Operator B
Core
Operator A
Access Abstraction
Access 1
Access 2
R4
R5
R5
Access Abstraction
Backhaul Abstraction

## Slide 16: Functional Requirements
R1: Access link
  SDN-based configuration/interaction between infrastructure and Terminal
    Remote configuration/management mechanisms for 802 radio links, including terminal and access network side.
    SDN-based configuration of 802 links, including QoS, setup, teardown, packet classification
    User plane management of the multiple-interfaced Terminal (e.g. generic 802-based logical interface to present to L3)
R2: User & terminal authentication, subscription & terminal management
  Control path from Terminal to the corresponding Core operator
    Setting up control path between Terminal and AAA Proxy server
    Setting up control path between AAA Proxy server and AAA server of corresponding operator
    Identification and mapping of user’s traffic data paths/flows
    Dynamic modification of control path (e.g. SDN-based actions based on packet content)
    Per-user radio statistics for terminal management

## Slide 17: Functional Requirements
R3: User data connection, service management
  SDN controller configuring user data path (end-to-end forwarding) and mobility update, real-time flow-based counter monitoring, queue control, link connection control, heterogeneous access network control
    Southbound interface for configuration/management of heterogeneous 802 links in the backhaul
    Generalized data plane with common behavior for 802 technologies
    Provisioning of data paths across heterogeneous 802 links with QoS support
    Per-user counters for accounting
R4: Inter-access network coordination and cooperation, fast inter-technology handover
  SDN-based forwarding state updates across different access networks
    SDN-based reconfiguration of data path
R5: Inter-operator roaming control interface
  Inter-operator roaming outside access network
    Subscription information exchange between service operators

## Slide 18: GAPS To EXISTING IEEE 802 Functionality
SDN-based OmniRAN Use Cases

## Slide 19: Gaps to existing IEEE 802 technologies
Control of data forwarding plane, common to 802 technologies
  Southbound interface enabling the communication between the 802 technologies and the central controller (e.g. access abstraction)
  Clearly defined interfaces, SAPs and behaviors
  Ability to modify data path based on arbitrary but bounded selection parameters
    Packet classification mechanisms based on templates (á la OpenFlow)
    End-to-end packet flow and QoS
Radio configuration mechanism for access and backhaul links
  With defined metrics and reporting
Data plane management of the multiple-interface Terminal
  Notion of 802 logical interface facing L3
Generic 802 access authorization and attachment

## Slide 20: OmniRAN ECSG Resources
Website: http://ieee802.org/OmniRANsg/
Document Archive: https://mentor.ieee.org/omniran/documents
Email reflector: ecsg-802-omniran@listserv.ieee.org
Email archive: http://ieee802.org/OmniRANsg/email/