## Slide 1
IEEE 802 Enhanced Network Detection and Selection |  |  | 
Date: 2013-08-26 |  |  | 
Authors: |  |  | 
Name | Affiliation | Phone | Email
Max Riegel | NSN | +49 173 293 8240 | maximilian.riegel@nsn.com
Notice: This document does not represent the agreed view of the OmniRAN EC SG. It represents only the views of the participants listed in the ‘Authors:’ field above. It is offered as a basis for discussion. It is not binding on the contributor, who reserve the right to add, amend or withdraw material contained herein. |  |  | 
Copyright policy: The contributor is familiar with the IEEE-SA Copyright Policy <http://standards.ieee.org/IPR/copyrightpolicy.html>. |  |  | 
Patent policy: The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. |  |  | 
Abstract
The presentation introduces enhanced requirements for IEEE 802 access network detection and selection aligned to recent work in IEEE 802.11 and Wi-Fi Alliance on public Wi-Fi access (Hotspot 2.0).
IEEE 802.11u introduced an Access Network Query Protocol (ANQP), which supports more comprehensive network selection functionalities and builds the base for the Hotspot 2.0 access procedures, which might be well suited for deployments of other IEEE 802 access technologies.

## Slide 2: IEEE 802 Enhanced Network Detection and Selection
(OmniRAN Gap Analysis)
Max Riegel
NSN

## Slide 3: ToC
The Access Network Selection Challenge
The IEEE 802.11 approach
  ANQP Usage by Hotspot 2.0
  E.g. ANQP Information Elements
  Upcoming Hotspot 2.0 Functionalities
ANQP would fit into any IEEE 802 technology
IEEE 802.1X-2010 Network Announcements
  Access Information per NID
Conclusion

## Slide 4: The Access Network Selection Challenge
Challenges in access network selection occur with
  Multiple different access networks
  Multiple subscriptions
  Specific service requirements
  No a-priori knowledge about offered services
Access Network
>1<
Access Network
>2<
SSP
A
SSP
B
SSP
C
Roaming
Broker
SSP = Subscription Service Provider

## Slide 5: The IEEE 802.11 Approach
A Wi-Fi terminal scans the air for finding the near-by access points
  Either by passive scanning (Beacon)
  or by active scanning (Probe Request & Probe Response)
Questions arising when discovering an access point:
The information in the beacon or probe response is often not sufficient to make the appropriate decision
IEEE802.11u defines a protocol allowing to query additional information about the Wi-Fi access before initiating the association and authentication
GAS (Generic Advertisement Service) provides a container for the ANQP (Access Network Query Protocol), which provides more information about the Wi-Fi access
Is this my Home Service Provider?
Is this a Visited Service Provider?
Will this Service Provider support the service I am looking for?
Do I need any special provisioning for this Service Provider?
?

## Slide 6: ANQP Usage by Hotspot 2.0
Hotspot 2.0 capable AP Beacons and Probe Response
RSN IE(WPA2), Interworking Element (includes HESSID and Venue Information), Advertisement Protocol Element (Indicates ANQP), Roaming Consortium Element(A list of roaming consortium identifier), The Hotspot 2.0 Indication element
Hotspot 2.0 capable STAs scan for networks and discover an AP advertising Hotspot 2.0 capability.
Hotspot 2.0 capable STA uses ANQP to the AP to determine properties of the Hotspot 2.0 Access Network. The Hotspot capable STA selects the ANQP query elements it requires to query the Hotspot 2.0 network for Interworking Service information.
GAS Initial Request Frame( Advertisement Protocol = ANQP;
ANQP Query = {Venue Name, Network Auth, Roaming Consortium, IP Address Type, NAI Realm, 3GPP Cellular information, Domain Name; Operator Friendly Name, WAN Metrics, Connection Capability}
GAS Initial Response Frame( Advertisement Protocol = ANQP;
(Venue Name; Network Auth; Roaming Consortium; IP Address Type; NAI Realm; 3GPP Cellular information; Domain Name; Operator Friendly Name,; WAN Metrics; Connection Capability)
Hotspot 2.0 capable STA evaluates the response based on its Hotspot 2.0 subscription information and associated policy and choose to associate to the AP.
Associate and WPA2 EAP Authentication
Secure WPA2 Data Connectivity

## Slide 7: E.g. ANQP Information Elements
IEEE 802.11 ANQP Information Elements
Venue Name
  Provides zero or more venue names associated with the BSS to support the user’s selection.
Network Authentication Type
  Provides a list of authentication types carrying additional information like support for online enrollment or redirection URL.
Roaming Consortium
  Provides a list of information about the Roaming Consortium and/or SSPs whose networks are accessible via this AP.
IP Address Type Availability
  Provides STA with the information about the availability of IP address version and type that could be allocated to the STA after successful association.
NAI Realm
  Provides a list of network access identifier (NAI) realms corresponding to SSPs or other entities whose networks or services are accessible via this AP; optionally amended by the list of EAP Method, which are supported by the SSPs.
3GPP Cellular Network
  Contains cellular information such as network advertisement information e.g., network codes and country codes to assist a 3GPP non-AP STA in selecting an AP to access 3GPP networks.
Domain Name
  Provides a list of one or more domain names of the entity operating the IEEE 802.11 access network.
Hotspot 2.0 ANQP Information Elements
HS Query list
  Provides a list of identifiers of HS 2.0 ANQP elements for which the requesting mobile device is querying in a HS ANQP Query.
HS Capability list
  Provides a list of information/ capabilities that has been configured on an AP. The HS Capability list element is returned in response to a GAS Query Request.
Operator Friendly Name
  Zero or more operator names operating the IEEE 802.11 AN.
WAN Metrics
  Information about the WAN link connecting a IEEE 802.11 AN and the Internet.
Connection Capability
  Provides connection status of the most commonly used communications protocols and ports.
NAI Home Realm Query
  Used by the STA to determine if the NAI realms for which it has security credentials are realms corresponding to SPs or other entities whose networks or services are accessible via this BSS
Operating Class Indication
  Provides information on the groups of channels in the frequency band(s) the Wi-Fi access network is using

## Slide 8: Upcoming Hotspot 2.0 Release 2 adds powerful functions for IEEE 802 access networks
Network Selection – ANQP
Network Selection – Priority selection of Wi-Fi Networks by SSID
Hotspot Security and Automatic Login – WPA2 Enterprise
Operator Policy
Online Sign-up
Release 1 Q3 2012
Release 2 Q1 2014
  Release 2 adds to Release 1:
  Provisioning
    Mainly provisioning of operator policies for automatic selection of preferred Wi-Fi access networks
    Management Object different to ANDSF
  Registration
    Procedure to establish ‘online’ a new subscription
    Mainly replacement of the legacy captive portal

## Slide 9: ANQP would fit into any IEEE 802 technology
Network Selection
Accounting
Disassociation
Host Configuration
Application
Policy Control
Application
Host Config Release
Accounting
Authentication
Authorization
Association
Scanning
AAA Policy
Configuration
DHCP
Application
ANQP
Access Technology
Control I/f
Access Network

## Slide 10: Network Announcements provided by IEEE 802.1X-2010
What network(s) or network service(s) are available
Is access to that network already available, or is authentication or secured connectivity required
What authentication and secure connectivity mechanisms are required or available
What credentials should be presented if EAP is to be used
What cached CAKs can be used with a reasonable chance of success
What level of access (authorization) is or may be provided

## Slide 11: Access Information per NID

## Slide 12: Conclusion
Network Announcements according to IEEE 802.1X-2010 provide basic information for network detection and selection
  However missing capabilities to serve more complex access network scenarios
IEEE 802.11u introduced by ANQP a query/response protocol to handle even very complex scenarios
  Supporting complex roaming scenarios with roaming brokers
  Allowing for pre-authentication service discovery
  Enabling powerful Hotspot 2.0 access procedures
It seems to be desirable to consider implementation of ANQP within other IEEE 802 access technologies, e.g. IEEE 802.3
  Potentially allowing to deploy enhanced Hotspot 2.0 procedures like provisioning or on-line sign-up also on wired Ethernet