## Slide 1: OmniRAN EC SG Nov 2013 Opening Report to IEEE 802.1
Chair:
Max Riegel (NSN)

## Slide 2: Outline
Jul ’13 EC conclusion on OmniRAN
What’s in the intended specification
PAR proposal and its creation
Outlook: organizational considerations

## Slide 3: Brief History of OmniRAN Gap Analysis
Defining a simplistic network reference model,
a couple of use cases were investigated:
  3GPP Trusted WLAN Access to EPC
    TS 23.402 V11.6.0 (2013-03)
  ZigBee SEP2 Smart Grid Use Case
    ZigBee docs-09-5449-33-0zse
  SDN-based OmniRAN Use Case
Initial investigations show missing functionalities in some IEEE 802 specifications regards the investigated use cases.
  Sharing of findings in progress with the related working group and investigations will continue directly together with working groups.
Main issue was, that it was less than obvious how the pieces of IEEE 802 are fitting together
  There is need for better documentation how IEEE 802 protocols work together to create access networks for particular deployments
Access
Ctrl
Internet
R1
R3
Terminal
R2

## Slide 4: Filling the gap in IEEE 802 Mapping IEEE 802 specifications to service requirements
Direct evaluation of IEEE 802 protocols out of service/deployment requirements is challenging.
A Stage 2 specification provides a mapping of protocols to a functional network model, which facilitates easier evaluation.
‘External’ requirements from the service/deployment perspective
Develop a logical/functional model for evaluation of those requirements;
Available IEEE 802 specifications of protocols and attributes.
?
?

## Slide 5: OmniRAN EC SG Status after Geneva Plenary Session
Motion in the EC closing meeting:
  Develop a PAR and 5C for an IEEE 802 Recommended Practice by Nov ‘13
    Potential title: ‘Network Reference Model and Functional Description of IEEE 802 based Access Networks’
      Similar to a ‘Stage 2’ specification
  Suggest the best home for the project.
  https://mentor.ieee.org/omniran/dcn/13/omniran-13-0057-00-ecsg-omniran-ec-closing-report.pptx
OmniRAN EC SG got extension for creation of PAR & 5C proposal (EC Motion passed by 13/0/1)
Tony Jeffree indicated that 802.1 could be a “host” for this effort.

## Slide 6: ‘Stage 2’ Definition by ITU-T I.130/Q.65
The Stage 2 defines
a functional model using functional entities,
the functional entity actions needed,
information flow or API calls between functional entities
recommendations for the allocation of functional entities to physical locations for a few examples.
The Stage 2 provides
a single functional specification which can be applied in a number of different physical realizations,
a precise definition of functional capabilities and their possible distribution in the network to support the required network capabilities,
a detailed description of what functions, information flows and API calls will be provided, but not how they are to be implemented,
requirements for protocol capabilities as input to Stage 3 of the method.
The output of Stage 2 is used by
protocol designers to specify the protocols between physical entities,
node designers to specify the functional requirements of the nodes,
network planners.

## Slide 7: Draft ToC of the proposed specification
Introduction and Scope
Abbreviations/Acronyms, Definitions, and Conventions
References
Identifiers
Tenets for IEEE 802 Access Network Systems
Network Reference Model
  Overview
  Reference Points
  Access Network to Core Internetworking Relationship
    Multiple deployment scenarios
Functional Design and Decomposition
  Network Discovery and Selection
  Authentication
  Link establishment
  QoS and policy control
  Link relocation
  Link teardown
  Accounting

## Slide 8: Reference Model for IEEE 802 Network with Reference Points
Access
Ctrl
Internet
R1
R3
R4
Access
Ctrl
Internet
R3
R5
Terminal
R3
Authentication
Authorization
Accounting
Location
CoA
Mobility
Encapsulation
Authentication
Authorization
Accounting
Location
CoA
Mobility
Encapsulation
DataPath
Access
Core
Transport
Reference Points represent a bundle of functions between peer entities
  Similar to real network interfaces
Functions are extensible but based on IEEE 802 specific attributes
R2
Access
R3

## Slide 9: IEEE 802 Access Network Functions
L2 Configuration
AAA Policy
DHCP
Application
ANQP
Access Technology
Control I/f
Access Network
Network Selection
Accounting
Disassociation
Host Configuration
Application
Policy Control
Application
Host Config Release
Accounting
Authentication
Authorization
Association
Scanning
Link Establishment
Link Relocation
Link Teardown

## Slide 10: Mapping of proposed Reference Points to IEEE 802 Architecture
Current scope of IEEE 802
Medium
Medium
Medium
Reference Points can be mapped onto the IEEE 802 Architecture Model
  R1 represents the PHY and MAC layer functions between terminal and base station/access point.
  R2 & R3 represents the control interface from a central control entity into the L1 & L2 network functions
R2 and R3 cover external control of IEEE 802 technologies
  IP based protocols may be used to carry control information between network elements and access network control
Data Link
Physical
Higher Layers
Data Link
Physical
Data Link
Physical
Data Link
Physical
Data Link
Physical
Data Link
Physical
Higher Layers Control
Higher Layers Control
Higher Layers
R3
R2 R3
R1

## Slide 11: OmniRAN EC SG Current Status and Objectives
OmniRAN EC SG submitted PAR proposal on ‘Recommended Practice for Network Reference Model and Functional Description of IEEE 802 Access Network’ on October 10th for consideration in the November plenary meeting
  https://mentor.ieee.org/omniran/dcn/13/omniran-13-0086-00-ecsg-proposed-par-and-5c.docx
  More information on the following slides
It is proposed to run the project within 802.1 WG
  No conclusion yet, how this would/should work within 802.1 WG
  Technical discussions took place between OmniRAN EC SG and 802.1 (Security TG) in the September interim
OmniRAN EC SG will review comments on PAR proposal and will submit final proposal for the EC closing plenary.
Organizational arrangements of running the project in 802.1 will be discussed during the week (and in the EC workshop on Saturday)

## Slide 12: OmniRAN EC SG Timeline
F2F meeting
Conf Call
Jan
Feb
Mar
Apr
May
Jun
Jul
Aug’7
Apr’11
May’2
Jun’20
Aug
Sep
Oct
Sep
Oct
‘4
‘17
‘27
‘4
‘10
Oct’11
Nov’11
Feb’28
Initial meeting
Use cases harmonization
Use cases contributions
Requirements within scope of IEEE 802
Gap analysis to existing solutions
Socializing of gap analysis
Refine scope of EC SG (crisp words)
Potential standardization topics for IEEE 802
Plan for PAR proposal submission until Oct’11
Create draft PAR proposal
Refine wording of draft PAR proposal
Finalize PAR proposal

## Slide 13: Draft PAR Proposal Network Reference Model and Functional Description of IEEE 802 Access Network
5.2 Scope:
This recommended practice specifies an access network utilizing technologies based on the family of IEEE 802 Standards. It provides a Network Reference Model, including entities and reference points along with behavioral and functional descriptions of communications among those entities.
5.4 Purpose:
This specification enables manufacturers and operators to more easily design and deploy access networks based on IEEE 802 technologies, guides the developers of extensions to the existing standards in support of a unified access network, and extends the applicability of IEEE 802 standards into new deployment domains by specifying the functions of the IEEE 802 technologies when deployed in access networks.

## Slide 14: Creation of the draft PAR proposal
The proposed PAR text was mainly drafted in the interim meeting in York on September 4th and refined by a series of conference calls from mid September to mid October with varying participation by a core team of about 9 people.
  The core team represented good interest of big network vendors and operators and was guided by several experienced IEEE standardization professionals.
The PAR proposal was finally approved by the OmniRAN EC SG in a conference call on October 10th with 6 participants, after a call for review comments was send out on October 4th to the OmniRAN EC SG mailing list with about 50 subscribers. The call for comments led to two final comments, which were unanimously resolved in the final call with the commenters being present in the call.

## Slide 15: Organizational Considerations
802.1 is an excellent home for the project due to its competence and central role
The project can’ t be completed by 802.1 alone but requires active contributions from each of the other 802 WGs
So far, the topic was driven mainly by members of the wireless WGs
Question: How to ensure that the engaged people are able/willing to continue?

## Slide 16: OmniRAN EC SG Plan Nov 2013 F2F
Meetings
  Tuesday, Nov 12th, 13:30 – 15:30
  Wednesday, Nov 13th, 08:00 – 10:00
  Wednesday, Nov 13th, 13:30 – 15:30
  Thursday, Nov 14th, 08:00 – 10:00
Meeting Room: Cockrell
Proposed Agenda:
  Call Meeting to Order
  Attendance recording, secretary
  Approval of minutes
  Reports
  Comment resolution and responses on PAR & 5C comments
  Presentation to closing EC meeting
  Conditional extension of OmniRAN EC SG
  Technical presentations on OmniRAN related matters
  AOB
  Adjourn

## Slide 17: OmniRAN ECSG Resources
Website: http://www.ieee802.org/OmniRANsg/
Document Archive on mentor: https://mentor.ieee.org/omniran/documents
Email reflector: ecsg-802-omniran@listserv.ieee.org
Email archive: http://grouper.ieee.org/groups/802/OmniRANsg/email/
Attendance: Paper list (normative) + IMAT
  IMAT mandatory for participants seeking attendence credits
  Reciprocal rights for most WGs