## Slide 1: IEEE 802 OmniRAN ECSG Results and Proposals
Scope of IEEE 802, gaps and proposed ways forward
2014-01-21

## Slide 2: ToC
Motivation
OmniRAN within the scope of IEEE 802
  Definition of IEEE 802 specific control attributes
Common Network Reference Model
Potential gaps to existing IEEE 802 standards
  Investigated use cases
    3GPP Trusted WLAN Access to EPC (3GPP SaMOG Rel 11)
    ZigBee Smart Energy Profile 2 (ZigBee SEP2)
    Software Defined Networking (SDN)
    Wi-Fi roaming
Necessary specification work within IEEE 802
Conclusion

## Slide 3: Motivation
IEEE 802 OmniRAN Results and Proposals

## Slide 4: There is Evidence to consider Commonalities of IEEE 802 Access Networks
More (huge) networks are coming up by everything gets connected
  e.g. SmartGrid, ITS, IoT, …
New markets for IEEE 802 access technologies
  e.g. factory automation, in-car communication, home automation, …
IEEE 802 access is becoming more heterogeneous
  multiple network interfaces
    e.g. IEEE 802.3, IEEE 802.11, IEEE 802.15…
  multiple access network topologies
    e.g. IEEE802.11 in residential, corporate and public
  multiple network subscriptions
    e.g. multiple subscriptions for same interface
New emerging techniques, like SDN and virtualization
802.16
802.11
802.15

## Slide 5: OmniRAN WITHIN The SCOPE of IEEE 802
IEEE 802 OmniRAN Results and Proposals

## Slide 6: Access Network Abstraction by OmniRAN
Scope of IEEE 802
Medium
Medium
Data Link
Physical
Network
Transport
Application
Data Link
Physical
Data Link
Physical
Data Link
Physical
Network
Transport
Application
Network
Network
Medium
Medium
Data Link
Physical
Data Link
Physical
Data Link
Physical
Data Link
Physical
OmniRAN provides a generic model of an access network based on IEEE 802 technologies
Access Network
Terminal
Ctrl
Service
Ctrl
R2
R1
R3
OmniRAN Network Reference Model
Access Network
Terminal

## Slide 7: Access networks are for dynamic attachment of terminals to networks
Communication networks supporting dynamic attachment of terminals are usually structured into
  Access Network
    Distributed infrastructure for aggregation of multiple network access interfaces into a common interface
  Control (Core)
    Infrastructure for control and management of network access and end-to-end IP connectivity
  Services
    Infrastructure for providing services over IP connectivity
Internet
Terminal
Access Network
Services
Control

## Slide 8: Functional decomposition of dynamic network access
Access Network
Network advertisement
Pre-association signaling
Authentication, authorization and accounting client
L2 session establishment
  w/ QoS and Policy Enforcement
L2 mobility management inside access networks
Traffic forwarding to core based on L2 addresses
Control (Core)
Subscription management
Terminal provisioning
Authentication, authorization and accounting server
IP address management
IP connectivity establishment to Internet and services
Policy & QoS management server (policy decision)
Mobility Anchor
Roaming support to other cores

## Slide 9: Access Network Control Plane Functions
Network Selection
Accounting
Disassociation
Host Configuration
Application
Policy Control
Application
Host Config Release
Accounting
Authentication
Authorization
Association
Scanning
AAA Policy
Configuration
DHCP
Application
ANQP
L2 Protocol
L2 Attributes
L3+ Protocol
L2 Attributes
L3+ Protocol
L3+ Attributes
Legend:
L2 Protocol
L3+ Attributes
Access Network

## Slide 10: IEEE 802 Access Network Functions
L2 Configuration
AAA Policy
DHCP
Application
ANQP
Access Technology
Control I/f
Access Network
Network Discovery Selection
Accounting
Disassociation
Host Configuration
Application
Policy Control
Application
Host Configuration Release
Accounting
Authentication Authorization
Association
Datapath Establishment
Datapath Relocation
Datapath Teardown
Out of scope

## Slide 11: Mapping of OmniRAN Reference Points to IEEE 802 Reference Model
Current scope of IEEE 802
Medium
Medium
Medium
Reference Points can be mapped onto the IEEE 802 Reference Model
  R1 represents the PHY and MAC layer functions between terminal and base station
    Completely covered by IEEE 802 specifications
  R2 represents the L2 control protocol functions between terminal and central entities for control and AAA.
  R3 represents the L1 & L2 control interface from a central control entity into the network elements
‘R2’ and ‘R3’ cover IEEE 802 specific attributes
  However IP based protocols are used to carry control information between network elements and access network control
  Effectively each of IEEE 802 network elements contains an IP communication stack on top of the IEEE 802 data path for the exchange of the control information.
Data Link
Physical
Higher Layers
Data Link
Physical
Data Link
Physical
Data Link
Physical
Data Link
Physical
Data Link
Physical
Higher Layers Control
Higher Layers Control
Higher Layers
R3
R2 R3
R1

## Slide 12: Handling IEEE 802 Attributes in IP Protocols
Current handling of IEEE 802 specific attributes for IP protocols:
  IEEE 802 has an established procedure for defining the MIBs of the own technologies
    Now completely in scope for IEEE 802
  Currently IEEE 802 does not deal with other IEEE 802 attribute definitions for IP protocols
    e.g. IEEE 802 specific AAA (RADIUS, DIAMETER) attributes are done by IETF with only some informal review by IEEE 802 WGs
Specification of IEEE 802 related attributes for IP protocols by IETF has cumbersome issues, e.g.:
  delayed availability (completion of RFC may last 2 years after completion of IEEE standard)
  RFC’s can’t cope with revisions and life cycle of IEEE standards
    new RFC required for each amendment and revision of IEEE 802 standard
    new RFC’s have different numbers
    RFCs stay forever, while IEEE 802 standards have limited lifecycle
IEEE 802 should take full responsibility for all its IEEE 802 specific attributes for IP protocols
  like done today for managed objects (MIBs)

## Slide 13: Common Network Reference Model
IEEE 802 OmniRAN Results and Proposals

## Slide 14: Make IEEE 802 technologies properly supporting important deployments
IEEE 802 technologies should fulfill the requirements of important deployments, e.g.:
  Telecommunication, Smart Grid, ITS, SDN, …
Two main questions have to addressed:
  Which IEEE 802 standards do contribute to the particular deployments?
  Do the IEEE 802 standards provide all required functions?
A common model is necessary to make IEEE 802 technologies assessable and comparable, e.g.
  a reference model to compare functionalities
  a reference architecture to show how the IEEE 802 standards are fitting together for particular deployments
OmniRAN defines a Network Reference Model which
  maps IEEE 802 technologies into a generic network architecture,
  allows functional evaluation of IEEE 802 access technologies.

## Slide 15: Reference Model for IEEE 802 Network with Reference Points
Access
Ctrl
Internet
R1
R3
R4
Access
Ctrl
Internet
R3
R5
Terminal
R3
Authentication
Authorization
Accounting
Location
CoA
Mobility
Encapsulation
Authentication
Authorization
Accounting
Location
CoA
Mobility
Encapsulation
Datapath
Access
Core
Transport
Reference Points represent a bundle of functions between peer entities
  Similar to real network interfaces
Functions are extensible but based on IEEE 802 specific attributes
R2
Access
R3

## Slide 16: OmniRAN explains IEEE 802 Standards for Smart Grid Communications
Access
Ctrl
Service
Ctrl
Ctrl
Access
Access
Access
Access
Access
Access
R5
R5
R4
R3
R3
R3
R3
R3
R3
R3

## Slide 17: OmniRAN for upcoming topics: IEEE 802 Deployment for ITS Communications
Mobile
Router
N
networking
&
Transport
Access
Technologies
...
M
a
n
a
g
e
m
e
n
t
S
e
c
u
r
i
t
y
Vehicle
Host
Facilities
N
etworking
&
Transport
Access
Technologies
...
M
a
n
a
g
e
m
e
n
t
S
e
c
u
r
i
t
y
Applications
Vehicle
Gateway
Facilities
N
networking
&
Transport
Access
Technologies
...
M
a
n
a
g
e
m
e
n
t
S
e
c
u
r
i
t
y
ECU
ECU
N
networking
&
Transport
Access
Technologies
...
M
a
n
a
g
e
m
e
n
t
Ethernet
S
e
c
u
r
i
t
y
IPv
6
Border
Router
Facilities
N
etworking
&
Transport
Access
Technologies
...
M
a
n
a
g
e
m
e
n
t
Ethernet
S
e
c
u
r
i
t
y
CAN bus
Facilities
N
etworking
&
Transport
Access
Technologies
...
M
a
n
a
g
e
m
e
n
t
S
e
c
u
r
i
t
y
Applications
Ethernet
Central
Host
Central
Gateway
Traffic Centre/Service Centre
N
etworking
&
Transport
Access
Technologies
...
M
a
n
a
g
e
m
e
n
t
Ethernet
S
e
c
u
r
i
t
y
IPv
6
Facilities
N
etworking
&
Transport
Access
Technologies
...
M
a
n
a
g
e
m
e
n
t
Ethernet
S
e
c
u
r
i
t
y
CAN bus
Facilities
N
etworking
&
Transport
Access
Technologies
...
M
a
n
a
g
e
m
e
n
t
S
e
c
u
r
i
t
y
Applications
Ethernet
Roadside
Host
N
etworking
&
Transport
Access
Technologies
...
M
a
n
a
g
e
m
e
n
t
5
.
9
GHz
S
e
c
u
r
i
t
y
Ethernet
Access
Router
Roadside
Gateway
Border
Router
Facilities
N
etworking
&
Transport
Access
Technologies
...
M
a
n
a
g
e
m
e
n
t
S
e
c
u
r
i
t
y
Applications
ITS: Intelligent Transportation System Reference: ISO 21217(2013) |  |  | 
Vehicle ITS Station | Roadside ITS Station | Central ITS Station | Personal ITS Station
Communication Network
Access
Service
Ctrl
Access
Access
R3
Terminal
Terminal
Access
Ctrl
R1
R2
R3
Terminal
Terminal
R1
R1
R1
R3
R3
5.9
SENS
Ctrl
Loop Detector
ITS Network Technology & Protocols Standards Mapping

## Slide 18: Potential gaps to existing IEEE 802 standards
IEEE 802 OmniRAN Results and Proposals

## Slide 19: Example use cases investigated for gap analysis
3GPP Trusted WLAN Access to EPC
  TS 23.402 V11.6.0 (2013-03)
ZigBee SEP2 Smart Grid Use Case
  ZigBee docs-09-5449-33-0zse
SDN-based OmniRAN Use Case
Wi-Fi Hotspot Roaming Use Case

## Slide 20: 3GPP Trusted WLAN Access to EPC TS 23.402 V11.6.0 (2013-03)
Support for non-seamless WLAN offload (NSWO) or single PDN connection selected by the network without IP address preservation
S2a bearer creation and deletion based on EAP and AAA signaling
  Emulating link state signaling of WLAN Access Network
Definition of a WLAN Access Network, a Trusted WLAN AAA Proxy (TWAP) and a Trusted WLAN Access Gateway (TWAG)
Requiring a point-to-point link between UE and TWAG across WLAN Access Network
Reference Model:

## Slide 21: 3GPP Trusted WLAN Access to EPC OmniRAN Reference Point mapping
Access
R1
R3
Terminal
R2
Core
R1 maps directly to the SWw reference point of 3GPP
R2 and R3 would provide specified interfaces for Trusted WLAN AAA Proxy and Trusted WLAN Access Gateway, which are not addressed by 3GPP by definition
3GPP does not provide details for direct Internet access.
Internet

## Slide 22: GAP#1: Support for point-to-point links in bridged networks
For security and operational reasons, real access networks require a point-to-point link between terminal and access router
The point-to-point link has to be maintained when the terminal is moving from one access point to another access point
  Mobility support; the link has to be re-located
IEEE 802.1 seems to miss support point-to-point links across a bridged infrastructure
  Real access networks deploy instead Ethernet over GRE over IP over Ethernet to emulate the desired point-to-point link behavior
  Required L2 behavior is realized by transport of L2 over L3
STA
Ctrl/Core
GW
AP/BS
PHY
PHY
PHY
PHY
PHY
PHY
DLL
DLL
DLL
DLL
DLL
DLL
IP
IP
Access Link Model – the networking theory
R1
R3
PHY
PHY
PHY
PHY
DLL
DLL
ETH
ETH
IP
IP
IP
GRE
GRE
ETH
ETH
Access Link Model – real world Ethernet
PHY
PHY
ETH
ETH
IP
PHY
PHY
DLL
DLL
PHY
PHY
ETH
ETH

## Slide 23: GAP#1: Required functionality in IEEE 802.1
Setting up and maintaining a point-to-point access link across a bridged infrastructure
  Initializing the point-to-point link under AAA based access control
  Maintaining the point-to-point link when STA roams to another AP
Link state signaling at the edge of the bridged infrastructure
  E.g.: 3GPP expects an trigger for setting up S2a context when point-to-point link in IEEE 802 is established
BTW: Provider Backbone Bridging (MAC in MAC) within the access network may be a solution
  unfortunately it is designed for provider backbones
  missing solution for dynamic VLAN assignment may be another issue

## Slide 24: ZigBee SEP2 Smart Grid Application SEP2 Communication Infrastructure
SEP2 defines a Smart Energy Profile Network by which a variety of devices can communicate with the Energy Services Interface
  Technical Requirements specified by ZigBee docs-09-5449-33-0zse
The network consists of
  Local access infrastructure (HAN) with
    Network Access Server
    Network Authentication Server
  Application Trust Center
  Energy Services Interface to energy provider
Local access infrastructure can be based on any technology enabling IP connectivity to the Application Trust Center and ESI.
HAN
Network Authentication Server
Application Trust Server
Network Access Server
ESI

## Slide 25: ZigBee SEP2 Smart Grid Application OmniRAN Reference Point Mapping
OmniRAN is applicable to the local access infrastructure providing IP connectivity to ESI and Application Trust Server
HAN represents the functions contained in Access and Core function blocks of OmniRAN
R3 allows for easy integration of different link layer technologies with common Network Authentication Server and Network Access Server
R2 provides access authentication for any link technology represented by R1
Core
R1
R3
Terminal
R2
Access
R3
Access
HAN
Network Authentication Server
Application Trust Server
Network Access Server
ESI

## Slide 26: GAP#2: Network-ID and service indication in wired Ethernet
ZigBee SEP2 requires support for network discovery and selection functions.
IEEE 802.3 explicitly mentioned as technology candidate does not provide network advertisement, network discovery and network selection functions like the IEEE 802 wireless interfaces.

## Slide 27: SDN-based OmniRAN Use Cases Scenario
Centrally controlled configuration, from Core to Terminal, of heterogeneous IEEE 802 links
Dynamic creation of data paths with dynamic reconfiguration and mapping to the terminal at flow granularity
Clean separation of data and control planes

## Slide 28: SDN-based OmniRAN Use Cases Reference Point Mappings
Terminal
Internet
Core Network(s)
Core
Operator C
Access Network
Backhaul
SDN
Controller
Data path
Control path
Access 3
Access Abstraction
Access Abstraction
Multiple Cores sharing Access Network
Access Abstraction
Data and Control plane separation
Central control
R1
R3
R2
AAA
Core
Operator B
Core
Operator A
Access Abstraction
Access 1
Access 2
R4
R5
R5
Access Abstraction
Backhaul Abstraction

## Slide 29: Functional Requirements
R1: Access link
  SDN-based configuration/interaction between infrastructure and Terminal
    Remote configuration/management mechanisms for 802 radio links, including terminal and access network side.
    SDN-based configuration of 802 links, including QoS, setup, teardown, packet classification
    User plane management of the multiple-interfaced Terminal (e.g. generic 802-based logical interface to present to L3)
R2: User & terminal authentication, subscription & terminal management
  Control path from Terminal to the corresponding Core operator
    Setting up control path between Terminal and AAA Proxy server
    Setting up control path between AAA Proxy server and AAA server of corresponding operator
    Identification and mapping of user’s traffic data paths/flows
    Dynamic modification of control path (e.g. SDN-based actions based on packet content)
    Per-user radio statistics for terminal management

## Slide 30: Functional Requirements, cont.
R3: User data connection, service management
  SDN controller configuring user data path (end-to-end forwarding) and mobility update, real-time flow-based counter monitoring, queue control, link connection control, heterogeneous access network control
    Southbound interface for configuration/management of heterogeneous 802 links in the backhaul
    Generalized data plane with common behavior for 802 technologies
    Provisioning of data paths across heterogeneous 802 links with QoS support
    Per-user counters for accounting
R4: Inter-access network coordination and cooperation, fast inter-technology handover
  SDN-based forwarding state updates across different access networks
    SDN-based reconfiguration of data path
R5: Inter-operator roaming control interface
  Inter-operator roaming outside access network
    Subscription information exchange between service operators

## Slide 31: GAP#3: Control Interfaces for SDN
Control of data forwarding plane, common to 802 technologies
  Southbound interface enabling the communication between the 802 technologies and the central controller (e.g. access abstraction)
  Clearly defined interfaces, SAPs and behaviors
  Ability to modify data path based on arbitrary but bounded selection parameters
    Packet classification mechanisms based on templates (á la OpenFlow)
    End-to-end packet flow and QoS
Radio configuration mechanism for access and backhaul links
  With defined metrics and reporting
Data plane management of the multiple-interface Terminal
  Notion of 802 logical interface facing L3
Generic 802 access authorization and attachment

## Slide 32: Wi-Fi Hotspot Roaming Use case
Roaming is a well know functionality in cellular networks allowing us to use our cellular phones worldwide without hassle.
Roaming among Wi-Fi hotspots belonging to different operators is seen a prerequisite to further develop Wi-Fi access service to a cellular like experience
Wireless ISPs
AC
3GPP2
MNO
HLR
3GPP
MNO
Home
ISP
Roaming
Broker
Users

## Slide 33: OmniRAN Architecture Mapping
Core
Internet
R1
R3
Terminal
R2
Access
Home Operator
Core
Internet
R3
R5
Access
Other Operator w/ own core
Access
Access Operator
R3

## Slide 34: 1. Home operator has roaming agreement with other operator. Traffic is routed via other operator’s core into the Internet
Core
Internet
R1
R3
Terminal
R2
Access
Home Operator
Core
Internet
R3
R5
Access
Other Operator w/ own core
R2
only control

## Slide 35: 2. Home operator has roaming agreement with other operator. Traffic is routed back to the home operator’s core network.
Core
Internet
R1
R3
Terminal
R2
Access
Home Operator
Core
Internet
R3
R5
Access
Other Operator w/ own core
R2

## Slide 36: 3. Home operator has Wi-Fi access sharing agreement with other operator allowing to serve customers like by the own access infrastructure
Core
Internet
R1
R3
Terminal
R2
Access
Home Operator
Access
Access Operator
R3

## Slide 37: 4. Home operator has agreement with roaming consortia which enables to use credentials for access to all other operators’ networks belong to the roaming consortia.
Core
Internet
R1
R3
Terminal
R2
Access
Home Operator
Core
Internet
R3
R5
Access
Other Operator w/ own core
Core
R5
Roaming Consortia

## Slide 38: Wi-Fi Hotspot Roaming Use case Impact on OmniRAN:
All different flavors of Wi-Fi roaming can be handled with just 2 Reference Points of the OmniRAN architecture:
  R3, when terminal is anchored in the home network
    Default router in the home network
  R5, when terminal is anchored in the visited network
    Default router in the visited network
A Roaming Consortium usually deploys R5 for inter-connection of all the involved operators only containing AAA attributes.
As only AAA attributes are in scope of IEEE 802 and link specific attributes on R5 are the same as on R3, there is hardly anything left for IEEE 802 to specify for R5.
The Wi-Fi Roaming use case seems not to add to the normative specification domain of OmniRAN.

## Slide 39: Necessary standardization work within IEEE 802
IEEE 802 OmniRAN Results and Proposals

## Slide 40: Topics for Standardization in IEEE 802
Establishing a common approach of specifying ‘external’ control into IEEE 802 technologies would require:
  a specification describing the Network Reference Model and listing the DL and PHY control functions required for access networks and SDN
    Addressed by the PAR developped by OmniRAN ECSG
  a specification on the usage of IP protocols for the transport of IEEE 802 attributes
    Topic for the joint IEEE 802 – IETF coordination group
  specifications of the control attributes for the individual IEEE 802 technologies by their working groups
    Should go into annex of related specifications to ensure consistency
Gaps within IEEE 802 technologies may be discovered but should be addressed by the related IEEE 802 WGs

## Slide 41: Tribute to ITU Network Protocol Specification in 3 Stages
For the specification of the Integrated Services Digital Network the ITU-T defined in its Rec. I.130 a sequential 3 stage process,.
This process is nowadays commonly used in most telecommunication network standardization activities.
Some IEEE 802 WGs have successfully followed this model.
Specify requirements from the user's perspective;
Develop a logical/functional model to meet those requirements;
Develop a detailed specification of the protocols and attributes.
More Information:
ETSI: Making Better Standards
  http://docbox.etsi.org/MTS/MTS/10-PromotionalMaterial/MBS-20111118/protocolStandards/stagedApproach.htm

## Slide 42: Filling the gap in IEEE 802 Mapping IEEE 802 specifications to service requirements
Direct evaluation of IEEE 802 protocols out of service/deployment requirements is challenging.
A Stage 2 specification provides a mapping of protocols to a functional network model, which facilitates easier evaluation.
‘External’ requirements from the service/deployment perspective
Develop a logical/functional model for evaluation of those requirements;
Available IEEE 802 specifications of protocols and attributes.
?
?

## Slide 43: Filling the gap in IEEE 802 Mapping IEEE 802 specifications to service requirements
Direct evaluation of IEEE 802 protocols out of service/deployment requirements is challenging.
A Stage 2 specification provides a mapping of protocols to a functional network model, which facilitates easier evaluation.
‘External’ requirements from the service/deployment perspective
Develop a logical/functional model for evaluation of those requirements;
Available IEEE 802 specifications of protocols and attributes.
?

## Slide 44: How does the 3 Stages Process relate to OmniRAN ECSG
Essentially OmniRAN ECSG proposes to develop a Stage 2 document for IEEE 802 network protocol specifications
  Actually re-engineering a Stage 2 to make it fitting to the existing IEEE 802 network protocol specifications (which represent Stage 3).
A Stage 2 specification makes it much more easy to evaluate and qualify ‘service’ requirements,
  and provide a common framework for further enhancements of IEEE 802 protocols

## Slide 45: ‘Stage 2’ Definition by ITU-T I.130/Q.65
The Stage 2 defines
a functional model using functional entities,
the functional entity actions needed,
information flow or API calls between functional entities
recommendations for the allocation of functional entities to physical locations for a few examples.
The Stage 2 provides
a single functional specification which can be applied in a number of different physical realizations,
a precise definition of functional capabilities and their possible distribution in the network to support the required network capabilities,
a detailed description of what functions, information flows and API calls will be provided, but not how they are to be implemented,
requirements for protocol capabilities as input to Stage 3 of the method.
The output of Stage 2 is used by
protocol designers to specify the protocols between physical entities,
node designers to specify the functional requirements of the nodes,
network planners.

## Slide 46: FYI: Usual ‘Stage 2’ Content
ITU-T Rec I.130
Derivation of a functional model
Information flow diagram
SDL diagrams for functional entities (optional)
Functional entity actions
Allocation of functional entities to physical locations
WiMAX Forum Stage 2 ToC
Introduction and Scope
Abbreviations, Definitions, and Conventions
References
Identifiers
Tenets
Network Reference Model
Functional Design and Decomposition
Reference:
http://resources.wimaxforum.org/sites/wimaxforum.org/files/technical_document/2010/12/WMF-T32-001-R016v01_Network-Stage2-Base.pdf

## Slide 47: Conclusion
IEEE 802 OmniRAN Results and Proposals

## Slide 48: P802.1CF Project Authorization Request
Project Title: Network Reference Model and Functional Description of IEEE 802 Access Network
Scope:
This Recommended Practice specifies an access network, which connects terminals to their access routers, utilizing technologies based on the family of IEEE 802 Standards by providing an access network reference model, including entities and reference points along with behavioral and functional descriptions of communications among those entities.
Purpose:
Heterogeneous networks may include multiple network interfaces, multiple network access technologies, and multiple network subscriptions. In some cases such heterogeneous functionality must be supported in a single user terminal.
This Recommended Practice supports the design and deployment of access networks based on IEEE 802 technologies, guides the developers of extensions to the existing standards in support of a heterogeneous access network, and enables the use of IEEE 802 standards in new network deployments by specifying the functions of the IEEE 802 technologies when deployed in access networks.

## Slide 49: Draft ToC of the proposed specification
Introduction and Scope
Abbreviations, Acronyms, Definitions, and Conventions
References
Identifiers
Tenets for IEEE 802 Access Network Systems
Network Reference Model
  Overview
  Reference Points
  Access Network Control Architecture
    Multiple deployment scenarios
Functional Design and Decomposition
  Network Discovery and Selection
  Association
  Authentication and Authorization
  Datapath establishment
  QoS and policy control
  Datapath relocation
  Datapath teardown
  Disassociation
  Accounting