## Slide 1
Network Detection and Selection |  |  | 
Date: 2014-02-25 |  |  | 
Authors: |  |  | 
Name | Affiliation | Phone | Email
Max Riegel | NSN | +49 173 293 8240 | maximilian.riegel@nsn.com
Notice: This document does not represent the agreed view of the OmniRAN EC SG. It represents only the views of the participants listed in the ‘Authors:’ field above. It is offered as a basis for discussion. It is not binding on the contributor, who reserve the right to add, amend or withdraw material contained herein. |  |  | 
Copyright policy: The contributor is familiar with the IEEE-SA Copyright Policy <http://standards.ieee.org/IPR/copyrightpolicy.html>. |  |  | 
Patent policy: The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. |  |  | 
Abstract
The presentation provides overview and introduction into the text contribution on Network Selection and Detection

## Slide 2: Network Detection and Selection Overview and Introduction
Max Riegel
(NSN)

## Slide 3: Topic
Network Detection and Selection denotes the process which allows a Station to learn about all accessible Access Networks and provides the means to the Station to attach to the most preferable Access Network Interface.

## Slide 4: OmniRAN Access Scenario
CORE
Internet
R1
R3
STA
R2
CORE
Internet
R3
R5
R3
AN
ANI
ANI
ANI
AN
ANI
ANI
ANI
AN
ANI
ANI
ANI
STA Station
AN Access Network
ANI Access Network Interface
CORE COntrol and Router Entitiy

## Slide 5: Mapping of OmniRAN Reference Points to IEEE 802 Reference Model
Current scope of IEEE 802
Medium
Medium
Medium
Reference Points can be mapped onto the IEEE 802 Reference Model
  R1 represents the PHY and MAC layer functions between terminal and base station
    Completely covered by IEEE 802 specifications
  R2 represents the L2 control protocol functions between terminal and central entities for control and AAA.
  R3 represents the L1 & L2 control interface from a central control entity into the network elements
‘R2’ and ‘R3’ cover IEEE 802 specific attributes
  However IP based protocols are used to carry control information between network elements and access network control
  Effectively each of IEEE 802 network elements contains an IP communication stack on top of the IEEE 802 data path for the exchange of the control information.
Data Link
Physical
Higher Layers
Data Link
Physical
Data Link
Physical
Data Link
Physical
Data Link
Physical
Data Link
Physical
Higher Layers Control
Higher Layers Control
Higher Layers
R3
R2 R3
R1

## Slide 6: Functional entities related to NDS
STA (Station) Terminal of a communication service
  STA is identified by a hardware identifier
    Usually a MAC address in IEEE 802
  May have single or multiple SUBSCRIPTIONs
    SUBSCRIPTION is a trust relationship with a CORE
      May be identified by username/shared secret, certificate or smartcard
      Comprises set of permissions (authorization) to make use of one or more Access Networks
        Access Networks may be attached to other COREs
          Usually denoted as ‘roaming’

## Slide 7: Functional entities related to NDS, cont.
AN (Access Network) Infrastructure providing IEEE 802 connectivity from STA to CORE
  Access Networks expose an AN_NAME, potentially amended by information about ownership, about relation to one or more COREs and about the kind of communication service provided.
    Multiple Access Networks may expose the same AN_NAME
    To support more complex deployment scenarios, the Access Network may provide a special protocol to query AN-related information (ANQP)
  Access Network comprises single or multiple Access Network Interfaces (ANIs)
    An ANI represents a single instance of Access Point (AP) or Base Station (BS)
  ANIs have unique identifiers
    In IEEE 802 usually a MAC address

## Slide 8: Functional entities related to NDS, cont.
CORE (COntrol and Routing Entity) Control entity for operation of Access Network comprising the access router(s) for forwarding user traffic
  A CORE is identified by a SP_NAME
    Often derived from or comprising a FQDN
  CORE is the instance establishing and maintaining SUBSCRIPTIONs
  A SP_NAME is an unique identifier
  A CORE may be implemented in a distributed manner to enable effective control of multiple Access Networks
    Supporting a single SUBSCRIPTION across all its attached Access Networks

## Slide 9: Network Detection Procedures A Station looking for attachment to a service performs:
Scanning the environment for all reachable Access Network Interfaces (ANIs)
  ‘point of attachments’
Grouping the ANIs according to their AN_NAME sorted by link quality
Amending each of the AN_NAME groups by the connected COREs represented by SP_NAMEs
  An AN_NAME may be associated with multiple SP_NAMEs
  Each of the SP_NAMEs may be associated with a cost function
Potentially collecting additional information:
  e.g. roaming relationship, ownership, offered service profiles, network capacity
  Potentially deploying ANQP to retrieve more detailed information

## Slide 10: Network Selection Procedures A Station looking for attachment to a service performs:
Removing all AN_NAME groups, which do not offer the desired service.
Removing all AN_NAME groups, for which no valid SUBSCRIPTION exists
  By filtering the entries according to the associated SP_NAMEs
Executing a filtering algorithm across the remaining AN_NAMEs to determine the AN_NAME offering the desired service by the most preferred SUBSCRIPTION
  Taking the cost function associated with each of the SP_NAMEs into account
Selection of the ANI of the determined AN_NAME Access Network providing the best link quality.
Initiation of the Access Network attachment procedure according to the particular IEEE 802 access technology.

## Slide 11: How to proceed?
The NDS procedures listed on the previous two slides describe the most comprehensive approach.
A-priori knowledge or decisions may lead to much shorter procedures, e.g.
  looking for just another ANI of the same AN_NAME access network
  attaching to a preconfigured ‘prioritized’ AN_NAME access network
A ‘Stage 2’ description should provide not only the most comprehensive procedure but also descriptions of ‘simplifications’
  Not all IEEE 802 technologies may support all scenarios
Is this presentation comprehensive also for more complex roaming scenarios?