## Slide 1
SDN-based OmniRAN Use Cases |  |  | 
Date: [2014-03-20] |  |  | 
Authors: |  |  | 
Name | Affiliation | Phone | Email
Antonio de la Oliva | UC3M | +34 657079687 | aoliva@it.uc3m.es
Juan Carlos Zúñiga | InterDigital | +1 514 904 6300 | j.c.zuniga@ieee.org
Paul Congdon | Tallac Networks | +1 916 765 4056 | paul.congdon@tallac.com
Notice: This document does not represent the agreed view of the OmniRAN EC SG. It represents only the views of the participants listed in the ‘Authors:’ field above. It is offered as a basis for discussion. It is not binding on the contributor, who reserve the right to add, amend or withdraw material contained herein. |  |  | 
Copyright policy: The contributor is familiar with the IEEE-SA Copyright Policy <http://standards.ieee.org/IPR/copyrightpolicy.html>. |  |  | 
Patent policy: The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. |  |  | 
Abstract
This presentation provides a summary of Use Cased derived from the ONF Wireless and Mobile WG Update presentation from January 2014, highlighting the ones that are relevant for IEEE 802.

## Slide 2: OmniRAN SDN Use Cases
Antonio de la Oliva (UC3M)
Juan Carlos Zúñiga (InterDigital)
Paul Congdon (Tallac Networks)

## Slide 3: Abstract
This presentation provides a summary of some possible use cases for SDN in 802 technologies
The objective is to trigger discussion and create inputs that can be used for an eventual OmniRAN SDN requirements and use cases document
It takes as starting point the presentation on ONF use cases:
    https://mentor.ieee.org/omniran/dcn/14/omniran-14-0009-00-0000-onf-wireless-and-mobile-wg-status-update.pptx

## Slide 4: SDN-based OmniRAN Network Reference Model
Terminal
Internet
Core Network(s)
Core
Operator C
Access Network
Backhaul
SDN
Controller
Data path
Control path
Access 3
Access Abstraction
Access Abstraction
Multiple Cores sharing Access Network
Access Abstraction
Data and Control plane separation
Central control
R1
R3
R2
Core
Operator B
Core
Operator A
Access Abstraction
Access 1
Access 2
R4
R5
R5
Access Abstraction
Backhaul Abstraction
AAA

## Slide 5: Use cases
Large Scale Access Management
Virtualization/sharing of access, backhaul/fronthaul and network supporting actions
Unified Access Control

## Slide 6: Large Scale Access Management
Management of 802-based heterogeneous access/backhaul/fronthaul networks
Data path control protocol interfaces to handle the setup of data flows paths
Control/management protocol interfaces to handle configuration of radio properties and MAC features
Abstraction layer to handle different link layer technologies

## Slide 7: Virtualization/sharing of access, backhaul/fronthaul and network supporting actions
Enable dynamic virtualization/sharing of the access, backhaul and fronthaul
Required actions in the network to differentiate the traffic associated to each virtual network
Single point of attachment running several dynamically created networks
QoS and isolated access/backhaul/fronthaul network instances

## Slide 8: Virtualization/sharing of access, backhaul/fronthaul and network supporting actions

## Slide 9: Unified Access Control
Enable the use of a single access control mechanism, allowing to:
  Perform access control or redirect to different network-specific instance access control (can be multiple of them)
  Configure network/access security and associate a data-path
    Enforce rich access/service policies across heterogeneous domains in a consistent way
  Push credentials to terminal and point of attachment (e.g., interface with 802.11r)
Interfaces to relay MAC-layer information to applications

## Slide 10: Unified Access Control

## Slide 11: Conclusion
  We believe the creation of a Use Cases document can be useful to understand the application of SDN principles on a future OmniRAN (802.1CF) Network Architecture