## Slide 1
OmniRAN R3 Considerations |  |  | 
Date: 2014-03-17 |  |  | 
Authors: |  |  | 
Name | Affiliation | Phone | Email
Max Riegel | NSN | +49 173 293 8240 | maximilian.riegel@nsn.com
Notice: This document does not represent the agreed view of the OmniRAN EC SG. It represents only the views of the participants listed in the ‘Authors:’ field above. It is offered as a basis for discussion. It is not binding on the contributor, who reserve the right to add, amend or withdraw material contained herein. |  |  | 
Copyright policy: The contributor is familiar with the IEEE-SA Copyright Policy <http://standards.ieee.org/IPR/copyrightpolicy.html>. |  |  | 
Patent policy: The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. |  |  | 
Abstract
The presentation provides further thoughts about R3 of the tentative Network Reference Model of the P802.1CF specification. Evidence to split up the user plane and control interface is provided by the initial results for the Network Discovery and Selection section.

## Slide 2: OmniRAN R3 Considerations
Max Riegel
(NSN)

## Slide 3: Reference Model for IEEE 802 Network with Reference Points
Access
Ctrl
Internet
R1
R3
R4
Access
Ctrl
Internet
R3
R5
Terminal
R3
Authentication
Authorization
Accounting
Location
CoA
Mobility
Encapsulation
Authentication
Authorization
Accounting
Location
CoA
Mobility
Encapsulation
Datapath
Access
Core
Transport
Reference Points represent a bundle of functions between peer entities
  Comprising control functions as well as the data path
Functions are extensible but based on IEEE 802 specific attributes
R2
Access
R3

## Slide 4: Control and Data of R3 may go different pathes
Scope of IEEE 802
Access Network
Medium
Medium
Medium
P802.1CF will define an abstraction of an access network based on IEEE 802 technologies
  The access network provides the link between a station (IP host) and the first hop router
The abstraction leads to very few generic interfaces for all kind of implementations
  R1 represents the PHY and MAC layer functions between terminal and base station, which are completely covered by the IEEE 802 specifications
  R2 represents a control interface between terminal and central control entity, e.g. for authentication
  R3 represents a control interface between the access network and a central control entity and the data path interface towards the first hop router, which is defined by the IEEE 802 Data Link SAP.
Data Link
Physical
Higher Layers
Data Link
Physical
Data Link
Physical
Data Link
Physical
Data Link
Physical
Data Link
Physical
Higher Layers Control I/f
Higher Layers Control I/f
Higher Layers
R1
STA
CORE

## Slide 5: Control is detached from the data path in the SDN model
SDN is based on the same architectural model as used by OmniRAN to describe the access infrastructure within the scope of IEEE 802
Effectively access networks enabling dynamic attachment of terminals to a communication infrastrucute have always been a kind of ‘software defined’ networks.
  ‘Software’ can just be considered as a synonym of the control protocols of the legacy access networks models.
Medium
Medium
Data Link
Physical
Data Link
Physical
Higher Layers Control I/f
Control Entity
CORE
Openflow Switch Specification v1.3.2

## Slide 6: R3 in the scope of NDS Functional Requirements
IEEE 802 network discovery and selection should support more complex scenarios:
  Multiple access technologies
  Multiple different access networks
  Multiple subscriptions
  Specific service requirements
  No a-priori knowledge about offered services
CORE
A
CORE
B
CORE
C
Access Network
>2<
Access Network
>3<
Access Network
>1<

## Slide 7: Network Discovery and Selection Functions
A process which allows a station to retrieve the list of all access network interfaces in reach by
  Passive scanning
  Active scanning
  Data base query
Retrieving supplementory information for each of the access network interfaces to learn about
  Identity of the access network
  Supported Subscriptions
  Supported Services
Some algorithm in the station, which processes all the retrieved information, for determination of the ‘best’ access network interface to connect to.

## Slide 8: NDS Roles and Identifiers
User
  One or more Subscriptions
    Subscription Identifier {NAI} + Subscription Name {String}
Terminal
  Station
    STA {EUI-48}
Access Network
  One or more Access Network Interfaces
    ANI {EUI-48}
  Access Network
    AN Identifier {EUI-48} + AN Name {String}
  Supported Subscription Services
  Supported User Services
  Access Network Capabilities
    Record of capabilities {t.b.d. (ANQP???}
CORE
  Subscription Service – ‘Termination point of AAA’
    SSP Identifier {FQDN} + SSP Name {String}
  User Service – ‘Termination point of IEEE 802 user plane’
    USP Identifier {???} + USP Name {String}
FFS: Is model sufficient for complex roaming scenarios? Split of CORE into SSP and USP (control- & user plane functions)?

## Slide 9: Conclusion
There is evidence that R3-Control should be separated from R3-Data
  SDN Model
  Protocol architecture
  NDS functional requirements
How to introduce the separation into the NRM?
  What would be appropriate for SDN?
  What are the entities and identifiers for the termination points of Control and Data?
  Should we introduce such separation also for other interfaces of the NRM?
    R4 ???
No final conclusion yet, however strong evidence.