## Slide 1
Logical Interface Overview |  |  | 
Date: [2014-03-20] |  |  | 
Authors: |  |  | 
Name | Affiliation | Phone | Email
Juan Carlos Zúñiga | InterDigital | +1 514 904 6300 | j.c.zuniga@ieee.org
Notice: This document does not represent the agreed view of the OmniRAN EC SG. It represents only the views of the participants listed in the ‘Authors:’ field above. It is offered as a basis for discussion. It is not binding on the contributor, who reserve the right to add, amend or withdraw material contained herein. |  |  | 
Copyright policy: The contributor is familiar with the IEEE-SA Copyright Policy <http://standards.ieee.org/IPR/copyrightpolicy.html>. |  |  | 
Patent policy: The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. |  |  | 
Abstract
This presentation provides a an overview of the Logical Interface definition and discussions that have taken place at the NETEXT working group in the IETF.
These discussions could be relevant to the latest developments in 802.1 OmniRAN and are presented for informational background purposes.

## Slide 2: Logical Interface Overview
Juan Carlos Zúñiga (InterDigital Labs)

## Slide 3: Logical Interface in IETF/NETEXT
The IETF NETEXT WG has discussed the concept of a logical interface to support multi-technology handovers and IP Flow mobility
These definitions are relevant to the latest discussions in 802.1 OmniRAN, especially with respect to handling multiple technologies
http://tools.ietf.org/html/draft-ietf-netext-logical-interface-support

## Slide 4: Logical Interface
Logical Interface
IP
TCP/UDP
L1
L2 (IF#1)
L2 (IF#2)
L2 (IF#n)
L1
L1
…
Session to IP address binding
IP to logical interface binding
Logical to physical interface binding

## Slide 5: Logical Interface Properties
The logical interface has a relation to a set of physical interfaces (sub-interfaces) on the host that it is abstracting. These sub-interfaces can be attached or detached from the Logical Interface at any time. The sub-interfaces attached to a Logical interface are not visible to the IP and upper layers.
The logical interface may be attached to multiple access technologies.
The Transmit/Receive functions of the logical interface are mapped to the Transmit/Receive services exposed by the sub- interfaces. This mapping is dynamic and any change is not visible to the upper layers of the IP stack.
The logical interface maintains IP flow information for each of its sub-interfaces. A conceptual data structure is maintained for this purpose. The host may populate this information based on tracking each of the sub-interface for the active flows.

## Slide 6: Some previous discussions/definitions
The Logical Interface may or may not use the same link layer identifier as the physical interfaces (i.e. some technologies might not allow changing the link layer ID, like 802.16)
The Logical Interface has the path awareness of an IPv4/IPv6 link through a sub-interface.
The logical Interface may manage heterogeneous links. As such, different MTUs may be announced on different links. The Logical Interface should be able to configure a common value (e.g., the minimum value observed by any link)
The Logical interface should transmit uplink packets on the same physical interface on which the downlink packet was received for the particular prefix/flow. This relationship should follow the policies configured by the network and can be dynamically reconfigured.

## Slide 7
The logical interface has a virtual link-layer identifier (VLL-ID), used to:
Used for the neighbor discovery operation
Used to configure the IP address for this logical interface when the SLAAC is applied
Stored in the BCE at the Local Mobility Anchor via the Link-layer Identifier Option of the PBU
Used as the source link-layer address for sending packets from this logical interface
Physical interface SHOULD be able to send packets with the VLL-ID as the source link-layer address and SHOULD be able to receive packets with the VLL-ID as the destination link-layer address
Some previous discussions/definitions
(cont.)

## Slide 8
The sub-interfaces of a logical interface can be bound to point-to-point links over any access technology. Shared media (e.g., IEEE 802.11) are supported as long as they provide a point-to-point link [rfc4861] as required by the Proxy Mobile IPv6 specification [RFC-5213]. The details of how a shared media provides a point to point link are link layer specific and/or operational matters that are out of scope of this document. For example IEEE 802.11 media can provide a point-to-point link Ex:, via the appropriate use of IEEE 802.1Q VLAN header where a distinct VLAN is configured between the MAG and each of the mobile node.
The logical interface appears as a shared-link to the applications, and adapts to the link model of the sub-interface for packet communication.
Some previous discussions/definitions
(cont.)