## Slide 1
VLANs in relation to P802.1CF NRM |  |  | 
Date: 2014-09-15 |  |  | 
Authors: |  |  | 
Name | Affiliation | Phone | Email
Max Riegel | Nokia Networks | +49 173 293 8240 | maximilian.riegel@nsn.com
Notice: This document does not represent the agreed view of the IEEE 802.1 OmniRAN TG. It represents only the views of the participants listed in the ‘Authors:’ field above. It is offered as a basis for discussion. It is not binding on the contributor, who reserve the right to add, amend or withdraw material contained herein. |  |  | 
Copyright policy: The contributor is familiar with the IEEE-SA Copyright Policy <http://standards.ieee.org/IPR/copyrightpolicy.html>. |  |  | 
Patent policy: The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. |  |  | 
Abstract
The presentation provides thoughts related to the consideration of VLANs in the context of the P802.1CF Network Reference Model

## Slide 2: VLANs in relation to P802.1CF NRM
Max Riegel
(Nokia Networks)

## Slide 3: P802.1CF in the big picture of the Internet
Internet/Web Applications
LINK
PHY
IP
TCP
HTTP
WWW
LINK
PHY
LINK
PHY
LINK
PHY
IP
TCP
HTTP
WWW
Peer
(Client)
Peer
(Server)
Internet
LINK
PHY
IP
LINK
PHY
IP
LINK
PHY
IP
LINK
PHY
IP
LINK
PHY
IP
LINK
PHY
IP
LINK
PHY
LINK
PHY
P802.1CF Domain
UE
Access Router

## Slide 4: Access Network Abstraction by OmniRAN
Scope of IEEE 802
Medium
Medium
Data Link
Physical
Network
Transport
Application
Data Link
Physical
Data Link
Physical
Data Link
Physical
Network
Transport
Application
Network
Network
Medium
Medium
Data Link
Physical
Data Link
Physical
Data Link
Physical
Data Link
Physical
OmniRAN provides a generic model of an access network based on IEEE 802 technologies
Access Network
Terminal
Core
Service
Core
R2
R1
R3
OmniRAN Network Reference Model
Access Network
Terminal

## Slide 5: Initial Proposal for Reference Model for P802.1CF with Reference Points
Access
Core
Internet
R1
R3
R4
Access
Core
Internet
R3
R5
Terminal
R3
Authentication
Authorization
Accounting
Location
CoA
Mobility
Encapsulation
Authentication
Authorization
Accounting
Location
CoA
Mobility
Encapsulation
Datapath
Access
Core
Transport
Reference Points represent a bundle of functions between peer entities
  Functions are extensible but based on IEEE 802 specific attributes
Discussions brought up evidence to split R3 into R3control and R3data
R2
Access
R3

## Slide 6: Scope of OmniRAN P802.1CF mapped to the IEEE 802 Reference Model
Scope of IEEE 802
Access Network
Medium
Medium
Medium
P802.1CF will define an abstraction of an access network based on IEEE 802 technologies
  The access network provides the link between a station (IP host) and the first hop router
The abstraction leads to very few generic interfaces for all kind of implementations
  R1 represents the PHY and MAC layer functions between terminal and base station, which are completely covered by the IEEE 802 specifications
  R2 represents a control interface between terminal and central control entity, e.g. for authentication
  R3 represents a control interface between the access network and a central control entity and the data path interface towards the first hop router, which is defined by the IEEE 802 Data Link SAP.
Data Link
Physical
Higher Layers
Data Link
Physical
Data Link
Physical
Data Link
Physical
Data Link
Physical
Data Link
Physical
Higher Layers Control I/f
Higher Layers Control I/f
Control Entity
R1
Terminal
CORE

## Slide 7: SDN-based OmniRAN Use Cases Reference Point Mappings
Terminal
Internet
Core Network(s)
Core
Operator C
Access Network
Backhaul
SDN
Controller
Data path
Control path
Access 3
Access Abstraction
Access Abstraction
Multiple Cores sharing Access Network
Access Abstraction
Data and Control plane separation
Central control
R1
R3
R2
AAA
Core
Operator B
Core
Operator A
Access Abstraction
Access 1
Access 2
R4
R5
R5
Access Abstraction
Backhaul Abstraction

## Slide 8: Virtual LANs
802.1Q provides the functionality to enable multiple independent LANs (Broadcast Domains) within the same infrastructure
  Making use of a VLAN Tag in each ETH frame to identify the membership to particular LANs
VLAN Tags can be stacked to allow for multiple operational domains
  Customer VLAN
  Service Provider VLAN
  Backbone Provider VLAN

## Slide 9: Ethernet Frame Formats
FCS
Data
DA
Length
TYPE
SA
0x8100
VID
PCP
FCS
Data
DA
Length
TYPE
SA
0x8100
VID
PCP
FCS
Data
DA
Length
TYPE
SA
0x88A8
S-VID
PCP
0x8100
VID
PCP
FCS
Data
DA
Length
TYPE
SA
0x88A8
S-VID
PCP
I-SID
PCP
B-DA
B-SA
Ethernet
‘802.1Q’
‘802.1ad’
‘802.1ah’
B-DA: Backbone Destination MAC Address
B-SA: Backbone Source MAC Address
I-SID: Backbone Service Instance Identifier
S-VID: Service Provider VLAN Identifier
DA: (Customer) Destination MAC Address
SA: (Customer) Source MAC Address
VID: (Customer) VLAN Identifier
PCP: Priority Code Point

## Slide 10: VLAN Deployment Example for Backhaul Provisioning
Core
Internet
R1
Terminal
Access
R1
Terminal
Access
R1
Terminal
Access
R1
Terminal
Access
Core
Internet
Core
Internet
Core
Internet
R3
R3
R3
R3
ETH Service Provider ##A##
ETH Service Provider ##B##
ETH Backbone Provider
ETH Service Provider ##A##
ETH Service Provider ##C##
Backhaul

## Slide 11: Potential NRM Refinements
Access
Access
Core
Internet
R1
R3d
Terminal
R2
R3c
Core
Internet
R1
R3d
Terminal
R2
R3c
Ctrl
R7
R7
Basic NRM
NRM with further details inside Access

## Slide 12: Conclusion
Backhaul is mostly represented by stacked VLANs
Exposing Backhaul in NRM can be done by further details inside Access
Integration of Backhaul into Access by SDN requires further thoughts about appropriate modeling and reference points.