## Slide 1: SDN & NFV
Author: Hesham ElBakoury; Yuanlong Jiang, Ruobin Zheng
Version: 1.0
omniran-14-0079-00-CF00

## Slide 2: AGENDA
SDN Architecture
  SDNv2 (SDN Fabric).
Network Function Virtualization (NFV)
  Architecture
  MANO
  Service Chaining
  Value Proposition
SDN & NFV combined together
  Value Proposition
  SDO
ETSI MANO & SDN Integration

## Slide 3
Software Defined Network

## Slide 4: Software Defined Network Architecture
*ONF White Paper: Software-Defined Networking: The New Norm for Networks
Network device uses openflow agent to communicate with openflow controller
SDN is an architectural concept that encompasses the programmability of multiple network layers -- including management, network services, control, forwarding and transport planes -- to optimize the use of network resources, promote interoperability across suppliers and network layers, increase network agility, unleash service innovation, accelerate service time-to-market, extract business intelligence and ultimately enable dynamic, service-driven virtual networks [Heavy Reading]
The goal of Software Defined network is to allow Applications to tailor network behavior to suit their needs.

## Slide 5: Centralized vs Distributed Control
Centralized Control
OpenFlow
Switch
OpenFlow
Switch
OpenFlow
Switch
Controller
Distributed Control
OpenFlow
Switch
OpenFlow
Switch
OpenFlow
Switch
Controller
Controller
Controller

## Slide 6: Orchestration of Distributed Control in SDN
OpenStack*
Orchestrator
Controller
Network Appliances
Media Gateways
BNG
Controller
EPC
C-RAN
Node
Node
Node
Node
Node
Top of Rack Switch
Node
Network Applications

## Slide 7: High Level Architecture with SDN Fabric
Network fabric is a collection of forwarding elements whose primary purpose is packet transport
Address Translation
  Translate edge addresses to fabric internal addresses (e.g. MPLS labels) and vice versa.
Encapsulation
  Encapsulate packets with another header that carries the fabric addresses.
This approach would require edge version of openflow and a core version of openflow.
  The Fabric and Edge are controlled by (logically) separate controllers.
  Edge provides more rich services such as security and mobility.
Edge Controller
Fabric Controller
Fabric
Ingress
(Ingress Switch)
Egress
(Edge Switch)
Src
Host
Dst
Host
Network Virtualization & VNF
Business Applications
SDN Fabric is Proposed by Martin Casado et al.
Management Applications
NBI

## Slide 8
Network Functions Virtualization

## Slide 9: Server Virtualization Is Unstoppable

## Slide 10: Network Functions Virtualization: Vision
Session Border
Controller
Classical Network Appliance Approach
BRAS
Firewall
DPI
CDN
Tester/QoE
monitor
WAN
Acceleration
Message
Router
Radio/Fixed Access
Network Nodes
Carrier Grade NAT
PE Router
SGSN/GGSN
Fragmented, purpose-built hardware.
Physical install per appliance per site.
Hardware development large barrier to entry for new vendors, constraining innovation & competition.
Network Functions Virtualization Approach
High volume Ethernet switches
High volume standard servers
High volume standard storage
Orchestrated,
automatic & remote install.
Competitive &
Innovative
Open Ecosystem
Independent
Software Vendors

## Slide 11: Distributed NFV (*)
(*) D-NFV is an idea that has been promoted by RAD.

## Slide 12: Network Function Virtualization Components

## Slide 13: CPE Virtualization
Open
Daylight
Subscriber Home
Cloud
Cable Modem
API
Open
Stack
Neutron
Mobile
PC
Tablet
Mobile
STB – Linear & DVR
PC
Tablet
Subscriber VM
provisioning
routing
firewall
Parental controls
Service Level Agreements
BW on Demand
SDN

## Slide 14: vCPE Value Proposition
Better service delivery (faster, cheaper, and easier)
  Less equipment to deploy on end-user’s premises, save on build out, power, cooling, wiring, and installation
  Faster service response
    Faster add, move, changes, deletes, and troubleshooting response.
  Simplifies Provisioning and service upgrades (e.g. faster Introduction of new Media services)
  Flexible Multiscreen support ; Unified UI on every screen
Policies tied to the user, not the device
  Same access, at home or on the road
Reduction of OPEX and CAPEX
  Eliminate the expensive STB costs.
  Less Call Center costs, Less Truck rolls
  Lower the costs to support multiple heterogeneous boxes
Significant OPEX/CAPEX reduction potential and flexible service innovation

## Slide 15: CCAP Virtualization
CM
PON
QAM D/S
DOCSIS U/S
EQAM
Access Interfaces
Routing
DOCSIS Encapsulation
IP Provisioning
Subscriber Mgmt
Encryption
Reporting/OSS
L2VPN
MPLS
Channel Prov.
Service Flow Mgmt
Rate Limiting
Scheduler
Packet Processing
Virtualization Candidates
CCAP Architecture

## Slide 16: NFV Value Proposition

## Slide 17: ETSI NFV ISG

## Slide 18: ETSI High-level NFV Framework
MANO

## Slide 19: MANO Functional Blocks
The NFV Orchestrator is the single point of access for all requests from the OSS/APP to simplify the interfacing.
The NFV Orchestrator handles lifecycles of Network Service and VNF Forwarding Graph.
The VNF Manager handles VNF lifecycle from an application point of view.
The NFV Orchestrator has the end-to-end view of the resources being allocated across Network Services and VNFs by VNF Managers: all requests for resource allocation transit through, or are verified and granted by the NFV Orchestrator
The Virtualised Infrastructure Manager (VIM) is responsible for controlling and managing the NFVI compute, storage and network resources, usually within one operator’s Infrastructure Domain.

## Slide 20: The NFV-MANO Architectural Framework with Reference Points GS NFV-MAN 001 V0.7.0 (2014-10)

## Slide 21: Service Chaining Requirements
Any order of Service Functions in a Service Chain must be possible;
Service function paths must be decoupled from their physical network connectivity
  That is, insertion/deletion of a service function or a change of Service Function Path does not necessitate a restructuring of the underlay network connectivity
A Service Function may be crossed by a Service Chain for multiple times
Processing of multiple subscriber service flows or Service Chains must be supported on a single Service Function.
Service Chaining should be flexible (more details in the next slide).
Service chaining should be bandwidth efficient

## Slide 22: Flexible Service Chaining

## Slide 23: Service Chaining Using Service Header

## Slide 24: Openflow-Based Service Chaining

## Slide 25: Service Chaining Use Cases for Cable

## Slide 26
Service composition & insertion
vCDN
vDPI
vLB
vFW
vADC
vDPI
vCDN
physical
switch
vSwitch
SDN
Controller
Programmable service chains
Policies determine the chain order: customized chains!
Service Chaining Examples
Notes: FB: on their Wedge switch: their requirements are on a 3-month cycle, hard to keep up with existing h/w. FB/Google/AMZN can afford to design their own h/w, but not everyone else can
Customized chains: can be app/user/network tailored

## Slide 27
SDN & NFV

## Slide 28
NFV
Abstraction of network functions from (dedicated) hardware
SDN
Abstraction of the control plane from the data plane

## Slide 29: SDN & NFV Progress
2012: NTT w NEC deploy 1st live SDN network
2013: Year of PoCs (Proof of Concept testing)
  Operators, vendors learn in the lab
2014: Vendors productize NFV/SDN software in operator Lab Trials and a few Field Trials
2015: Field trials move to commercial deployments
  Many operators deploy 1 or 2 use cases (contained domains)
2016: Wider spread commercial deployments
  Many operators deploy several use cases
2017: SDN and NFV are mainstream, but much left to do
29
© Infonetics Research 2013: “SDN and NFV Strategies: Global Service Provider Survey,” July, 2013

## Slide 30: SDN & NFV SDO
Open Networking Foundation
  Standardize openflow.
  Several working groups such as architecture and framework, extensibility, forwarding abstractions, wireless & mobility, Northbound Interfaces
ETSI NFV Industry Specification Group.
  Main SDO for NFV standardization
IETF has different WG that are working on SDN &NFV related standards activities
  PCE, FORces, SPRIN, PCE, I2RS, SFC.
IETF SDNRG provides a forum for researchers to investigate key and interesting problems in the Software-Defined Networking field.
Q.14 of Study Group 13 is developing generic SDN framework for telecom carriers
  SDN-related discussion in NGN groups of SG11 and SG 15/Q12
Huawei has significant contributions and plays leadership roles in these SDO

## Slide 31: SDO Applying SDN & NFV
OIF
  Transport SDN
BBF
  SDN Use Case for broadband access network
  Virtua Gateway
MEF (Metro Ethernet Forum)
  Define use cases (e.g. bandwidth on demand) that are applicable to Carrier Ethernet Services

## Slide 32: Status of Cablelabs Virtualization Projects
V-CCAP
  The 1st release of the V-CCAP TR will be issued end of October.
  Huawei is very active and ahead of the game compared with other vendors.
vBCPE
  Identify CPE functions that can be virtiualized to support EPL service
  Huawei is involved in developing the solution architecture which uses opendaylight SDN controller.
vHomeNet
  This new project is driven by Jeff (Cox).
  The scope of the project is still under discussion with MSO
  Vendors will get involved by January next year
  Don Clarke is leading the project.
  The project draws on the results of vBCPE project.

## Slide 33: SDN an NFV are Complementary Technologies
Neither is dependent on (or requires) the other; but functionality is complementary
NFV contributes virtualized infrastructure upon which SDN control plane software, L2 – L3 data plane software, or network services runs in.
Both use programmatic application interfaces (APIs) for (southbound) data plane control and (northbound) service provisioning.
Together enable orchestration, virtualization, and automation of network services

## Slide 34: Drivers SDN and NFV: $$ Service Agility, Flexibility, Automation
© Infonetics Research: SDN and NFV Strategies: Global Service Provider Survey, July, 2013. (53% of world telecom capex)
SDN
NFV
Create new network services
quickly
Optimize network configurations
in real-time
Simplify multi-vendor network provisioning
and management (reduce OPEX)
Create new virtual networks quickly
Create virtual networks across
multi-vendor gear
Use lower-cost routers
and switches
Scale services up or down quickly
Reduce capex through standard servers
Introduce new services quickly
Optimize network in real time
Multi-tenants on the same hardware
Reduce energy consumption through standard servers
100%
100%
0%

## Slide 35: NFV and SDN together can create greatest value
SDN can play a key role in the orchestration of the infrastructure (physical, virtual)
  Provisioning and configuration of VNFs
  Allocate and manage resources (e.g., bandwidth)
  VM mobility
  Automation & programmability
  Security & policy control
  Centralized network control. Unified control & management plane?
Service composition (NFV Forwarding Graphs)
  Directing traffic flows to VNFs
  Traffic flow characterization very important (especially for mobile, E2E scenarios)
Ad-hoc, on-demand, secure virtual tenant networks

## Slide 36: SDN & NFV Value Proposition
Lack of service agility and length of time to implement new services and / or changes to the network have negative impact on costs and revenue.
  Ability to quickly introduce new revenue generating services to customers
  Ability for customers to order and instantly receive new services
Lack of visibility and instrumentation impact ability to grow network and manage OPEX costs
Reduce OPEX via automation of network management functions and dynamic control of network resources. and instantly receive new service
Notes: We create innovations (with our members and vendors)
We do NOT create products, we occasionally provide services
The cable industries success comes from a leveraged R&D model
  CableLabs, members and vendors agree on standards, specifications
  Vendors build products based on the standards and specifications
  Members deploy those products that enable products and services
CableLabs’ charter has been to:
  Provide timely & evaluated information
  Fund R&D projects
  Facilitate transfer of relevant technology and best practices
  Promote interoperability
To better address the Innovation Gap and Innovation Delay, CableLabs charter has been expanded to include:
  Cultivate an innovation pipeline focused on future 5+ year planning horizon
  Take educated risks

## Slide 37: SDN+ NFV Value Proposition
Business Agility
Operational Simplicity
Monetization
Service Orchestration – Customized Delivery
  Automation / Accelerate Time to Revenue
NFV – Elastic Resource Capacity
  Reduce Total Costs Across All Services
SDN – Open and Programmable at All Layers
  Simplify / Reduce Complexity
Velocity
Scale

## Slide 38: Strategic Networking Paradigms
Creates competitive supply of innovative applications by third parties
NFV and SDN are highly complementary, they are mutually beneficial but not dependent on each other.
Software is common denominator
Creates abstractions to enable faster innovation
Software
Defined
Networking
Leads to agility, Reduces CAPEX, OPEX,
Network
Functions
Virtualisation
Open
Innovation

## Slide 39: MANO Network Controllers
The Network Controllers is an abstraction layer below the VIM for a given administrative domain.
When present, the controller provides intuitive programmatic interfaces for the VIM that enable the establishment of connectivity within the domain
An SDN controller could be a VNF or part of service orchestration (NFV’s MANO)
SDN Controller can be a Network Controller which provides control plane abstraction.

## Slide 40: SDN-Based NFV
Openflow is used to build
The network path between
Service functions
MANO

## Slide 41: ETSI Phase 2 New Work Item on SDN & NFV Integration
Software-Defined Networking (SDN) is mentioned in different ETSI NFV GSs (e.g. SWA001 Annex A). A number of POCs also combine NFV with SDN. This Work Item (WI) describes the usage of SDN within the context of the NFV architecture framework, including SDN Controller as a VNF, SDN Controller as a realization of the Infrastructure network controller, etc. , and specifies corresponding requirements to be fulfilled, e.g. by an SDN controller playing the role of network controller in the NFV architecture

## Slide 42
Thank you
www.huawei.com

## Slide 43: Virtual Network Functions Forwarding Graph