## Slide 1
Key Concepts of Data Path Design and Control |  |  | 
Date: 2015-01-12 |  |  | 
Authors: |  |  | 
Name | Affiliation | Phone | Email
Max Riegel | Nokia Networks | +49 173 293 8240 | maximilian.riegel@nsn.com
Notice: This document does not represent the agreed view of the IEEE 802.1 OmniRAN TG. It represents only the views of the participants listed in the ‘Authors:’ field above. It is offered as a basis for discussion. It is not binding on the contributor, who reserve the right to add, amend or withdraw material contained herein. |  |  | 
Copyright policy: The contributor is familiar with the IEEE-SA Copyright Policy <http://standards.ieee.org/IPR/copyrightpolicy.html>. |  |  | 
Patent policy: The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. |  |  | 
Abstract
The presentation provides a summary of the key concepts and facts for the specification of data path establishment, re-location and teardown. It is brought up to build concensus within OmniRAN TG on the topic to establish a foundation for creation of a text contribution to P802.1CF on data path design and control.

## Slide 2: Key Concepts of Data Path Design and Control
Max Riegel
(Nokia Networks)

## Slide 3: P802.1CF Draft ToC
Introduction and Scope
Abbreviations, Acronyms, Definitions, and Conventions
References
Identifiers
Network Reference Model
  Overview
  Reference Points
  Access Network Control Architecture
    Multiple deployment scenarios including backhaul
Functional Design and Decomposition
  Dynamic Spectrum Access
  Network Discovery and Selection
  Association and Disassociaiton
  Authentication and Trust Establishment
  Datapath establishment, relocation and teardown
  Authorization, QoS and policy control
  Accounting and monitoring
SDN Abstraction
  Terminal
  Access Network
Annex:
  Tenets (Informative)

## Slide 4: Data Path Chapter ToC
Introduction
Terminology
Roles and identifiers
Use cases
Functional requirements
Data path specific attributes
Data path basic functions
NA attributes mappings to IEEE 802 technologies
IEEE 802 backhaul solutions

## Slide 5: Introduction
Data path carries user payload between Terminal and Core Network Service
Desired solution is a fully bridged access network solution supporting various link behaviors
  point-to-point
  Shared
Data path is established when terminal connects to access network and can be modified on demand anytime during the terminal session.
TE
CNS
NA
PHY
PHY
PHY
PHY
PHY
PHY
DLL
DLL
DLL
DLL
DLL
DLL
IP
IP
PHY
PHY
DLL
DLL
BH

## Slide 6: Terminology
TE Terminal
AN Access Network
NA Node of Attachment
BH Backhaul
SS Subscription Service
CNS Core Network Service
CIS Coordination and Information Service

## Slide 7: Roles and Identifiers
Terminal
  Terminal Interface
    TE {EUI-48}
    R1-Interface ID
Access Network
    Access Network Identifier: ANID {EUI-48} + AN Name {String}
  Node of Attachment
    NA {EUI-48}
    R1-Interface ID
    R6d-Interface ID
    Supportive Information
  Backhaul
    BH-ID
    R6d-Interface ID
    R3d-Interface ID
    Supportive Information
Core Network Service
    CNS ID: CNS Identifier {???} + CNS Name {String}
    R3d-Interface ID
    Supportive Information
Subscription Service
  ‘AAA and policy control’
    SS Identifier {FQDN} + SSP Name {String}
    Supportive Information

## Slide 8: Roles and Identifiers Data path in the NRM
Terminal
R1
Coordination and Information Service
R2
R9c
R8c
AN Ctrl
TE Ctrl
Subscription
Service
Core Network Service
R3d
R3s
CNS Ctrl
R3c
NA
Backhaul
R6d
R6c
R7c
Access Network
Core Network

## Slide 9: Use cases
Shared wireless access network
  Point-to-point link behavior is required to
    Enforce all traffic passing through the CNS
    Isolate terminal communication in a shared infrastructure
  Mobility support is required in the bridged infrastructure
    Without impacting IP connectivity, i.e. IP session has to be maintained while moving
  Point-to-point link state signalling required towards CNS
CNS
A
CNS
B

## Slide 10: Use Cases Further Considerations
An access network may be shared by multiple CNSs
VLANs may be used to differentiate services
  E.g. setting up dedicated VLANs for data, guest and voice terminals
C-VIDs may be used as service differentiators in the access network.
Terminals being either end-stations or bridges eventually deploying (C-)VLAN with C-VLAN tag carrying up to terminals
Access network may be spotty and being spread across large areas
CNS
A
CNS
B

## Slide 11: Use Cases Backhaul composed of multiple segments
CNS
Internet
R1
Terminal
NA
R1
Terminal
NA
R1
Terminal
NA
R1
Terminal
NA
CNS
Internet
CNS
Internet
CNS
Internet
R3d
R3d
R3d
R3d
ETH Operator ##A##
ETH Operator ##B##
ETH Backbone
Operator
ETH Operator ##A##
ETH Operator ##C##
Backhaul provided by ETH Service Provider
R6d
R6d
R6d
R6d

## Slide 12: Use Cases Further backhaul characteristics
Transport of the user plane between NA and CNS
Consists of bridges and links between bridges
Mix of wired or wireless medium possible within a backhaul
Isolation of user plane from transport network through VLANs
  User plane is ‘tunneled’ through
  Backhaul does not modify payload
Multiple operational domains possible within backhaul
  Bridges and links may belong to multiple operators.
  However a single brigde device has a single owner

## Slide 13: Use Cases 3GPP Trusted WLAN Access to EPC TS 23.402
Support for non-seamless WLAN offload (NSWO) or single PDN connection into EPC
Definition of a
  WLAN Access Network,
  Trusted WLAN AAA Proxy
  Trusted WLAN Access Gateway
Requiring a point-to-point link between UE and Trusted WLAN Access Gateway across WLAN Access Network
Requiring also link state signaling of WLAN Access Network towards Trusted WLAN Access Gateway
Very similar requirements exist also in other access networks carrying Ethernet frames between terminal and access router
  E.g. WiMAX

## Slide 14: Functional requirements
Datapath SHOULD be configurable as either point-to-point or multipoint-to-multipoint or rooted-multipoint (point-to-multipoint) behavior
Successful completion of datapath establishment SHOULD be indicated.
Relocation of datapath within the access network SHOULD be supported.
Datapath should be configurable to support the transport of C-VIDs between terminal and CNS
Datapath should protect integrity of user payload
Datapath should support encrypted transport of user payload
Datapath should allow for differentiated services based on C-VIDs and priority bits
Datapath should support wired and wireless links in the access and backhaul.

## Slide 15: Datapath specific attributes
Node of Attachment
  R1 MAC and PHY configuration parameters
  R1 performance and QoS parameters
    E.g. supported service classes (Throughput up/down, delay, jitter)
  R6d configuration parameters
  VLAN configuration and mapping
Backhaul (remark: check MEF for further attributes)
  R6d configuration parameters
  R3d configuration parameters
  Service specification
  Service mapping table
Subscription Service
  User specific service specification
Core Network Service
  R3d configuration parameters
  Network Interface performance
    E.g. supported service classes (throughput up/down, delay, jitter)

## Slide 16: Data path basic functions
Data path establishment
  Retrieve user specific configuration information from Subscription Service
  Configure terminal interface R1
  Configure forwarding and interfaces R1 and R6d in NA
  Configure link performance and interfaces R6d and R3d in Backhaul
  Initiate configuration of R3d in CNS
  Signal completion of access link establishment
Data path relocation
  Reconfigure terminal interface R1 to new NA
  Configure forwarding and interfaces R1 and R6d in new NA
  Relocate interface R6d in Backhaul towards new NA
  Signal completion of access link relocation
Data path tear down
  Teardown interface in Terminal
  Teardown forwarding function and interfaces in NA
  Teardown interface in CNs
  Remove resource allocations in Backhaul
  Signal completion of teardown

## Slide 17: Data path basic functions
AAA Policy
Configuration
DHCP
Application
ANQP
Access Network
Network Selection
Accounting
Disassociation
Host Configuration
Application
Policy Control
Application
Host Config Release
Accounting
Authentication
Authorization
Association
Scanning
Data path establishment
Data path relocation
Data path teardown
Terminal
Subscription
Service

## Slide 18: NA attributes mapping to IEEE 802 technologies
 |  | 802.3 | 802.11 | 802.15.? | 802.16 | 802.22
R1 Config | QoS Parms |  |  |  |  | 
 | Forwarding |  |  |  |  | 
 | Filtering |  |  |  |  | 
 | Security |  |  |  |  | 
R6d Config |  |  |  |  |  | 
VLAN Config |  |  |  |  |  | 
NA configuration is performed from information delivered by the Subscription Service as part of authorization

## Slide 19: IEEE 802 backhaul solutions MAC-in-MAC (Provider Backbone Bridging)
NA effectively representing ‘BEB’
Link identified by B-SA + I-SID
  B-SA uniquely correlated to terminal MAC address
    Would it work using terminal MAC as B-SA (C-SA = B-SA)?
  B-DA represents access router peer
  I-SID for further study;
Mobility support by learning B-bridges
Protocol for dynamic configuration of PBBN
Open: Link state signaling?
Security assessment

## Slide 20: IEEE 802 backhaul solutions MACsec
MACsec establishes single hop across multiple bridges
MACsec peers are R6d at the NA and R3d at the CNS
Control protocol by 802.1X
  EAP based establishment of security association
    How to tie with EAP based access authentication
  Well defined link state management
Protocol for mobility support required
  Wouldn’t be a kind of 802.11r applicable to MAC sec ptp links?
Scalability and performance issues
  MACsec Ys well distributed on NA side, however the entity at the CNS may have to handle a huge number of sessions.

## Slide 21: IEEE 802 backhaul solutions SDN
T.b.d., e.g. https://mentor.ieee.org/omniran/dcn/14/omniran-14-0040-00-CF00-ethernet-connection-service.pdf
  Proposal of Paul Bottorff (May 2014)

## Slide 22: Conclusion
The slides present the logical structure and the essential content of the intented data path section.
Is there any other recommendation or hint for the section?