## Slide 1
P802.1CF NRM Refinements |  |  | 
Date: 2015-03-03 |  |  | 
Authors: |  |  | 
Name | Affiliation | Phone | Email
Max Riegel | Nokia Networks | +49 173 293 8240 | maximilian.riegel@nokia.com
Notice: This document does not represent the agreed view of the IEEE 802.1 OmniRAN TG. It represents only the views of the participants listed in the ‘Authors:’ field above. It is offered as a basis for discussion. It is not binding on the contributor, who reserve the right to add, amend or withdraw material contained herein. |  |  | 
Copyright policy: The contributor is familiar with the IEEE-SA Copyright Policy <http://standards.ieee.org/IPR/copyrightpolicy.html>. |  |  | 
Patent policy: The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. |  |  | 
Abstract
Document ‘omniran-14-0083-00-00TG-p802-1cf-network-reference-model.docx’ specifies the Network Reference Model of P802.1CF. This document proposes further refinements to the NRM figures considered in ‘omniran-15-0003-01-CF00’ to enhance clarity and completeness of the NRM representation. This revision provides further refinements on top of the conclusions of the discussion in the Feb 16th conference call.

## Slide 2: P802.1CF NRM Refinements
2015-03-03
Max Riegel
(Nokia Networks)

## Slide 3: Terminology
SS: Subscription Service
CIS: Coordination and Information Service
AN: Access Network
ANC: Access Network Controller
NA: Node of Attachment
CN: Core Network
CNI: Core Network Interface
CNC: Core Network Controller
TE: Terminal
TEI: Terminal Interface
TEC: Terminal Controller
BH: Backhaul

## Slide 4: From omniran-14-0083-00-00TG-p802-1cf-network-reference-model.docx Detailed Network Reference Model
Figure 4: Network Reference Model exposing Access Network details

## Slide 5: ATL F2F discussion results
Access Network denotes complete network entity including control entity
Terminal represents complete entity including data path interface, control entity and functions out of scope
  Endpoint of data path denoted ‘Terminal Interface’
  Control rephrased to ‘Terminal Controller’
Core Network represents complete entity including data path interface, control entity and higher layer functions out of scope of P802.1CF
  Endpoint of data path denoted ‘Core Network Interface’
  Control rephrased to ‘Core Network Controller’
Dotted line between Subscription Service and CNC to indicate, that existence of such interface is assumed but details are out of scope.

## Slide 6: From omniran-15-0003-01-CF00-nrm-ambiguities: ATL F2F discussion result
Core Network
Access Network
Terminal
Terminal Interface
R1
Coordination and Information Service
R2
R9c
R8c
AN Ctrl
TE Ctrl
Subscription
Service
Core Network Interface
R3d
R3s
CN Ctrl
R3c
NA
Backhaul
R6d
R6c
R7c

## Slide 7: Conclusions of Feb 16th call
For further discussion
More clear definition of ‘Terminal Interface’ and ‘Core Network Interface’ required
Why do we not split R1 into R1d and R1c to make it more aligned to R3
  By this split, R8c might become superfluous
Why embedding Subscription Service into Core Network?
  There is good reason to separate these entities with bringing the interface between Subscription Service and Core Network Interface into scope.

## Slide 8: Proposed revision of the NRM
Core Network
Access Network
Terminal
Terminal Interface
R1d
Coordination and Information Service
R2c
R9c
R8c/1c
AN Ctrl
TE Ctrl
Subscription
Service
Core Network Interface
R3d
R4c
CN Ctrl
R3c
NA
Backhaul
R6d
R6c
R7c
R5c

## Slide 9: Resolving the R8c vs. R1c issue
R8c
Denotes ctrl-to-ctrl interface
May comprise information elements not defined within R1 specification
..?
R1c
For symmetry reasons, R1 should follow R3
Label should be aligned to data path interface
No major distinction necessary as R1 may comprise multiple specifications
..?
Maybe, we have to more clearly specify the scope of a data path interface. IMHO, an data path interface comprises all functions required for sending and receiving Ethernet frames once the connection is established.

## Slide 10: Additional considerations
Discussions have shown that further information is required to show scope and applicability of NRM
  How NRM is related to ‘real’ networks?
    Operators expressed that applicability is limited due to missing IP layer functionality
  What benefits is the NRM providing with its focus on PHY and LINK layer?
  What are the endpoints of communication and reference points in the bigger picture?
The next slide may provide some figures for explaining the scope and applicability.

## Slide 11
Medium
Medium
Data Link
Physical
Network
Transport
Application
DL
Phy
DL
Phy
Data Link
Physical
Network
Transport
Application
Network
Network
Medium
Medium
Data Link
Physical
Data Link
Physical
Access Network
Terminal
Core Network
Information Service
DL
Phy
DL
Phy
DL
Phy
DL
Phy
Medium
Backhaul
Backhaul
End-to-end network topology
Subscription Service
R1
Schematic NRM for the IEEE 802 access network
Terminal
Access Network
Core Network
Subscription Service
R3
R4
R2
Scope of P802.1CF in the protocol layer architecture
Node of Attachment
Terminal Interface
Core Network Interface
Scope of P802.1CF

## Slide 12: NRM benefits for SDN
The chapter on NRM should close with a section on applicability of the definitions for SDN.
Generic architecture model for Ethernet access networks defining entities and interfaces, providing the base for
  Identity and attribute information of entities
  Functional behavior and message exchanges
However P802.1CF will not …
  define higher layer protocols for conveying information between SDN controller and access network nodes
  specify higher layer protocols for the exchange of control information between network entities
  make pre-assumptions about the network layer protocol