## Slide 1
P802.1CF architectural considerations for EM and NM |  |  | 
Date: 2016-03-15 |  |  | 
Authors: |  |  | 
Name | Affiliation | Phone | Email
Max Riegel | Nokia | +49 173 293 8240 | maximilian.riegel@nokis.com
Notice: This document does not represent the agreed view of the IEEE 802.1 OmniRAN TG. It represents only the views of the participants listed in the ‘Authors:’ field above. It is offered as a basis for discussion. It is not binding on the contributor, who reserve the right to add, amend or withdraw material contained herein. |  |  | 
Copyright policy: The contributor is familiar with the IEEE-SA Copyright Policy <http://standards.ieee.org/IPR/copyrightpolicy.html>. |  |  | 
Patent policy: The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. |  |  | 
Abstract
The presentation provides considerations for the architectural arrangement of EM and NM within P802.1CF architecture

## Slide 2: P802.1CF architectural considerations for EM and NM
Max Riegel
(Nokia)

## Slide 3: Problem description
OmniRAN currently investigates the representation of Network Management within its P802.1CF architecture.
Various options have been introduced by https://mentor.ieee.org/omniran/dcn/16/omniran-16-0019-01-CF00-measurement-and-management-in-ieee-802-11.pptx and https://mentor.ieee.org/omniran/dcn/16/omniran-16-0012-01-CF00-ethernet-oam-survey-and-introducing-nms.pptx without a conclusive proposal for the architectural arrangements.
To mature consensus on the architectural concepts, Network Management should be considered from various perspectives including operational models, network virtualization and modern software-driven implementation aspects.

## Slide 4: NRM Overview
The NRM defines a generic architecture of IEEE 802 access network
It provides the set of functions and their relationships of an IEEE 802 access network.
The NRM does not specify the operational composition of access network functions with interconnected functions on the network side.
Access Router
Access Network
Terminal
TEI
R1
CIS
R2
R10
R8
ANC
TEC
SS
ARI
R3
R4
ARC
R9
NA
BH
R6
R5
R7
R11
CIS Coordination and Information Service
SS Subscription Service
TEC Terminal Control
TEI Terminal Interface
ANC Access Network Control
NA Node of Attachment
BH Backhaul
ARC Access Router Control
ARI Access Router Interface

## Slide 5: Operational assumption for authentication and trust establishment
Service Provider
User
Subscription

## Slide 6: Generic case of Access Network operation
Focus of P802.1CF
Service Provider
User
Subscription
Access Network Operator
IP Network
Operator

## Slide 7: NMS vs. ‘Management Function Set’ Deployment Case (III)
NMS
(SS)
Controller
(EM)
Interface
(NE)
OmniRAN
R2, R4,
R11
R5, R7
N<>S
E<>W
Management plane
Network plane
ItfN
NMS
EM
R1, R6,
R3
Slide from: https://mentor.ieee.org/omniran/dcn/16/omniran-16-0019-01-CF00-measurement-and-management-in-ieee-802-11.pptx

## Slide 8: Location of NM: Option 1
Access Router
Access Network
Terminal
TEI
R1
CIS
R2
R10
R8
ANC
TEC
SS
ARI
R3
R4
ARC
R9
NA
BH
R6
R5
R7
R11
Access Network Operator
BSS
OSS
NM
NMfkts
EM
EM
EM

## Slide 9: Location of NM: Option 2
Access Router
Access Network
Terminal
TEI
R1
CIS
R2
R10
R8
ANC
TEC
SS
ARI
R3
R4
ARC
R9
NA
BH
R6
R5
R7
R11
Access Network Operator
BSS
NM
NMfkts
EM
EM
EM
OSS

## Slide 10: Conclusion
NMS belongs into the operational domain of the Access Network Operator
Element management is part of Access Network Control
Multiple options possible for location of Network Management
  It seems more logical to locate NM into the OSS of the AN operator with communication towards the EM happening by EM function calls
    Like done by RESTful interfaces today.