## Slide 1
Investigation on Accounting and Monitoring |  |  | 
Date: [2016-05-26] |  |  | 
Authors: |  |  | 
Name | Affiliation | Phone | Email
Hao Wang | Fujitsu R&D Center | +86-10-59691000 | wangh@cn.fujitsu.com
Lefei Wang | Fujitsu R&D Center | +86-10-59691000 | wanglefei@cn.fujitsu.com
Ryuichi Matsukura | Fujitsu/Fujitsu Laboratory | +81-44-754-2667 | r.matsukura@jp.fujitsu.com
Notice: This document does not represent the agreed view of the OmniRAN EC SG. It represents only the views of the participants listed in the ‘Authors:’ field above. It is offered as a basis for discussion. It is not binding on the contributor, who reserve the right to add, amend or withdraw material contained herein. |  |  | 
Copyright policy: The contributor is familiar with the IEEE-SA Copyright Policy <http://standards.ieee.org/IPR/copyrightpolicy.html>. |  |  | 
Patent policy: The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. |  |  | 
Abstract
The presentation provides preliminary investigation results on account and monitoring. The contents include terms, architectures, and process defined by other SDOs. It is aimed to get the agreement of the group on what concept is currently in scope of P802.1CF.

## Slide 2: Investigation on Accounting and Monitoring
2016-05-26
Hao Wang
Fujitsu R&D Center

## Slide 3: What is Accounting
Accounting describes the process of gathering usage data records at network devices and exporting those records to a collection server, where processing takes place. Then the records are presented to the user or provided to another application, such as performance management, security management, or billing.
Historically close linkage between accounting and billing, but accounting is different from billing, because billing is just one of the applications that leverage accounting.
3-Tier Accounting
Infrastructure

## Slide 4: Accounting Architecture in IETF
Data about resource consumption (e.g. transmitted volume)
Meters is probably placed at the edge of the network
Static meters and configurable meters
Collection of meter data can be initiated by the meter itself (push model) or by a collector entity (pull model).
Metering policies define how collection and aggregation is done.
Control of data gathering (via metering)
Transport and storage of accounting data.
Associate the metered data with a user Associate the metered data with a customer (service subscriber) that is responsible for payment.
Charging derives non-monetary costs for accounting data sets based on service and customer specific tariff parameters.
Charging policies define the tariffs and parameters which are applied.
Billing translates costs calculated by the Charging into monetary units and generates a final bill for the customer.
IETF RFC 3334

## Slide 5: Accounting Management
Accounting now becomes a major building block for network and application design and deployment.
  collected accounting data records are not limited to billing applications, in addition, can be used for other applications such as performance monitoring, checking that a configuration change fixed a problem, or even security analysis.
  For example, if the administrator has configured the network so that business-critical data should go via one path and best-effort traffic should take another path, accounting can verify if this policy is applied and otherwise notify the fault and configuration tools.
Management Functional Area (MFA) | Management Function Set Groups
Fault | Alarm surveillance, fault localization and correlation, testing, trouble administration, network recovery
Configuration | Network planning, engineering, and installation; service planning and negotiation; discovery; provisioning; status and control
Accounting | Usage measurement, collection, aggregation, and mediation; tariffing and pricing
Performance | Performance monitoring and control, performance analysis and trending, quality assurance
Security | Access control and policy; customer profiling; attack detection, prevention, containment, and recovery; security administration

## Slide 6: Monitoring for Accounting and Performance
Similarities | Differences
Both parts collect usage information, which can be applied to similar applications afterward | performance addresses details such as network load, device load, throughput, link capacity, different traffic classes, dropped packets, congestion accounting addresses usage data collection, such as transmission volume, online time, etc
Same protocols are applicable for both, such as SNMP counters can be assigned to both performance and accounting | for performance, collection interval needs to be real time for accounting, it doesn’t have to be real time, except for prepaid billing
Both monitoring sources are important for security management - combination of the two areas can be a strong instrument to identify security attacks almost in real time | accounting don’t keep historical data sets, because the billing application does this. performance needs history data to analyze deviation from normal as well as trending functions
 | accounting monitoring is always passive, by meters performance monitoring can be passive or active

## Slide 7: Accounting, Charging Deployment (WiMAX)
Accounting Client
  Receiving the charging information in the PCC rule and forwarding it as accounting information to Accounting Agent;
  Collecting the accounting information from Accounting Agent and relaying it to the OCS for online charging and offline charging.
Accounting Agent
  Enforcement point of charging in the ASN.
  Enforcing charging policy of PCC rule and generating offline accounting information;
  Reporting accounting information to accounting client

## Slide 8: Accounting, Charging Deployment (3GPP)
Functional blocks for offline charging
  Charging Trigger Function (CTF), mandatory
    Transferring ‘chargeable events’ to ‘charging events’
  Charging Data Function (CDF)
    Generate CDR, well defined content and format
  Charging Gateway Function (CGF)
    Processing, routing, filtering, managing CDR
Accounting
Metrics Collection
Accounting
Data Forwarding
Charging events
Chargeable events
CTF
Collected accounting metrics
Rf
Chargeable event: A single call, service profile administration, or roaming.
Charging event : Set of charging information forwarded by the CTF.
Accounting Metrics Collection
  Provide metrics that identify the user and the user’s consumption of network resources and/or services in real-time.
Accounting Data Forwarding
  Assembles charging events
  Forwards the charging events towards the CDF

## Slide 9: Accounting and Monitoring Mapping to NRM
Access Router
Access Network
Terminal
TEI
R1
CIS
R2
R10
R8
ANC
TEC
SS
ARI
R3
R4
ARC
R9
NA
BH
R6
R5
R7
R11
BSS
OSS
NM
NMfkts
EM
EM
EM
BSS
OSS
NM
EM
EM
Monitoring
Accounting
Access Network Operator
IP Service Provider
Billing
(Out of scope)

## Slide 10: Accounting and Monitoring Mapping to NRM
Monitoring
Collection, mediation,
accounting,
Performance Monitoring for real time data
Metering for usage data

## Slide 11: Questions, Comments