## Slide 1
Model for Accounting and Monitoring |  |  | 
Date: [2017-05-15] |  |  | 
Authors: |  |  | 
Name | Affiliation | Phone | Email
Hao Wang | Fujitsu R&D Center | +86-10-59691000 | wangh@cn.fujitsu.com
Xiaojing Fan | Fujitsu R&D Center | +86-10-59691000 | fanxiaojing@cn.fujitsu.com
Su Yi | Fujitsu R&D Center | +86-10-59691000 | yisu@cn.fujitsu.com
Ryuichi Matsukura | Fujitsu/Fujitsu Laboratory | +81-44-754-2667 | r.matsukura@jp.fujitsu.com
Notice: This document does not represent the agreed view of the IEEE 802.1 OmniRAN TG. It represents only the views of the participants listed in the ‘Authors:’ field above. It is offered as a basis for discussion. It is not binding on the contributor, who reserve the right to add, amend or withdraw material contained herein. |  |  | 
Copyright policy: The contributor is familiar with the IEEE-SA Copyright Policy <http://standards.ieee.org/IPR/copyrightpolicy.html>. |  |  | 
Patent policy: The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. |  |  | 
Abstract
This presentation proposes the initial thoughts on modeling the accounting and monitoring attributes and functions.

## Slide 2: Model for Accounting and Monitoring
2017-05-17
Hao Wang
Fujitsu R&D Center

## Slide 3: Introduction
Accounting is about gathering usage data records for network devices, exporting those records to a collection server, processing the records for user or another application.
  Usage data records could be generated based on
    User session statistics
    Port performance statistics
Monitoring on the port provides real-time and accurate observation of the performance of network resource.

## Slide 4: Accounting and Authentication
User session started when user has been authenticated by 802.1X.
802.1X PAE maintains session statistics for accounting purposes.
PAE resides in both TEC and ANC, and may reside in ARC in some scenarios.
Accounting can be augmented to ‘control’ as a function, avoid to import the full model of 802.1X.
  Accounting policy refers to the set of parameters for configuration in order to provide the appropriate accounting records.
  Accounting records can be leveraged in multiple use cases, such as billing, security management, etc.

## Slide 5: Accounting and Authorization
QoS is authorized to the terminal and required by new services when user session established.
The ANC processes the network resource requests and determines the policy for QoS control.
Accounting gathers the utilization information of network resources and maintain the statistics for QoS.
Accounting records can be provided to external management entities such as NMS for auditing the operation of services in a user session.

## Slide 6: Monitoring
Monitoring the performance of a physical port can be implemented on the interface entities, or as a separate entity.
Monitoring the user specific traffic requires filtering rules provided by the control entities.
Monitoring jobs and reports are scheduled and configured by the control entities.
Monitoring records based on the performance statistics can be pushed to or pulled from the control entities for accounting or other management purposes.

## Slide 7: Generic OmniRAN Model
For network management purposes, the underlay network infrastructure needs to be modeled.
Control and service entities form a common client-server pair support the network management protocol such as NETCONF.
Interface entities should be separated for outstanding IEEE 802 attributes and functionality.
Refer to the UML model in 802.1X
Port
OmniRAN Network
Control
*
Ctrl_ID
Service
Control
Interface
Interface
*
Intf_ID
Port
*
Port_ID
ANC
AN
ARC
AR
TEC
TE
NA
NA
BH
BH
TEI
TE
ARI
AR
802.11
802.11
802.16
802.16
802.22
802.22
802.3
802.3

## Slide 8: Model for OmniRAN Control Functions
OmniRAN Network
Control
*
Ctrl_ID
Interface
*
Intf_ID
ANC
AN
ARC
AR
TEC
TE
Authentication
AuthenProc
SessionStatistics
session
Port
*
Port_ID
NA
NA
BH
BH
TEI
TE
ARI
AR
Authorization
AuthorProc
QoS
Serviceflow
Accounting
AccountProc
AccountingRecords
mediation
AccountingPolicy
Monitoring
MonitorProc
MonitoringRecords
measurement
MonitoringPolicy
PAE
supplicant
authenticator
LogonProcess
SessionStatistics
PAE System
…
IEEE 802.1X model

## Slide 9: Element: Accounting
Control
AccountProc
AccountingPolicy
Accounting
+accounting-id
+ss-id
+state
+accounting-type
+user-id
AccountingRecords
+application-ready-data
mediation
*
1
+accounting-condition
+accounting-action

## Slide 10: Element: Monitoring
Port
MonitorProc
Monitoring
+monitoring-id
+state
+monitor-type
MonitoringRecords
+Tx-volume
+Rx-volume
+Throughput
+QoS-monitoring
measurement
*
1
MonitoringPolicy
+start-time
+duration
+interval
+storage-time
+accuracy
+monitor-source
+trigger-condition

## Slide 11: Snapshot of 802.1X UML Model

## Slide 12: Reference
802.1X-2010
802.1Xck-d1-0
omniran-17-0028-00-CF00-data-model-for-fdm.pptx
omniran-16-0039-00-CF00-key-concepts-of-accounting-and-monitoring.pptx
802-1cf-d0-4

## Slide 13: Questions, Comments Thank YOU!