## Slide 1
Layer-2 Network Virtualization |  |  | 
Date: 2017-07-10 |  |  | 
Authors: |  |  | 
Name | Affiliation | Phone | Email
Max Riegel | Nokia Bell Labs |  | maximilian.riegel@nokia.com
Notice: This document does not represent the agreed view of the IEEE 802.1 OmniRAN TG. It represents only the views of the participants listed in the ‘Authors:’ field above. It is offered as a basis for discussion. It is not binding on the contributor, who reserve the right to add, amend or withdraw material contained herein. |  |  | 
Copyright policy: The contributor is familiar with the IEEE-SA Copyright Policy <http://standards.ieee.org/IPR/copyrightpolicy.html>. |  |  | 
Patent policy: The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. |  |  | 
Abstract
The presentation provides an introduction into the rationales and basic concepts for Layer-2 virtualized networks.

## Slide 2: Layer-2 Network Virtualization
Max Riegel
(Nokia Bell Labs)
2017-07-10

## Slide 3: Outline
Preface
Multi-tenancy networks
  Example: Shopping mall
  Example: Factory floor
Virtual networks
Virtualized networks
Standardization demand
P802.1CF
Data model of virtualized access network
Way forward

## Slide 4: Preface
Presentation provides idea of standardization demand.
  Idea stems from observations of emerging networking demand in the enterprise market.
Preliminary thoughts, no firm proposal
Further discussions required with potential stakeholders to create sharper picture.

## Slide 5: Multi-tenancy networks
Shared use of common infrastructure
  For operational or economic reasons
Multiple operational domains
  A tenant pays for some exclusive rights to use a defined portion of the infrastructure
  Infrastructure is owned by a ‘landlord’
Growing importance in highly distributed economy
  Smaller, highly specialized entities operate pieces of a bigger process
  Such independent business entities require independent networks at a common location.

## Slide 6: Example: Shopping mall
Shopping malls assemble a variety of (even) competing shops at a common building.
Stores gain their competitiveness through offering the same goods at many places
  Common supply processes and correlation of customer insights
With ‘cloud’, ‘big data’ and ‘customer intelligence’ driving the evolution of the business, vendors require their own network
  Not only a networking service of the mall owner
    Responsiveness and flexibility to install new functions
    Exclusive access to communications’ meta-data

## Slide 7: Example: Factory floor
Production processes are getting split up into multiple separate businesses
  E.g. a brewery may outsource the bottling of the beer to a specialized company
    Instead of the brewery buying the bottling plant and taking care of the logistics by itself
    The manufacturer of the bottling plant may increase its business through selling a bottling service instead of only selling the machinery.
Subcontractors will require their own networks at the production plant
  Not only a networking service of the production plant
    Responsiveness to issues and reorganizations
    Liability

## Slide 8: Virtual networks
IEEE 802 supports virtual networks. (VLAN, multi-SSID)
Virtual networks separate the data paths but do not isolate control and management (meta data).

## Slide 9: Virtualized networks
Virtualization separates data path as well control and management.
Can be implemented through virtualized SDN.

## Slide 10: Standardization demand
Tenant
Produces a service at multiple locations
Requires same kind of virtualized network at all of the locations.
A common template of a virtualized network would simplify operation and negotiations with the landlords.
Landlord
Owns and operates the network infrastructure at a location
Assigns resources to multiple tenants according to contractual agreements.
A common template of a virtualized network would simplify business.
There is demand for a common template (blue-print of a data model) of a virtualized network for running a small business inside a bigger location.

## Slide 11: P802.1CF
P802.1CF defines Network Reference Model and Functional Description of IEEE 802 Access Network
Network model fits well to the deployment scenario in shopping malls and production plants.
  Plain Layer-2 data path avoids interdependencies with network layer configuration particularities.
Specification contains generic information model (UML) of an IEEE 802 network connecting multiple terminals/devices to a gateway/router.
P802.1CF could be used as the base for specification of the template.

## Slide 12: Data model of virtualized access network
Template would be a data model of the virtualized local area network.
Only external interfaces to be covered.
Description could be done in YANG.
Scope of data model

## Slide 13: Way forward
Does it really make sense to standardize a data model of a virtualized IEEE 802 Access Network?
  For which deployment scenario?
    IMHO: There is not the one-fits-all solution.
  Where are the market drivers?
  Who are the opponents?
  Is a YANG data model the right approach?
Who would be interested in progressing the idea further?