## Slide 1
P802.1CF Information Model Structure |  |  | 
Date: 2017-09-06 |  |  | 
Authors: |  |  | 
Name | Affiliation | Phone | Email
Max Riegel | Nokia |  | maximilian.riegel@nokia.com
Notice: This document does not represent the agreed view of the IEEE 802.1 OmniRAN TG. It represents only the views of the participants listed in the ‘Authors:’ field above. It is offered as a basis for discussion. It is not binding on the contributor, who reserve the right to add, amend or withdraw material contained herein. |  |  | 
Copyright policy: The contributor is familiar with the IEEE-SA Copyright Policy <http://standards.ieee.org/IPR/copyrightpolicy.html>. |  |  | 
Patent policy: The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. |  |  | 
Abstract
The revision of the presentation provides an initial example of the basic structure of the P802.1CF information model.
Revision 2 adds the core model for service as well as a short explanation of the notation

## Slide 2: P802.1CF Information Model Structure
Max Riegel
(Nokia)
2017-09-06

## Slide 3: Information Model
An information model* in software engineering is a representation of concepts and the relationships, constraints, rules, and operations to specify data semantics for a chosen domain of discourse.
Typically it specifies relations between kinds of things, but may also include relations with individual things.
It can provide sharable, stable, and organized structure of information requirements or knowledge for the domain context.
Y. Tina Lee (1999). "Information modeling from design to implementation" National Institute of Standards and Technology.
* On difference between Information Model and Data Model: RFC 3444; A. Pras , J. Schoenwaelder; IETF, 2003

## Slide 4: Purpose of P802.1CF Information Model
Graphical representation of the configuration information and statistics of the IEEE 802 access network infrastructure and communication service.
Distinction and relationship between ‘network’ information and ‘service’ information
  Structural description of network architecture.
    Describe what the thing is
  Description of parameters of user service
    Describe what the thing delivers
Description of the structure of the management information and the control functions of IEEE 802 access network.

## Slide 5: Network management approaches
FCAPS
Fault management
  Detection, correction and logging of faults that occur in the network
Configuration management
  Monitoring of system configuration information, and any changes of it
Accounting management
  Collection and tracking of network utilization information
Performance management
  Ensuring that network performance remains at acceptable levels
Security management
  Controlling access to assets in the network
OAMPT
Operation
  Procedures used to control normal network operation
Administration
  Support procedures accompanying normal network operation
Maintenance
  Re-adjustments of system operation due to failures and regular needs
Provisioning
  Installation and activation of new network resources.
Troubleshooting
  Procedures due to fault or failure to compensate the misbehavior
Neither approach can really be directly reflected in information model; OAMPT may be more suited for IEEE 802 access network.

## Slide 6: Thoughts on information model structure
Essentially two information models needed:
  Network model
  Service model
Network information model
  Description of network infrastructure
  Structured according to the functional entities of NRM
  Differentiating configuration (wr) and statistics (ro)
User service information model
  Abstract description of communication service
    Description of user session
    End-points, performance attributes, security aspects

## Slide 7: AN Information Model - a first attempt
Access Network
AN-ID
Network Management Service
NMS-ID
Coordination and Information Service
CIS-ID
Access Network Control
ANC-ID
Subscription Service
SS-ID
Service Provider: FQDN
1+
0+
1
Access Router Control
ARC-ID
Access Router Interface
ARI-ID
Access Router
AR-ID
1+
1
Backhaul
BH-ID
Node of Attachment
NA-ID
0+
1
1+
1
Terminal Control
TEC-ID
Terminal Interface
TEI-ID
Terminal
TE-ID
1+
1
0+

## Slide 8: Service Information Model - a first attempt
User Service
Service-ID
Service Provider
SP-ID:FQDN
Subscription Service
CIS-ID
Subscription
NAI
0+
1
Service-Flow
Service-Flow-ID
Terminal
TE-ID
Session
Session-ID
1+
1
User
User-ID
Datapath
Datapath-ID
0+
1
1
1
IP Provider
NMS-ID
0+
Access Network Operator
AN-Op-ID
1

## Slide 9: Information model notation
Class name
Attribute#1: abstract type
Attribute#2: abstract type
…
Response Function#1(parameter)
Response Function#2(parameter)
...
Information element with specification of attributes as well as functions, which could be invoked by other elements over reference points. Functions return an result value.
Whole
Part
Aggregation
Aggregation is a special type of association used to model a "whole to its parts" relationship.
In basic aggregation relationships (framed diamond), the lifecycle of a part class is independent from the whole class's lifecycle.
- Associations are always assumed to be bi-directional; this means that both classes are aware of each other and their relationship
- In a uni-directional association (arrow), two classes are related, but only one class knows that the relationship exists.
The composition aggregation relationship (filled diamond) is just another form of the aggregation relationship, but the child class's instance lifecycle is dependent on the parent class's instance lifecycle.
- Associations are always assumed to be bi-directional; this means that both classes are aware of each other and their relationship
- In a uni-directional association (arrow), two classes are related, but only one class knows that the relationship exists.
0+
Whole
Part
1+
Whole
Part
0-1
Whole
Part
1

## Slide 10: Conclusion
Do the first attempts make sense?
How to proceed?:
  More comprehensive listing of attributes
    Config attributes: ‘wr’
    Statistics attributes: ‘ro’
  Adding of methods to object classes
    Methods denote functional procedures described in chapter 7