## Slide 1: Time Sensitive Networking within the scope of P802.1CF
Max Riegel
OmniRAN TG chair
(Nokia)

## Slide 2: TSN and OmniRAN architectural models
OmniRAN will adopt TSN functionality to its P802.1CF specification. Amending the P802.1CF functional description chapters on ‘Data path’ and ‘QoS, authorization, and policy control’
How does it fit together?

## Slide 3: P802.1CF architectural model
TSN within the scope of P802.1CF

## Slide 4: P802.1CF Access network reference model
P802.1CF provides reference architecture and functional description of IEEE 802 LANs supporting managed attachments of terminals
  Such networks are commonly called ‘access networks’
Fits to nearly all kind of managed LANs w/ access control

## Slide 5: P802.1CF Network Reference Model
NRM represents a logical view on an access network architecture
Functional entities represented by rounded rectangles
Relations are shown by reference points indicating interfaces
  Forwarding path of Ethernet frames represented by solid lines
  Control interfaces represented by dotted lines

## Slide 6: Representation of TSN configuration models in P802.1CF NRM
AR
AN
TE
TEI
R1
CIS
R2
R8
ANC
TEC
SS
ARI
R3
R4
ARC
R12
NMS
R11
NA
BH
R6
R5
R7
R10
Listener/Talker
Listener/Talker
Bridge
Bridges
Centralized Network Configuration
Centralized User Configuration
R9
User/Network Configuration info
User/Network Configuration info

## Slide 7: Adoption of TSN Functionality to P802.1CF
TSN within the scope of P802.1CF

## Slide 8: P802.1CF supports TSN
P802.1CF access network represents the bridged connectivity between end stations
  Supports as well multicast behavior for single Talker forwarding streams to multiple Listener
P802.1CF datapath (solid line) can provide support for time-sensitive streams and real-time data
  Implementation of TSN queuing and forwarding in the Bridges in NA and Backhaul required
The TSN configuration models w/ centralized network configuration can be easily represented in the P802.1CF Network Reference Model

## Slide 9: Centralized network / distributed user configuration in P802.1CF NRM
AR
AN
TE
TEI
R1
CIS
R2
R8
ANC
TEC
SS
ARI
R3
R4
ARC
R12
NMS
R11
NA
BH
R6
R5
R7
R10
Listener/Talker
Listener/Talker
Bridge
Bridges
Centralized Network Configuration
R9
User/Network Configuration info
User/Network Configuration info
Access Network Control (ANC) provides centralized network configuration for user sessions
  Basic network configuration delivered by Network Management Service (NMS)
  User session configuration info provided through R8 and R9 from/to end stations
CNC is contained in ANC
  ANC is control entity to align user demand with available network resources
R8, R9, and ANC provide means to process User/ Network Configuration Info

## Slide 10: Fully centralized TSN configuration in P802.1CF NRM
AR
AN
TE
TEI
R1
CIS
R2
R8
ANC
TEC
SS
ARI
R3
R4
ARC
R12
NMS
R11
NA
BH
R6
R5
R7
R10
Listener/Talker
Listener/Talker
Bridge
Bridges
Centralized Network Configuration
Centralized User Configuration
R9
User/Network Configuration info
Access Network Control (ANC) provides centralized network configuration for user sessions
  Basic network configuration delivered by Network Management Service (NMS)
  User session configuration delivered by Subscription Service (SS)
CUC maps to SS
CNC maps to ANC
  ANC is control entity to align user demand with available network resources
No use of R8, R9

## Slide 11: Distributed TSN configuration model doesn’t work well in P802.1CF NRM
AR
AN
TE
TEI
R1
CIS
R2
R8
ANC
TEC
SS
ARI
R3
R4
ARC
R12
NMS
R11
NA
BH
R6
R5
R7
R10
Listener/Talker
Listener/Talker
Bridge
Bridges
R9
User/Network Configuration info
User/Network Configuration info
Access Network Control (ANC) doesn’t have any control role in TSN configuration
  User session configuration info provided through R8 and R9 from/to end stations
  ANC purely forwards configuration information to the bridges in NA and BH
No central knowledge about resource usage throughout the network.
Not really the scenario P802.1CF is designed for!

## Slide 12: Amendments to P802.1CF Specification
TSN within the scope of P802.1CF

## Slide 13: Necessary amendments to P802.1CF spec
Overview
References, definitions, acronyms and abbreviations
Conformance
Access network reference model
  Basic architectural concepts and terminology
  Overview of NRM
  Basic, enhanced and comprehensive NRM
  Operational roles
  Network virtualization
  Identifiers
  Deployment scenarios
Functional Design and Decomposition
  Access network setup
  Network discovery and selection
  Association and disassociation
  Authentication and trust establishment
  Data path establishment, relocation and teardown
  Authorization, QoS and policy control
  Accounting and monitoring
  Fault diagnostics and maintentance
  Information model
Network softwarization functions
  SDN functional decomposition
  Network Function Virtualization
  Virtualized network instantiation

## Slide 14: Necessary amendments to P802.1CF specification
Data path
  Extension to time-sensitive and real-time traffic classes
  Shaping, scheduling and forwarding functions in bridges for best effort, time-sensitive and real-time traffic
  Clock distribution
Authorization, QoS, and policy control
  Amend QoS model for time-sensitive and real-time traffic classes
  Description of fully centralized and centralized/distributed TSN configuration models
Open: Coexistence with P802.1CF policy control model

## Slide 15: P802.1CF QoS architecture
Repository of QoS control/policy information is part of Subscription Service
  Policy parameters belong to subscription
  Subscription service provides QoS parameters as part of authorization
    … and might have possibilities to change parameters during ongoing session
Generic policy control architecture
Policy decision point
Policy enforcement
point
Policy enforcement point
Policy enforcement point
Policy data base
Resource Request

## Slide 16: Policy control in P802.1CF NRM
AR
AN
TE
TEI
R1
CIS
R2
R10
R8
ANC
TEC
SS
ARI
R3
R4
ARC
R9
R12
NMS
R11
NA
BH
R6
R5
R7
Policy Data Base
Policy Decision Point
PEP
PEP

## Slide 17: Conclusion
TSN within the scope of P802.1CF

## Slide 18: Conclusion
It seems that TSN can be well covered in P802.1CF
  At least configuration models with centralized network configuration
  Distributed network configuration is not inline with centralized control structures of P802.1CF
P802.1CF could provide additional capabilities to TSN through its authorization and policy control features
  User initiated stream reservation can be checked against policies