## Slide 1
Information Model Structure |  |  | 
Date: [2017-11-07] |  |  | 
Authors: |  |  | 
Name | Affiliation | Phone | Email
Hao Wang | Fujitsu R&D Center | +86-10-59691000 | wangh@cn.fujitsu.com
Xiaojing Fan | Fujitsu R&D Center | +86-10-59691000 | fanxiaojing@cn.fujitsu.com
Ryuichi Matsukura | Fujitsu/Fujitsu Laboratory | +81-44-754-2667 | r.matsukura@jp.fujitsu.com
Notice: This document does not represent the agreed view of the IEEE 802.1 OmniRAN TG. It represents only the views of the participants listed in the ‘Authors:’ field above. It is offered as a basis for discussion. It is not binding on the contributor, who reserve the right to add, amend or withdraw material contained herein. |  |  | 
Copyright policy: The contributor is familiar with the IEEE-SA Copyright Policy <http://standards.ieee.org/IPR/copyrightpolicy.html>. |  |  | 
Patent policy: The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. |  |  | 
Abstract
This presentation provides further thoughts on the 802.1CF information model structure.

## Slide 2: Information Model Structure
2017-11-07
Hao Wang
Fujitsu R&D Center

## Slide 3: TMN 5-Layer Management Architecture
Every layer suggests certain management functionalities
  EML provides management functions for network elements on an individual or group basis. It also supports an abstraction of the functions provided by the network element layer.
  NML offers a holistic view of the network, independent of device types and vendors. It manages a network as supported by the element management layer.
FCAPS have different tasks at each layer.
EML-NML interface is the point

## Slide 4: 802.1X Model (1) – Symmetric Function
Symmetric structure & functions
  EAP higher layer
    EAP parser
  PAE logon process
    manage credential, initiate the use of supp and authen
  ‘X’ PACP
    802.1X control
  PDU tx & rx
    process EAPOL messages
‘X’ PAE can be implemented on single physical port
802.1X model describes ‘entities’ inside the dotted box
  essential attributes that need to be ‘set’ (enable) or ‘get’ (state)
  EAPOL Statistics survey the results of EAPOL request-response

## Slide 5: 802.1X Model (2) – Symmetric Function
PAE
supplicant
authenticator
LogonProcess
SessionStatistics
PAE System
…
Part of Figure 12-3 PAE management information
EAPOLStatistics

## Slide 6: 802.1X Model (3) – Asymmetric Function
An EAPOL Announcement protocol that allows a PAE to indicate the availability of network services, helping other PAEs to choose appropriate credentials and parameters for authentication and network access (Clause 10).
  Pair relationship: announcer & listener
  Associated to PAE, but roles are bounded to Authenticator and Supplicant separately
  Implementation flexibility
PAE
supplicant
authenticator
Announce
Announcement*
PAE System
Part of Figure 12-3 PAE management information
Announcer
Listener
*Announcement statistics

## Slide 7: Two Options for Creating Network Operation Model
AN only focus on the core of the NRM
The whole NRM make use of the symmetric structure
Core of the NRM
Service
Control
Interface
NMS
ANC
1
CIS
SS
TE
AR
NA
BH
Interface

## Slide 8: Practice with 7.1 AN Setup
Take AN setup for unlicensed spectrum (7.1) as an example
ANC
enable
(power-up)
NA
BH
NA_activated
AN operator
NMS
ANC_activated
NA_configuration
AN_configuration
AN_operation_status
enable
(power-up)
AN operator
NA_operation_status
Status, set and/or cleared by source
Procedures initiated by source and consumed by destination
(no need to specify details, maybe out of scope of 802)
…

## Slide 9: Option 1
Network Management Service
NMS-ID
Access Network Control
ANC-ID
bool activated
enum operationStatus;
// for setup on authorized spectrum
Timeout heldPeriod
1
Backhaul
BH-ID
bool activated
enum operationStatus
Node of Attachment
NA-ID
bool activated
enum operationStatus
// for setup on authorized spectrum
Geolocation
bool enableSensing
Timeout quietPeriod
1
1+
SpectrumDatabase
CIS-ID
preferredChannelList
backupChannelList
SensingStatistics
spectrumAvailability
channelClassification
1
1

## Slide 10: Option 2
Network Management Service
NMS-ID
Access Network Control
ANC-ID
bool activated
enum operationStatus;
// for setup on authorized spectrum
Timeout heldPeriod
1
Backhaul
BH-ID
bool activated
enum operationStatus
Node of Attachment
NA-ID
bool activated
enum operationStatus
// for setup on authorized spectrum
Geolocation
bool enableSensing
1
1+
SpectrumDatabase
CIS-ID
preferredChannelList
backupChannelList
SensingStatistics
spectrumAvailability
channelClassification
Timeout quietPeriod
1
1
TE
TE-ID
Geolocation
bool enableSensing
1
Interface

## Slide 11: Consensus have been Reached
It was agreed to keep the attributes as generic as possible, examples are shown in the following contribution,
  https://mentor.ieee.org/omniran/dcn/17/omniran-17-0081-01-CF00-user-service-information-model.pptx
It was agreed not to integrate the FDM functionalities at this moment, but to create a separate FDM model when the main model got shaped.
Some of the attributes related with FDM functionalities may appear in the main model.
Since there are two separate models under discussion, same attributes may appear in both the user service model and network operation model, but consisted by different classes.

## Slide 12: Reference: 802.1X model

## Slide 13: Questions, Comments Thank YOU!