## Slide 1
Information Model Structure |  |  | 
Date: [2017-12-03] |  |  | 
Authors: |  |  | 
Name | Affiliation | Phone | Email
Hao Wang | Fujitsu R&D Center | +86-10-59691000 | wangh@cn.fujitsu.com
Xiaojing Fan | Fujitsu R&D Center | +86-10-59691000 | fanxiaojing@cn.fujitsu.com
Ryuichi Matsukura | Fujitsu/Fujitsu Laboratory | +81-44-754-2667 | r.matsukura@jp.fujitsu.com
Notice: This document does not represent the agreed view of the IEEE 802.1 OmniRAN TG. It represents only the views of the participants listed in the ‘Authors:’ field above. It is offered as a basis for discussion. It is not binding on the contributor, who reserve the right to add, amend or withdraw material contained herein. |  |  | 
Copyright policy: The contributor is familiar with the IEEE-SA Copyright Policy <http://standards.ieee.org/IPR/copyrightpolicy.html>. |  |  | 
Patent policy: The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. |  |  | 
Abstract
This presentation provides further thoughts on the 802.1CF information model structure.
Complete network model is proposed based on consensus reached in previous meetings.
Contribution is updated based on the discussions on Nov. 28th confcall.

## Slide 2: Information Model Structure
2017-12-03
Hao Wang
Fujitsu R&D Center

## Slide 3: TMN 5-Layer Management Architecture
Every layer suggests certain management functionalities
  EML provides management functions for network elements on an individual or group basis. It also supports an abstraction of the functions provided by the network element layer.
  NML offers a holistic view of the network, independent of device types and vendors. It manages a network as supported by the element management layer.
FCAPS have different tasks at each layer.
EML-NML interface is the point

## Slide 4: Network Infrastructure Model
To be modified

## Slide 5: Practice with 7.1 AN Setup
ANC
enable
(power-up)
NA
BH
NA_activated
AN operator
NMS
ANC_activated
NA_configuration
AN_configuration
AN_operation_status
enable
(power-up)
AN operator
NA_operation_status
Status, set and/or cleared by source
Procedures initiated by source and consumed by destination
(no need to specify details, maybe out of scope of 802)
…

## Slide 6: IM for 7.1 AN Setup
Network Management Service
{1} NMS-ID: Unique NMS identifier
Access Network Control
{1} ANC-ID: Unique ANC identifier
{1} Activated: boolean type on/off switch
{1} OperationStatus: enum type operation state
// for setup on authorized spectrum
{1+} SpectrumSensingPeriod: time period for sensing
{1} PreferredChannelList: preferred channels provided by spectrum database
{1+} BackupChannelList: backup channels provided by spectrum database
1
Backhaul
{1} BH-ID: Unique BH identifier
{1} Activated: boolean type on/off switch
{1} OperationStatus: enum type operation state
Node of Attachment
{1} NA-ID: Unique NA identifier
{1} Activated: boolean type on/off switch
{1} OperationStatus: enum type operation state
// for setup on authorized spectrum
{1} Geolocation: geo location
{1+} SensingCapability: capability parameters
related to sensing
1
1+
SensingStatistics
{1} NA-ID
{1} Sensing-ID: identifier for the sensing task
{1} SensingConfig: config for the sensing task
{1} SpectrumAvailability: sensing results
{1} ChannelClassification: sensing results
of channel classification
1+
* more details & comments

## Slide 7: Practice with 7.2 NDS
ANC
NA
Passive scan
TE
Status, set and/or cleared by source
Procedures initiated by source and consumed by destination
(no need to specify details, maybe out of scope of 802)
Subscription
Sup. SS
Sup. AR
Certificate
AN capability
Open questions
Should ‘AN’ changed to ‘ANC’ ?
Is a role for SS & AR ?
NA has a role but doesn’t hold any attributes?
  Scanning, a 802 procedure, is for NA discovery only. What key information should delivered?
  should have the ‘NA capability’ advertisement
AN, SS, AR detection relies on non-802 proc?
  How ANC send ‘attribute’ to TE?
  It’s necessary for TE to retrieve something directly from AR and SS? A: not SS, but ANC, e.g ‘ANQP’
Remote database
Active scan
Retrieve specific info. (ANQP)
Not specified
NA capability

## Slide 8: IM for 7.2 NDS
Network Management Service
{1} NMS-ID: Unique NMS identifier
Access Network Control
{1} ANC-ID: Unique ANC identifier
{1} SupportedSS: supported subscription service ID
{1} SupportedAR: supported access router ID
{1} SP-ID: service provider ID
Certificate
AN capabilities
1
Backhaul
{1} BH-ID: Unique BH identifier
Node of Attachment
{1} NA-ID: Unique NA identifier
{1} ANInfo: AN short information
{1} BeaconPeriod: config for beacon broadcast
1
1+
modified in order to line up with the user service model
not show the ‘AN-ID’
‘certificate’ is described in the text but not specified in the user service model
‘ANInfor’ moves from ANC to NA

## Slide 9: Practice with 7.3 Association
ANC
NA
TE
Status, set and/or cleared by source
Procedures initiated by source and consumed by destination
(no need to specify details, maybe out of scope of 802)
Decision point
Agent ctrl account.
Functions of ANC
  Asso. decision point: approve / reject
  Agent control for accounting: terminate accounting (SS) after disassociation
  Session transfer: support fast handover
Attributes of NA
  NA capability: denote the negotiable options of the association
  Preferred connection parameters
Attributes of TE
  TE capability (link, security, & QoS capabilities)
SS
Asso.
disAsso.
Not specified
Terminate accounting
capability
ReAsso.
NA capability
Session transfer
Listed Attributes (7.3.5) | Presumed Owner
Protocol configuration | ANC NA
Link capability information | TE, NA
Preferred and requested link capabilities | NA
Security and QoS capabilities | TE, NA
Support of particular services | ANC NA
Result codes | ANC NA
Pref. conn. Para.

## Slide 10: IM for 7.3 Association
Network Management Service
{1} NMS-ID: Unique NMS identifier
Access Network Control
{1} ANC-ID: Unique ANC identifier
protocolConfiguration
SpecialServicesSupport
1
Backhaul
{1} BH-ID: Unique BH identifier
Node of Attachment
{1} NA-ID: Unique NA identifier
{1} NA capability: link, security and QoS capability of NA
{1+} PreferredLinkProfile: preferred link config
{1+} PreferredSecurityProfile: preferred security config
{1+} PreferredQosProfile: preferred QoS config
{1} ProtocolConfig: 802 protocol config
{0} SpecialServicesSupport: emergency support
1
1+
AssociationStatistics
{1} Association-ID: unique association ID
{1} TE-ID: unique TE ID
{1} LinkProfile: allowed link config
{1} SecurityProfile: allowed security config
{1} QoSProfile: allowed QoS config
{1} ResultCodes: association results
0+
move attributes from ANC to NA
move association statistics from ANC to NA, showing the ‘decision point’ is on NA

## Slide 11: Practice with 7.4 Authentication
ANC
NA
TE
Status, set and/or cleared by source
Procedures initiated by source and consumed by destination
(no need to specify details, maybe out of scope of 802)
Forward point
Supp. auth method
Functions of ANC
  Forwarding point: forward subscription to SS
Attributes of ANC
  Supported authentication method
  supported encryption method
  credential
Attributes of TE
  Supported authentication method
  supported encryption method
  credential
SS
ID requst
EAP
Not specified
Access request
Access response
supp. encry
Result
Supp. encr. method
credential
supp. auth
credential
Decision point

## Slide 12: IM for 7.4 Authentication
Network Management Service
{1} NMS-ID: Unique NMS identifier
Access Network Control
{1} ANC-ID: Unique ANC identifier
{1} ANCredential: authenticator credential
{1} SupportedEncryptionModes: possible encryption modes
{1} PreferredEncryptionMode: preferred encryption mode
1
Backhaul
{1} BH-ID: Unique BH identifier
Node of Attachment
{1} NA-ID: Unique NA identifier
1
1+
AuthenticationStatistics
{1} Subscription-ID: NAI
{1} TE-ID: terminal identifier
{1} User-ID: username
{1} SessionKey: session credential
{1} EncryptionMode: encryption config
{1} ResultCodes: authentication result
0+

## Slide 13: Practice with 7.5 Datapath
ANC
NA
TE
Status, set and/or cleared by source
Procedures initiated by source and consumed by destination
(no need to specify details, maybe out of scope of 802)
NA & BH config
SS
Datapath ind.
Auth. accept w/
authorization
AR config
Open questions
‘Subscriber’ vs. ‘User’?
‘user-specific’ vs. ‘subscriber-specific’ vs. ‘session-specific’ vs. ‘service-specific’?
Datapath can be shared by terminals?
  L2236: The datapath is either pre-established during access network setup and/or dynamically configured when terminal connects to access network.
  L2185: The datapath is usually preconfigured during access network setup when being shared for multiple user sessions, and may be dynamically established just for the lifetime of a user session
Detach vs. Disassociation?
Datapath relocation vs. session relocation with fast transition?
Authorization
AR
R3 negotiation
R3 negotiation
NA config
BH
BH config
AR config
R1 negotiation
R1 negotiation

## Slide 14: IM for 7.5 Datapath
Network Management Service
{1} NMS-ID: Unique NMS identifier
Access Network Control
{1} ANC-ID: Unique ANC identifier
1
Backhaul
{1} BH-ID: Unique BH identifier
{1} R3Config: datapath config for R3
{1} R6Config: datapath config for R6
{1} BridgeConfig: config for bridges
Node of Attachment
{1} NA-ID: Unique NA identifier
{1} R1Config: datapath config for R1
{1} R6Config: datapath config for R6
{1} BridgeConfig: config for bridges
1
1+
DatapathStatistics
{1} TE-ID: terminal identifier
{1} AR-ID: access router identifier
{1} Datapath-ID: unique identifier
{1} DatapathConfig: datapath config
{1} ResultCodes: states of the datapath
0+

## Slide 15: Practice with 7.6 QoS
ANC
NA
TE
Status, set and/or cleared by source
Procedures initiated by source and consumed by destination
(no need to specify details, maybe out of scope of 802)
SF config
SS
SF add. req & res.
Authorization w/
QoS policy
QoS repository
Service flow attached to DP
Service flow negotiation happens both inside and outside AN
Either TE, AR, or SS can initialize, change and delete the SF?
  part of the cases are covered
SF (admission) control is based on QoS policy provided and changed by SS
SF has operational states: provisioned, permitted, and active
pre-prov. SF
QoS decision
DP reg. req & res
BH
Policy decision ctrl
preferred QoS
Admission ctrl
SF change. req & res.
SF delete. req & res.
Authorization change
request
SF para.
SF para.
filter
filter

## Slide 16: IM for 7.6 QoS
Network Management Service
{1} NMS-ID: Unique NMS identifier
Access Network Control
{1} ANC-ID: Unique ANC identifier
{1+} QoSPolicy: QoS policy rules for service flow
1
Backhaul
{1} BH-ID: Unique BH identifier
{0+} SFParameters: service flow config
{0+} FilterRules: for QoS enforcement
Node of Attachment
{1} NA-ID: Unique NA identifier
{0+} SFParameters: service flow config
{0+} FilterRules: for QoS enforcement
1
1+
DatapathStatistics
{1} Datapath-ID: unique identifier
0+
ServiceFlowStatistics
{1} SF-ID: unique identifier
{1} SFConfig: service flow config
{1} State: service flow operational
state
1+

## Slide 17: Practice with 7.7 Accounting
ANC
NA
TE
Status, set and/or cleared by source
Procedures initiated by source and consumed by destination
(no need to specify details, maybe out of scope of 802)
mon. ctrl pt
SS
user session
session-specific
config
session mon. config
SS provides the mon. config as
  user specific
  session specific
ANC controls mon. on sub NEs
NEs perform the mon. tasks and report the records
Mon. records are processed and forwarded to SS for accounting
collection
Monitoring req & rsp
BH
mediation
account req & rsp
mon. pt
mon. pt

## Slide 18: IM for 7.7 Accounting
Network Management Service
{1} NMS-ID: Unique NMS identifier
Access Network Control
{1} ANC-ID: Unique ANC identifier
{1} MonitorConfig: parameter set for monitoring tasks
{1} CollectionConfig: parameter set for collection procedure
{1} MediationConfig: parameter set for mediation procedure
1
Backhaul
{1} BH-ID: Unique BH identifier
Node of Attachment
{1} NA-ID: Unique NA identifier
1
1+
MonitoringStatistics
{1} Monitor-ID: unique identifier
{1} User-ID: username
{1} TE-ID: terminal identifier
{1} Session-ID: session identifier
{1} MonitorParameter: monitor config
{1} ResultCodes: operational state of the
monitoring task
{1} MonitorRecords: monitoring statistics
0+

## Slide 19: Practice with 7.8 FDM
Summary of detail procedures
ANC
NA
BH
FDM_capability_NA
NMS
FDM_capability_ANC
FDM_config
FDM_config
FDM_aggregation_statistics
Alarm
Status, set and/or cleared by source
Procedures initiated by source and consumed by destination
(no need to specify details, maybe out of scope of 802)
…
Link monitoring
Test
TE
FDM_capability_TE
FDM_config
Alarm/Event

## Slide 20: IM for 7.8 Accounting
Network Management Service
{1} NMS-ID: Unique NMS identifier
{1} FDMRules: policy rules for FDM
Access Network Control
{1} ANC-ID: Unique ANC identifier
{1} FDMCapability: FDM capability of ANC
{1} FDMAggregationConfig: config for aggregations
1
Backhaul
{1} BH-ID: Unique BH identifier
{1} FDMCapability: FDM capability for BH
{1} FDMConfig: config for FDM
Node of Attachment
{1} NA-ID: Unique NA identifier
{1} FDMCapability: FDM capability for NA
{1} FDMConfig: config for FDM
1
1+
AlarmList
{1} Alarm-ID: unique identifier
{1} AlarmParameter: alarm parameters
{1} ProbCause: probable cause of
the alarm
{1} Events: events caused the alarm
{1} State: state of the alarm
LinkMonitoringStatistics
{1} LM-ID: unique identifier
{1} Host-ID: identifier of network entity
{1} State: state of the LM task
{1} NBinfo: neighbor information
{1} EnInfo: environmental information
{1} Events: events of link monitoring
1+
1+
TestStatistics
{1} Test-ID: unique identifier
{1} TestConfig: parameter of the test
{1} Test Results: results of the test
1
SelfCheckStatistics
{1} SC-ID: unique identifier
{1} Host-ID: identifier of network entity
{1} Hwinfo: hardware information
{1} Swinfo: software information
{1} MIBinfo: local MIB information
{1} Loginfo: system log information
{1} Cominfo: Communication information
1+

## Slide 21: Network Infrastructure Model (Complete)
To be modified

## Slide 22: For reference

## Slide 23: 802.1X Model (1) – Symmetric Function
Symmetric structure & functions
  EAP higher layer
    EAP parser
  PAE logon process
    manage credential, initiate the use of supp and authen
  ‘X’ PACP
    802.1X control
  PDU tx & rx
    process EAPOL messages
‘X’ PAE can be implemented on single physical port
802.1X model describes ‘entities’ inside the dotted box
  essential attributes that need to be ‘set’ (enable) or ‘get’ (state)
  EAPOL Statistics survey the results of EAPOL request-response

## Slide 24: 802.1X Model (2) – Symmetric Function
PAE
supplicant
authenticator
LogonProcess
SessionStatistics
PAE System
…
Part of Figure 12-3 PAE management information
EAPOLStatistics

## Slide 25: 802.1X Model (3) – Asymmetric Function
An EAPOL Announcement protocol that allows a PAE to indicate the availability of network services, helping other PAEs to choose appropriate credentials and parameters for authentication and network access (Clause 10).
  Pair relationship: announcer & listener
  Associated to PAE, but roles are bounded to Authenticator and Supplicant separately
  Implementation flexibility
PAE
supplicant
authenticator
Announce
Announcement*
PAE System
Part of Figure 12-3 PAE management information
Announcer
Listener
*Announcement statistics

## Slide 26: Two Options for Creating Network Operation Model
AN only focus on the core of the NRM
The whole NRM make use of the symmetric structure
Core of the NRM
Service
Control
Interface
NMS
ANC
1
CIS
SS
TE
AR
NA
BH
Interface

## Slide 27: Consensus have been Reached
It was agreed to keep the attributes as generic as possible, examples are shown in the following contribution,
  https://mentor.ieee.org/omniran/dcn/17/omniran-17-0081-01-CF00-user-service-information-model.pptx
It was agreed not to integrate the FDM functionalities at this moment, but to create a separate FDM model when the main model got shaped.
Some of the attributes related with FDM functionalities may appear in the main model.
Since there are two separate models under discussion, same attributes may appear in both the user service model and network operation model, but consisted by different classes.

## Slide 28: Reference: 802.1X model

## Slide 29: Questions, Comments Thank YOU!