## Slide 1
Proposal to Amend the Configuration and Maintenance Model |  |  | 
Date: [2018-03-05] |  |  | 
Authors: |  |  | 
Name | Affiliation | Phone | Email
Hao Wang | Fujitsu R&D Center | +86-10-59691000 | wangh@cn.fujitsu.com
Notice: This document does not represent the agreed view of the IEEE 802.1 OmniRAN TG. It represents only the views of the participants listed in the ‘Authors:’ field above. It is offered as a basis for discussion. It is not binding on the contributor, who reserve the right to add, amend or withdraw material contained herein. |  |  | 
Copyright policy: The contributor is familiar with the IEEE-SA Copyright Policy <http://standards.ieee.org/IPR/copyrightpolicy.html>. |  |  | 
Patent policy: The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. |  |  | 
Abstract
This presentation grouped the comments from the initial WG ballot related to the attributes and information model in D1.0, and proposed a rough resolution to initiate discussions in the TG.

## Slide 2: Proposal to Amend the Configuration and Maintenance Model
2018-03-05
Hao Wang
Fujitsu R&D Center

## Slide 3: Comments Collected on the Subject
101 | Technical | 109 | 7.7.5 | 3049 | The accounting and monitoring-specific attributes only list usage related attributes, but only few performance related attributes as detailed in section 7.7.8 | Enhance chapter 7.7.5 with performance related attributes as shown for the various technologies in section 7.7.8 | Yes | Max R. | for further discussion, depends on the conclusion on section 8.1.2 | Open
103 | Technical | 123 | 7.8.5 | 3364 | FDM-specific attributes only roughly specified without taking attributes into account listed in 7.8.8, and without proper notation of number of occurency. | Extend list of FDM-specific attributes to reflect attributes shown in section 7.8.8 with proper denotation of number of occurences. | Yes | Max R. | Dublicate of #36 | Open
36 | Technical | 123 | 7.8.5 | 3364 | Descriptions on 7.8.5 are inconsistent with the information model on 8.1.2.9. | Change the texts of 7.8.5 accordingly. Will be provided in a separate contribution. | No | Hao W. | Agreed in principle, but requires more input | Open
104 | Technical | 134 | 8.1 | 3625 | Information model is devided between service model and configuration and maintenance model. Combination of configuration and maintenance model creates overly complex structure and leads to less useful results. | Access network information model should be structured into operation, administration, and maintenance parts. The operational part is already roughly covered by the service information model, but the infrastructure configuration and maintenance model should be separated into an infrastructure configuration model (administration) and a fault diagnostic (maintenance) model. | Yes | Max R. | Agreed in principle, but requires more input | Open
37 | Technical | 146 | 8.1.2.8 | 3731 | Information described in Figure 92 is not consistent with 7.7.5 accounting attributes. | Change Figure 85, 92, 94, accordingly. Will be provided in a separate contribution. | No | Hao W. | further input needed | Open
Summary of the comments
  Reconsider the structure of the information model of infrastructure configuration and maintenance on clause 8.1.2
    Eliminate the duplication, keep both models informational
  Line up the attributes in clause 7 to the information model
https://mentor.ieee.org/omniran/dcn/18/omniran-18-0006-04-CF00-d1-0-collected-comments.xls

## Slide 4: Definitions (Wikipedia) https://en.wikipedia.org/wiki/Operations,_administration_and_management
Operations
  Basically, these are the procedures you use during normal network operations.
  They are day to day organizational procedures: handover, escalation, major issue management, call out, support procedures, regular updates including emails and meetings. In this section group you will find things like: Daily Checklists, On-call and Shift rotas, Call response and ticket opening procedures, Manufacturer documentation like technical specifications and operator handbooks, OOB Procedures
Administration
  These are support procedures that are necessary for day-to-day operations - things like common passwords, equipment and tools access, organizational forms and timesheets, meetings minutes and agendas, and customer Service Reports.
  This is not necessarily 'network admin', but also 'network operations admin'.
Maintenance
  Tasks that if not done will affect service or system operation, but are not necessarily as a result of a failure. Configuration and hardware changes that are a response of system deterioration. These involve scheduling provider maintenance, standard network equipment configuration changes as a result of policy or design, routine equipment checks, hardware changes and software/firmware upgrades. Maintenance tasks can also involve the removal of administrative privileges as a security policy.
Provisioning
  Introducing a new service, creating new circuits and setting up new equipment, installing new hardware. Provisioning processes will normally include 'how to' guides and checklists that need to be strictly adhered to and signed off. They can also involve integration and commissioning process which will involve sign-off to other parts of the business life cycle.
Troubleshooting
  Troubleshooting is carried out as a result of a fault or failure, may result in maintenance procedures, or emergency workarounds until such time as a maintenance procedure can be carried out. Troubleshooting procedures will involve knowledge databases, guides and process to cover the role of network operations engineers from initial diagnostics to advanced troubleshooting. This stage often involves problem simulation, and is the traditional interface to design.
Copy from omniran-17-0080-00-CF00-information-modeling-for-network-operation

## Slide 5: Mapping of 802.1CF to OAMPT
Operations
    Procedures used to control normal network operation
  Sections 7.2 – 7.7 of Functional decomposition and design
Administration
    Support procedures accompanying normal network operation
  Section 6.6 Operational roles, and Section 7.1 Access network setup
Maintenance
    Re-adjustments of system operation due to failures and regular needs
  Section 6.3 – 6.5 NRM, Section 7.1 Access network setup, and Section 7.8 Fault diagnostics and maintenance
Provisioning
    Installation and activation of new network resources.
  Section 6.8 Network virtualization, and Section 8.2 Virtualized network instantiation (maybe 7.2 NDS can be part of it?)
Troubleshooting
    Procedures due to fault or failure to compensate the misbehavior
  Section 7.8 Fault diagnostics and maintenance
Copy from omniran-17-0080-00-CF00-information-modeling-for-network-operation

## Slide 6: Practice of a Network OAM Model
Merge model in clauses 8.1.2.3 – 8.1.2.8 into the corresponding model of the user session (8.1.1.2 – 8.1.1.7), result in an update of the user session model.
Exploring a new network OAM model in replace of current infrastructure configuration and maintenance model in clause 8.1.2.
Network OAM
NMS
{1} NMS-ID
{1} FDMRules
ANC
{1} ANC-ID
{1} FDMCapability
{1} FDMAggregationConfig
User Session
{1} Session-ID
ANInitialization
{1} ANConfig
FaultManagement
{1+} Alarms-ID
LinkMonitoring
…
Test
…
Selfcheck
…
Refer to 8.1.1 for complete information, represents ‘O’
Inclusion of 8.1.2.2, represent ‘A’
In combination of ‘M’ and ‘T’
Orchestrator

## Slide 7: Questions, Comments Thank YOU!