## Slide 1: MAC Address Acquisition Protocol
Antonio de la Oliva (UC3M)

## Slide 2: MAAP
Defined in IEEE 1722: IEEE Standard for a Transport Protocol for Time-Sensitive Applications in Bridged Local Area Networks
It is defined to self-claim multicast addresses
Protocol based on claiming, probe and defend messages
Acquisition of addresses:
  Select an address range from the MAAP dynamic allocation pool.
  Send a series of MAAP_PROBE protocol data units (PDUs) to determine whether the address range is already in use.
  Listen for MAAP_DEFEND PDUs indicating the address range is in use.
  Repeat the above steps until an unused address range has been found.

## Slide 3: MAAP
Defending addresses:
  Send MAAP_ANNOUNCE PDUs periodically to inform the network of address ranges that are currently in use. This allows networks that are joined after the MAAP has been run to identify conflicts.
  Listen for MAAP_PROBE PDUs and send MAAP_DEFEND PDUs in response to any address ranges that conflict with previously acquired address range(s).
  Listen for MAAP_ANNOUNCE PDUs that conflict with previously acquired address range(s).
  If a conflicting MAAP_ANNOUNCE PDU is received, then MAAP discontinues use of the conflicting address range(s) and acquires new address range(s).

## Slide 4: MAAP message format

## Slide 5: MAC addresses used by MAAP
Similar to IEEE 802.1CQ mandate, but for multicast only:
  A block of multicast MAC addresses has been reserved for the use of AVTP.
  The MAAP specifies a mechanism to allocate multicast MAC addresses dynamically in a specified address range.
  Any application that uses addresses from the MAAP dynamic allocation pool shall implement the MAAP and MAAP shall be used to allocate these addresses.
In MAAP messages:
  All MAAP_PROBE and MAAP_ANNOUNCE frames are sent with a multicast destination MAC address set to the reserved MAAP multicast address defined in the specification (Table B.10 of IEEE 1722).
  All MAAP_DEFEND frames are sent with a destination MAC address set to the source MAC address received in the MAAP_PROBE frame that caused the sending of the MAAP_DEFEND frame.
  The source MAC address shall be set to the MAC address of the sender.

## Slide 6: MAAP message format
To be considered when extending this protocol:
  MAAP AVTPDUs that carry a protocol version higher than the protocol version implemented by the receiver shall be interpreted according to the protocol definition of the receiver’s implemented version.
  All MAAP AVTPDUs received that contain a higher version number and a message type that is defined in the implemented version of MAAP shall be interpreted using the implemented version of MAAP, ignoring all unknown fields. This requires that future versions of MAAP maintain compatibility with the message types implemented in all previous versions of MAAP.

## Slide 7: MAAP State Machine

## Slide 8: Reuse of MAAP for unicast addresses
Common Encapsulation for LAAP server and MAAP:
  Need to define a new Ethertype (probably using 802.2 LLC and SNAP)
  Following same idea as MAAP uses for its encapsulation: use of common header with subtypes to also cover the LAAP server communication
    One common generic header for both self assignment and LAAP communication
    Use of subtypes of header to differentiate
  Removal of Stream ID
    Replacement by optional LAAP ID?
Other considerations
  MAAP assumes assignment of addresses is done in contiguous blocks

## Slide 9: Addressing of messages
MAAP uses the following addresses:
  All MAAP_PROBE and MAAP_ANNOUNCE frames are sent with a multicast destination MAC address set to the reserved MAAP multicast address defined in the specification (Table B.10 of IEEE 1722).
  All MAAP_DEFEND frames are sent with a destination MAC address set to the source MAC address received in the MAAP_PROBE frame that caused the sending of the MAAP_DEFEND frame.
  The source MAC address shall be set to the MAC address of the sender.
Problems with this addressing:
  Do we want to have all stations listening to a multicast address?
    Would not be better to have a solution similar to the solicited multicast address used by IPv6 neighbor Discovery?
      Bad thing of this approach will be that Proxy is not able to listen to all
  What unicast address do we use for sending the DEFEND and PROBE?, we do not have a MAC address at this point.

## Slide 10: Conclusions
Can MAAP be taken as basis for the self-assignment protocol?
How can we extend it to cover unicast MAC addresses?