## Slide 1
Bluetooth LE/Smart/v4 Privacy |  |  | 
Date: [2014-09-03] |  |  | 
Authors: |  |  | 
Name | Affiliation | Phone | Email
Piers O’Hanlon | Oxford Internet Institute |  | piers.ohanlon@oii.ox.ac.uk
Notice: This document does not represent the agreed view of the IEEE 802 EC Privacy Recommendation SG. It represents only the views of the participants listed in the ‘Authors:’ field above. It is offered as a basis for discussion. It is not binding on the contributor, who reserve the right to add, amend or withdraw material contained herein. |  |  | 
Copyright policy: The contributor is familiar with the IEEE-SA Copyright Policy <http://standards.ieee.org/IPR/copyrightpolicy.html>. |  |  | 
Patent policy: The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. |  |  | 
Abstract
[place document abstract text here]

## Slide 2: Bluetooth LE/Smart/v4 Privacy
Piers O’Hanlon
Oxford Internet Institute University of Oxford

## Slide 3: Bluetooth Origins
Invented by Ericsson
Standardized by Bluetooth Special Interest Group (SIG)
  Earlier version by IEEE (no longer maintained)
Bluetooth Smart/LE came from Nokia
  Originally known as WiBree (2006)
Named after King Harald Bluetooth
  King of Denmark and Norway in AD 935

## Slide 4: Bluetooth LE/Smart
Bluetooth V4.0 Core Specification (2010)
  Comprises 6 Volumes over 2,300 pages
Fundamentally different from BT v1-3
Provides for much Lower Energy operation
  Device can operate for 3 yrs on a button cell
Data services oriented approach
  No audio/media transport facilities
Spread Spectrum design:40x2MHz channels

## Slide 5: Architecture
Applications [Central, Peripheral]
Host [L2CAP, AP, SM]
Controller

## Slide 6: ‘Privacy Feature’ (Vol 3, Section 10.7)
Random Device Addresses
  Static random addresses
    Initialised at power on
  Private random addresses
    Non-Resolvable
    Resolvable using a shared secret key
Their use can impact power utilisation
Use configurable per entity
  In both Central and Peripheral devices

## Slide 7: Random Addressing: Static
Static Random Addresses
  A new random address may be set on each power cycle
  No change permitted at any other time
LSB | MSB | 
Random part of static address | 1 | 1
 48-Bit Address  |  | 

## Slide 8: Random Addressing: Non-Resolvable
Non-resolvable Private Addresses
  May be changed at any time for anonymity
  Can be used for temporary purposes
    e.g When scanning for devices
LSB | MSB | 
Random part of non-resolvable address | 0 | 0
 48-Bit Address  |  | 

## Slide 9: Random Addressing: Resolvable
Resolvable Private Address
  May be changed at any time
  Can be resolved by use of a shared key
    The Identity Resolving Key (IRK)
  Generated: hash = F(IRK, prand)
    Where F() is the ‘Random Address Function’
LSB |  | MSB | 
Hash | Random part of prand | 1 | 0
 24-Bits  |  24-Bits  |  | 

## Slide 10: Other privacy aspects
Use of random ‘Access Address’ in Link Layer data packets
  Makes it harder to guess which devices are talking to one another