## Slide 1
Overview of Privacy in 802.16 |  |  | 
Date: 2014-10-08 |  |  | 
Authors: |  |  | 
Name | Affiliation | Phone | Email
Phillip Barber | Broadband Mobile Tech |  | pbarber@broadbandmobiletech.com
Notice: This document does not represent the agreed view of the IEEE 802 EC Privacy Recommendation SG. It represents only the views of the participants listed in the ‘Authors:’ field above. It is offered as a basis for discussion. It is not binding on the contributor, who reserve the right to add, amend or withdraw material contained herein. |  |  | 
Copyright policy: The contributor is familiar with the IEEE-SA Copyright Policy <http://standards.ieee.org/IPR/copyrightpolicy.html>. |  |  | 
Patent policy: The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. |  |  | 
Abstract
This document provides an overview of Privacy methods in 802.16 standards.

## Slide 2: History of Privacy in 802.16
Privacy features introduced as part of IEEE 802.16m-2011 amendment
Later re-published as the standalone standard IEEE 802.16.1-2012, the ‘WirelessMAN-Advanced Air Interface’ [1].
The Privacy features applied only to Advanced Mobile Stations and Advanced Base Stations; were not backwards compatible.

## Slide 3: Basics of 802.16.1 Privacy
Privacy achieved through near total replacement of the use of MAC Address (MAC-48/EUI-48) as the AMS identifier in AMS-ABS communications
  in both data plane and management/control plane.
Replaced with a transitory, 12-bit Station Identifier (STID) on AMS
  STID assigned from a managed number pool by the ABS.
Replaced with ABSID (24-bit 802.16 Operator ID + 24-bit operator programmable number) on ABS
  802.16 Operator ID a managed number space administered by the IEEE RAC.

## Slide 4: STID in 802.16.1
For both data plane and management/control plane, STID to uniquely identify the AMS in AMS-ABS communications
  Identifier has relevance only within the 802.16.1 communications link AMS-ABS.

## Slide 5: 802.16.1 Privacy Process
MAC-48/EUI-48 still present in two messages in initial network entry process
  Provides MAC-48/EUI-48 to network during INE for various purposes
  For increased privacy MAC Address may be ciphered in first message
  Second message is encrypted so MAC Address instance is obfuscated
STID installed during INE
  Messages that install STID and index/relate STID to MAC Address are encrypted

## Slide 6: 802.16.1 Privacy Process (continued)
On data plane MAC Address, IP Address or other identifiers may appear in the higher layer SDU
802.16.1 addresses this by
  Supporting encryption of MAC data SDUs;
  Supporting Payload Header Suppression (PHS) and Robust Header Compression (RoHC)

## Slide 7: Conclusions
Overall it is the combination of management/control plane and data plane techniques that provide the method of 802.16.1 privacy protection.
The use of transitory, randomly assigned temporary addresses, the suppression of identifiers embedded in the data stream, and ciphering and integrity protection provide a combination of methods to improve privacy protection in 802.16.1 systems.

## Slide 8: References
[1] IEEE 802.16.1TM-2012, IEEE Standard for WirelessMAN-Advanced Air Interface for Broadband Wireless Access Systems, September 2012