## Slide 1
WiFi Privacy network experiment at IETF91 |  |  | 
Date: [2014-12-10] |  |  | 
Authors: |  |  | 
Name | Affiliation | Phone | Email
Carlos Jesús Bernardos | UC3M |  | cjbc@it.uc3m.es
Fabio Giust | UC3M |  | fgiust@it.uc3m.es
Antonio de la Oliva | UC3M |  | aoliva@it.uc3m.es
Juan Carlos Zúñiga | InterDigital |  | JuanCarlos.Zuniga@InterDigital.com
Notice: This document does not represent the agreed view of the IEEE 802 EC Privacy Recommendation SG. It represents only the views of the participants listed in the ‘Authors:’ field above. It is offered as a basis for discussion. It is not binding on the contributor, who reserve the right to add, amend or withdraw material contained herein. |  |  | 
Copyright policy: The contributor is familiar with the IEEE-SA Copyright Policy <http://standards.ieee.org/IPR/copyrightpolicy.html>. |  |  | 
Patent policy: The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. |  |  | 
Abstract
The present reports on the trial performed at IETF91 and presents some preliminary results

## Slide 2: Experiment goals
Carry out a Wi-Fi MAC randomization trial/experiment at IETF91
  Evaluating support of different OSes (Windows, Mac OS X and Linux)
  Analyzing the impact of L2 address randomization on the user experience and the network infrastructure
    Specially in case of L2 address collision
  Learn from this initial experience so we can gather further information in subsequent trials

## Slide 3: Network setup
A specific SSID (ietf-PrivRandMAC) was deployed on the wireless IETF Internet infrastructure
  Deployed on all IETF physical APs, as an additional virtual AP
  WPA PSK security, to avoid non participants to accidentally connect to our trial WLAN
  Connected via a different VLAN to the DHCP server and Internet gateway
    Provides certain isolation to the rest of the infrastructure
    Isolated pool of IPv4 addresses

## Slide 4: Trial setup
Participants were asked to notify their participation to a mailing list (ietf91-mac-privacy@ietf.org)
WLAN address randomization scripts developed and provided for 3 different OSes:
  Microsoft Windows (tested on Windows 7)
  Apple Mac OS X (tested on Version 10.10, alias Yosemite)
  GNU Linux (tested on Debian testing/unstable, Ubuntu 13.10, and Fedora 20)
Use of DHCP client identifier for debugging
https://www.ietf.org/registration/MeetingWiki/wiki/91privacy

## Slide 5: OS participants distribution
Chart: 
| Windows | Mac OS X | Linux
 | 0.066667 | 0.53333 | 0.4

## Slide 6: Preliminary results
Around 50 participants
  Not all of them informed about their participation
Number of “seen” L2 addresses roughly 60% higher than with no address randomization
  From logged results, local addresses were used between 1 and 2 hours on average
Collisions were forced in a controlled environment
  Results depends of the scenario, but apparently affected user is not always only the device colliding

## Slide 7: Next steps
Additional logs being prepared
  Process information from new set of logs
  Current logs do not capture all the participants, nor provide all the information
Prepare a “wish list” for network administrators of future trial experiments
  Logged information
  Access setup
  Increased sampling rate
Prepare address randomization tools for more platforms/OSes, including mobile ones (e.g. Android)
Make a more detailed study of collision effects under different scenarios