## Slide 1
WiFi Privacy network experiment at IEEE 802 Berlin Plenary and IETF92 |  |  | 
Date: [2015-07-15] |  |  | 
Authors: |  |  | 
Name | Affiliation | Phone | Email
Carlos Jesús Bernardos | UC3M |  | cjbc@it.uc3m.es
Antonio de la Oliva | UC3M |  | aoliva@it.uc3m.es
Juan Carlos Zúñiga | InterDigital |  | JuanCarlos.Zuniga@InterDigital.com
Notice: This document does not represent the agreed view of the IEEE 802 EC Privacy Recommendation SG. It represents only the views of the participants listed in the ‘Authors:’ field above. It is offered as a basis for discussion. It is not binding on the contributor, who reserve the right to add, amend or withdraw material contained herein. |  |  | 
Copyright policy: The contributor is familiar with the IEEE-SA Copyright Policy <http://standards.ieee.org/IPR/copyrightpolicy.html>. |  |  | 
Patent policy: The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. |  |  | 
Abstract
The present document reports on the trials performed at IEEE 802 plenary in Berlin and IETF92.

## Slide 2: Experiment Goals
Continue with the Wi-Fi MAC randomization trial at IEEE 802 March 2015 Plenary and IETF92 meetings
  First trial at IETF91, on an experimental network
    Now running on all the regular attendees’ networks
  Evaluating support of different OSes
    Windows, OS X and Linux already supported in IETF91
    Android support added for IETF92
  Analyzing the impact of L2 address randomization on the user experience and the network infrastructure
    Specially in case of L2 address collision
  Keep on learning from this experience

## Slide 3: Network Setup
Running on all wireless Internet infrastructure
  No isolated SSID (ietf-PrivRandMAC) deployed on the IETF network.
  Deployed on all physical Access Points
  Minor change for the second and third trial:
    Shorter DHCP lease (one hour) for those IP addresses assigned to a local MAC

## Slide 4: Trial Setup
WLAN address randomization scripts developed and provided for 4 different OSes:
  Microsoft Windows (tested on Windows 7)
  Apple Mac OS X (tested on Version 10.9.5 and 10.10)
  GNU Linux (tested on Debian testing/unstable, Ubuntu 13.10, and Fedora 20)
  Android (rooted devices, working on Nexus 4 & 5)
    Impact of Android version + HW
Use of DHCP client identifier for debugging
https://oruga.it.uc3m.es/802-privacy/index.php/MAC_address_change_tutorial

## Slide 5: Participants’ Statistics
OS distribution
Chart: 
| Windows | OS X | Linux | Android
 | 0.143 | 0.5 | 0.286 | 0.071

## Slide 6: DHCP Logs
144 local MACs seen during the week (IETF92)
97 IP addresses were assigned to local MAC addresses. Out of them:
  76 IP addresses were assigned to one local MAC address, e.g., because no DHCP client identifier was used by the client
  21 IP addresses were assigned to multiple local MAC address
Chart: 
| 31.133.140.197 | 31.133.143.128 | 31.133.143.131 | 31.133.143.140 | 31.133.143.149 | 31.133.160.163 | 31.133.167.134 | 31.133.168.103 | 31.133.175.127 | 31.133.180.232 | 31.133.183.132 | 31.133.167.16 | 31.133.167.19 | 31.133.167.5 | 31.133.175.1 | 31.133.177.55 | 31.133.178.27 | 31.133.178.76 | 31.133.183.17 | 31.133.183.2 | 31.133.183.3
 | 2 | 3 | 2 | 6 | 5 | 3 | 9 | 2 | 3 | 4 | 3 | 2 | 2 | 2 | 2 | 3 | 3 | 5 | 2 | 3 | 2
# MAC addresses for IP address

## Slide 7: Impact on Network Infrastructure
Users were asked to use a specific dhcp-client-identifier
  Issue: Server delegates the same IP address to a client even if it changes its L2 address
Observed behavior on DHCP server
  If DHCP server receives a request for which it finds a matching DHCP lease (i.e., existing client-id) within the 25% of the DHCP lease time, the server does not reply
  This limits the speed a client can change its L2 address, which besides depends on a configuration parameter on the network side (the DHCP lease time)
  The implications of this issue requires further analysis

## Slide 8: Next Steps
Planning to leave the network setup permanently at IETF and IEEE 802 meetings
Continue analyzing the impact of MAC address collision under different scenarios and with different network equipment vendors
Some conference/technical papers under submission/preparation